PROPOSAL FOR A NEW DRAFT REGULATION

UNIFORM PROVISIONS CONCERNING THE APPROVAL OF:

1.	SPECIFIC COMPONENTS OF MOTOR VEHICLES USING COMPRESSED GASEOUS HYDROGEN;

2.	VEHICLES WITH REGARD TO THE INSTALLATION OF SPECIFIC COMPONENTS FOR THE USE OF COMPRESSED GASEOUS HYDROGEN;

Prepared by the Partners of the European Integrated Hydrogen Project (EIHP)

Note:	Green highlighting identifies reference to standards etc.

Yellow highlighting identifies references to other parts of this document.

CONTENTS

REGULATION

Page No.

|  | 1 | Scope |  |
| --- | --- | --- | --- |
|  | 2 | Definitions, container types and pressure classifications |  |
| Part I |  | SPECIFIC COMPONENTS OF MOTOR VEHICLES USING COMPRESSED GASEOUS HYDROGEN |  |
|  | 3 | Application for approval |  |
|  | 4 | Markings |  |
|  | 5 | Approval |  |
|  | 6 | Specifications for hydrogen components |  |
|  | 7 | Modification of a type of a specific component and extension of approval |  |
|  | 8 | Conformity of production |  |
|  | 9 | Penalties for non-conformity of production |  |
|  | 10 | Production definitely discontinued |  |
|  | 11 | Names and addresses of Technical Services conducting approval tests and of Administrative Departments |  |
| Part II |  | VEHICLES WITH REGARD TO THE INSTALLATION OF SPECIFIC COMPONENTS FOR THE USE OF COMPRESSED GASEOUS HYDROGEN |  |
|  | 12 | Application for approval |  |
|  | 13 | Approval |  |
|  | 14 | Requirements for the installation of specific components for the use of compressed gaseous hydrogen within motor vehicles |  |
|  | 15 | Modification of a vehicle type or hydrogen system and extension of approval |  |
|  | 16 | Conformity of production |  |
|  | 17 | Penalties for non-conformity of production |  |
|  | 18 | Production definitely discontinued |  |
|  | 19 | Names and addresses of Technical Services conducting approval tests and of Administrative Departments |  |

ANNEXES

| 1 | Essential characteristics of specific components |
| --- | --- |
| 2 | Essential characteristics of the vehicle, propulsion system and hydrogen related systems |
| 3 | Arrangement of the specific component approval marks |
| 4 | Communication concerning the approval, or refusal, or extension, or withdrawal, or production definitely discontinued of a specific component pursuant to Regulation No. Xx |
| 5 | Arrangements of approval marks for a vehicle type with regard to the installation of a hydrogen system |
| 6 | Communication concerning the approval, or refusal, or extension, or withdrawal, or production definitely discontinued of a vehicle type with regard to the installation of a Hydrogen System pursuant to Regulation No. Xx |
| 7 | Requirements and approval test procedures for containers |
| *8 | Requirements for specific components excluding hydrogen containers |
| 8A | Provisions regarding the approval of pressure relief devices |
| 8B | Provisions regarding the approval of hydrogen valves |
| 8C | Provisions regarding the approval of heat exchangers |
| 8D | Provisions regarding the approval of refuelling connections or receptacles |
| 8E | Provisions regarding the approval of pressure regulators |
| 8F | Provisions regarding the approval of sensors for hydrogen systems |
| 8G | Provisions regarding the approval of flexible fuel lines |
| 8H | Provisions regarding the approval of fittings or screwed connection systems |
| 8I | Provisions regarding the approval of excess flow systems |
| 8J | Provisions regarding the approval of hydrogen filters |
| *8x | Provision for additional sub-annexes |
| 9 | Approval test procedures for specific components excluding hydrogen containers |
| 10 | Special requirements to be applied to the safety aspects of complex electronic vehicle control systems |

* If Type Approval is required for components other than those listed above, a new sub-annex shall be created.

1	SCOPE

This regulation applies to:

1.1	Compressed gaseous hydrogen systems for motor vehicles in which the hydrogen is stored in its gaseous phase under pressure and essentially at ambient temperatures.

1.2	Specific Components of motor vehicles using compressed gaseous hydrogen (Part 1 of this Regulation).

1.3	Vehicles with regard to the installation of Specific Components for the use of compressed gaseous hydrogen (Part 2 of this Regulation).

2	DEFINITIONS, CONTAINER TYPES, PRESSURE CLASSIFICATIONS AND STANDARD SERVICE CONDITIONS

2.1	DEFINITIONS

For the purpose of this Regulation and accompanying Annexes the following definitions shall apply:

2.1.1	"Approval of a Vehicle" The approval of a vehicle type of categories M and N with regard to its Hydrogen System installed as original equipment.

2.1.2	"Automatic Valve" A valve which is not operated manually, excluding Non-return Valves.

2.1.3	“Auto-frettage”: A pressure application procedure used in manufacturing Composite Containers with metal liners, which strains the liner past its yield point sufficiently to cause permanent plastic deformation, which results in the liner having compressive stresses and the fibres having tensile stresses at zero internal pressure.

2.1.4	“Auto-frettage Pressure”: The pressure within the over-wrapped Container at which the required distribution of stresses between the liner and the over-wrap is established.

2.1.5	“Batch - Composite Containers”: A “batch“ shall be a group of Containers successively produced from Liners having the same size, design, specified materials of construction and process of manufacture.

2.1.6	“Batch - Metal Containers and Liners”: A “batch“ shall be a group of metal Containers or Liners successively produced having the same nominal diameter, wall thickness, design, specified material of construction, process of manufacture, equipment for manufacture and heat treatment, and conditions of time, temperature and atmosphere during heat treatment.

2.1.7	“Batch - Non-metallic Liners”: A “batch“ shall be a group of non-metallic Liners successively produced having the same nominal diameter, wall thickness, design, specified material of construction and process of manufacture.

2.1.8	"Boundary of Functional Operation" Defines the boundaries of the external physical limits within which a system is able to maintain control.

2.1.9	“Burst Pressure”: The pressure at which the Container ruptures.

2.1.10	"Check Valve or Non-return Valve" A valve which allows Hydrogen to flow in only one direction.

2.1.11	"Complex Electronic Vehicle Control Systems" Those Electronic Control Systems which are subject to a hierarchy of control in which one electronically controlled function may be over-ridden by a higher level Electronic Control System/function. In this case, the function which is over-ridden becomes part of the complex system.

2.1.12	“Composite Container”: A Container made of resin impregnated continuous filament wound over a metallic or non-metallic Liner. Composite Containers using non-metallic Liners are referred to as All-composite Containers.

2.1.13	"CGH2" Compressed gaseous hydrogen.

2.1.14	"Container" Any system used for the storage of compressed gaseous hydrogen at ambient temperature, excluding any other Hydrogen Components which may be attached to or fitted inside the Container.

2.1.15	“Controlled Tension Winding”: A process used in manufacturing hoop wrapped composite Containers with metal Liners by which compressive stresses in the Liner and tensile stresses in the Over-wrap at zero internal pressure are obtained by winding the reinforcing filaments under significant high tension.

2.1.16	“Design Pressure”: The Settled Pressure at a uniform temperature of 65°C that a component is subjected to. The Design Pressure is equal to the Working Pressure multiplied by 1.175.

2.1.17	“Electronic Control System” A combination of Units, designed to co-operate in the production of the stated vehicle control function by electronic data processing. Such systems, often controlled by software, are built from discrete functional components such as sensors, electronic control units and actuators and connected by Transmission Links. They may include mechanical, electro-pneumatic or electro-hydraulic elements.

2.1.18	"Equipment Of The Container" All devices which are fixed directly to the Container.

2.1.19	"Excess Flow System" A system or single valve that shuts off the flow without manual intervention, or limits the gas flow when the flow exceeds a specified value.

2.1.20	“Finished Container”: Completed Container that is typical of normal production, complete with identification marks and external coating including integral insulation specified by the Manufacturer, but free from non-integral insulation or protection.

2.1.21	"Fitting Or Screwed Connection System" A connector used in a piping, tubing or hose system.

2.1.22	"Flexible Fuel Line" A flexible tubing or hose through which hydrogen flows.

2.1.23	"Fuel Supply Line" The line which supplies the Hydrogen Conversion System with hydrogen.

2.1.24	“Fully Wrapped”: An Over-wrap having a filament wound reinforcement both in the circumferential and axial direction of the Container.

2.1.25	“Gas Temperature”: The temperature of gas in a Container.

2.1.26	“Gas Tight”: A Hydrogen Component or System shall not leak when pressurised with hydrogen, helium or a gas mixture containing at least 10% helium, i.e. stay bubble free if using leak detection spray.

2.1.27	"Ground Clearance Of The Vehicle" The shortest distance between the ground plane and the lowest fixed point of the vehicle.

2.1.28	"H2" Hydrogen.

2.1.29	“Hoop Wrapped”: An Over-wrap having a filament wound reinforcement in a substantially circumferential pattern over the cylindrical portion of the Liner so that the filament does not carry any significant load in a direction parallel to the Container longitudinal axis.

2.1.30	"Hydrogen Component" A component that is in direct contact with hydrogen or which forms part of a system installed because of the use of hydrogen.

2.1.31	"Hydrogen Conversion System" Any system designed for the consumption of hydrogen.

2.1.32	“Hydrogen Filter” A filter used to separate oil, water and dirt from hydrogen.

2.1.33	“Hydrogen Sensor” A sensor used to detect hydrogen in air.

2.1.34	"Hydrogen System" An assembly of Hydrogen Components and connecting parts fitted on motor vehicles using hydrogen, excluding the Propulsion System(s) or auxiliary power unit(s).

2.1.35	“Liner”: A Container that is used as a Gas Tight, inner shell, on which reinforcing fibres are filament wound to reach the necessary strength. Liners may be designed to share the load with the reinforcement, or not to carry any part of the load.

2.1.36	"Manual valve" A manually operated valve.

2.1.37	“Manufacturer”: The person or organisation responsible for the design, fabrication and testing of the Hydrogen Components.

2.1.38	“Maximum Service Temperature”: The maximum temperature which a component is subjected to and for which the component is designed.

2.1.39	“Over-wrap”: The reinforcement system of filament and resin applied over the Liner.

2.1.40	"Pressure" Gauge pressure measured in MPa against atmospheric pressure, unless otherwise stated.

2.1.41	"Pressure Regulator" A device used to control the delivery pressure of gaseous fuel to the Hydrogen Conversion System.

2.1.42	"Pressure Relief Device" A device that prevents a pre-determined upstream pressure from being exceeded.

2.1.43	“Prestressing”: The process of applying Auto-frettage or Controlled Tension Winding.

2.1.44	"Propulsion System" The internal combustion engine or fuel cells of the vehicle.

2.1.45	"Range of Control" Refers to an output variable and defines the range over which the system is likely to exercise control.

2.1.46	"Refuelling Connection or Receptacle" A device fitted in the vehicle used to fill the Container at the filling station.

2.1.47	"Rigid Fuel Line" Tubing which has not been designed to flex in normal operation and through which hydrogen flows.

2.1.48	”Safety Concept" Measures designed into the system to ensure safe operation even in the event of a failure.

2.1.49	"Safety Device" A device intended to ensure safe operation.

2.1.50	"Safety Instrumented Systems" Process control systems that prevent an impermissible fault range from being reached by an automatic intervention in the process.

2.1.51	“Service Life”: The life in years during which the Containers may safely be used in accordance with the standard service conditions.

2.1.52	“Settled Pressure”: The maximum gas pressure when a given Settled Temperature is reached.

2.1.53	“Settled Temperature”: The uniform Gas Temperature after any change in temperature caused by filling has dissipated.

2.1.54	"Specific Component" A Hydrogen Component that is subjected to type approval in accordance with this Regulation. Specific Components are, where used in the Hydrogen System:

Automatic valve,

Check valve or non-return valve,

Container,

Excess flow system,

Fitting or screwed connection system,

Flexible fuel line,

Heat exchanger,

Hydrogen filter,

Manual valve,

Sensors (pressure or temperature or hydrogen or flow sensors) if used as a Safety Device,

Pressure regulator,

Pressure relief device,

Refuelling connection or receptacle.

The functions of the Specific Components listed above may be combined or fitted together with other Specific Components or Hydrogen Components as a "Multifunctional Component", but for the purposes of this Regulation will still be referred as a Specific Component.

2.1.55	“Test Pressure”: The maximum pressure to which a Hydrogen Component is subjected to during acceptance testing.

2.1.56	"Transmission Links" The means used for interconnecting distributed Units for the purpose of conveying signals, operating data or an energy supply. This equipment is generally electrical but can be mechanical, pneumatic or hydraulic.

2.1.57	"Units" The smallest divisions of system components that will be considered, as these combinations of components will be treated as single entities for purposes of identification, analysis or replacement.

2.1.58	"Vehicle Type" A vehicle fitted with Specific Components for the use of Hydrogen which do not differ with respect to the following conditions:

- The Manufacturer,

- The type designation established by the Manufacturer,

- The essential aspects of construction and design,

- Chassis/floor pan (obvious and fundamental differences),

- The installation of the Hydrogen Components (obvious and fundamental differences),

- Type(s) of specific components.

2.1.59	“Working Pressure”: The Settled Pressure at a uniform temperature of 15°C that a component is subjected to.

2.2	CONTAINER TYPES

A Container shall be classified into the following types according the type of construction:

Type 1 (Metal)		All metal construction.

Type 2 (Hoop Wrapped)	Metal Liner reinforced with resin impregnated continuous filament wrapped in discrete circumferential bands.

Type 3 (Fully Wrapped)	Metal Liner reinforced with resin impregnated continuous filament fully wrapped around the Liner.

Type 4 (Non-metallic)	Resin impregnated continuous filament with a non-metallic Liner.

Type 5 (Other)	Type of construction not covered by Types 1 to 4 above.

2.3	PRESSURE CLASSIFICATIONS

2.3.1	Hydrogen Components and Systems for use in vehicles shall be classified with regard to their Working Pressure and function as defined below:

Class 0	High pressure components/systems including tubes and fittings containing hydrogen at a Working Pressure greater than 3 MPa.

Class 1	Medium pressure components/systems including tubes and fittings containing hydrogen at a Working Pressure greater than 0.45 MPa and up to and including 3.0 MPa.

Class 2	Low pressure components/systems including tubes and fittings containing hydrogen at a Working Pressure up to and including 0.45 MPa.

2.3.2	A Hydrogen Component or System can consist of several parts, each part classified in its own class with regard to Working Pressure and function.

2.4	SERVICE CONDITIONS

Unless indicated otherwise the following service conditions will apply throughout this Regulation and its Annexes:

2.4.1	Service Life

The service life for which Hydrogen Components and their installation shall be safe and shall be specified by the component Manufacturer, and may vary with different applications. The minimum service life shall be 20 years unless indicated otherwise in this Regulation and its Annexes.

The maximum number of filling cycles shall be 1 000 cycles per year of service unless stated otherwise in this Regulation or its Annexes.

2.4.2	Working Pressure

Unless indicated otherwise the Working Pressure(s) of the Hydrogen System(s) shall be in accordance with recognised industry standards for CGH2 systems where available otherwise being specified by the vehicle Manufacturer.

2.4.3	External Surfaces

Unless indicated otherwise the Hydrogen Components and their installation need not be designed for continuous exposure to mechanical or chemical attack, e.g. leakage from cargo that may be carried on vehicles or severe abrasion damage from road conditions. However, the effects on external surfaces of the Hydrogen Components in their installed position shall be considered in relation to the following:

- Water, either by intermittent immersion or road spray,

- Salt, due to the operation of the vehicle near the ocean or where ice melting salt is used,

- Ultra-violet radiation from sunlight,

- Impact of gravel,

- Solvents, acids and alkalis, fertilisers,

- Automotive fluids, including gasoline, hydraulic fluids, battery acid, glycol and oils,

- Exhaust gases.

2.4.4	Gas Permeation

Permeation of gas through the walls of Hydrogen Components shall be considered in the design of the Hydrogen Components.

2.4.5	Gas Composition

Compressed hydrogen gas shall comply with gas compositions specified in ISO Hydrogen Fuel Specification standard ISO/FDIS 14687:1999 “Hydrogen Fuel – Product Specification”.

2.4.6	Service Temperatures

2.4.6.1	Material Temperatures

The temperature range of materials used in Hydrogen Components shall be:

| Propulsion System Compartment | On Board |
| --- | --- |
| -40°C to +120°C | -40°C to +85°C |

For Hydrogen Components outside of the Propulsion System compartment material temperatures exceeding 65°C are considered to be sufficiently local or of short enough duration that they are not considered for the mechanical design of the equipment.

2.4.6.2	Gas Temperatures

The Settled Temperature of gas may vary between -40°C to +65°C. Developed gas temperatures during filling or discharging shall not exceed +85°C.

PART I

SPECIFIC COMPONENTS OF

MOTOR VEHICLES USING COMPRESSED GASEOUS HYDROGEN

3	APPLICATION FOR APPROVAL

3.1	The application for approval of a Specific Component or Multifunctional Component shall be submitted by the holder of the trade name or mark or by his duly accredited representative.

3.2	The application for Type Approval shall be accompanied by the following documents in triplicate:

- A detailed description of the type of the Specific Component according to Annex 1 to this Regulation,

- A drawing of the Specific Component sufficiently detailed and on an appropriate scale with a list of parts including material data and intended operating mode,

- In case of an approval for a Container, a piping and instrumentation drawing.

- Description of the manufacturing process.

- Verification of compliance with the specifications prescribed in Paragraph 6 of this Regulation.

3.3	At the request of the Technical Service responsible for conducting approval tests, at least two samples of the Specific Component shall be provided if not otherwise stated in the Annexes to this Regulation. Supplementary samples shall be supplied upon request.

3.4	The Competent Authority shall verify the existence of satisfactory arrangements for ensuring effective control of conformity of production before type approval is granted.

4	MARKINGS

4.1	The samples of the Specific Component submitted for approval shall bear the trade name or mark of the Manufacturer and the type; and in addition for Flexible Fuel Lines the manufacturing month and year. The marking shall be legible and indelible.

4.2	All Specific Components shall have a space large enough to accommodate the approval mark. This space shall be shown on the drawings referred to in Paragraph 3.2 ii) above.

4.3	On each Container the Manufacturer shall provide clear permanent markings with a font not less than 6 mm high. Marking shall be made either by labels incorporated into resin coatings, labels attached by adhesive, low stress stamps used on the thickened ends of Type 1 and 2 designs, or any combination of the above. Adhesive labels and their application shall be in accordance with ISO 7225, or an equivalent Standard. Multiple labels are allowed and should be located such that they are not obscured by mounting brackets. Every Container approved in accordance with this Regulation shall bear a marking place with the following data clearly legible:

- Name of the Manufacturer,

- A unique serial number for every Container,

- The marking “CGH2”,

- Working pressure (MPa) at 150C and Maximum Filling Mass of Hydrogen (kg)

- The water capacity in litres,

- Empty weight (kg),

- Year and month of approval, e.g. 2000/01,

- Approval mark in accordance with Paragraph 5.4 below,

- When labels are used, the unique serial number referred to in ii) above shall be stamped on an exposed surface,

- The marking “DO NOT USE AFTER yyyy/mm” where yyyy/mm is the year and month of approval plus the approved lifetime of the Container.

5	APPROVAL

5.1	If the Specific Component samples submitted for approval meet the relevant requirements of Paragraph 6 of this Regulation, approval of the type of Specific Component shall be granted.

5.2	An Approval number shall be assigned to each type of Specific Component or Multifunctional Component approved. Its first two digits shall indicate the series of amendments to this Regulation incorporating the most recent major technical amendments made at the time of granting the approval (00 for the Regulation in its original form). The same Contracting Party shall not assign the allocated code to another type of Specific Component.

5.3	Notice of approval or of refusal or of extension of approval of a Hydrogen Component in accordance with this Regulation shall be communicated to the Parties to the Agreement applying this Regulation by the Administrative Department by means of a form conforming to the model in Annex 4 to this Regulation.

5.4	In addition to the markings prescribed in Paragraphs 4.1 and 4.3 above, there shall be affixed conspicuously in the space referred to in Paragraph 4.2 above, to all Specific Components conforming to a type approved under this Regulation, an international approval mark consisting of:

5.4.1	A circle surrounding the letter "E“ followed by the distinguishing number of the country which has granted approval (see Note 1/ below).

5.4.2	The number of this Regulation, followed by the letter "R", a dash and the approval number to the right of the circle prescribed in Paragraph 5.4.1. This approval number consists of the Specific Component type approval number which appears on the certificate completed for this type (see Paragraph 5.2 above and Annex 4) proceeded by 2 figures indicating the sequence of the latest series of amendments to this Regulation.

5.5	The approval mark shall be clearly legible and indelible.

5.6	Annex 3 to this regulation gives examples of the arrangement of the aforesaid approval mark.

__________________________________________________________________________

Note 1/:

1 for Germany, 2 for France, 3 for Italy, 4 for Netherlands, 5 for Sweden, 6 for Belgium, 7 for Hungary, 8 for the Czech Republic, 9 for Spain, 10 for Yugoslavia, 11 for the United Kingdom, 12 for Austria, 13 for Luxembourg, 14 for Switzerland, 15 (vacant), 16 for Norway, 17 for Finland, 18 for Denmark, 19 for Romania, 20 for Poland, 21 for Portugal, 22 for the Russian Federation, 23 for Greece, 24 Ireland, 25 for Croatia, 26 for Slovenia, 27 for Slovakia, 28 for Belarus, 29 for Estonia, 30 (vacant), 31 for Bosnia and Herzegovina, 32-36 (vacant), 37 for Turkey,38-39 (vacant) and 40 for the former Yugoslav Republic of Macedonia, 43 Japan.

Subsequent numbers shall be assigned to other countries in the chronological order in which they ratify or accede to the Agreement concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions, and the numbers thus assigned shall be communicated by the Secretary-General of the United Nations to the Contracting Parties to the Agreement.

6	SPECIFICATIONS FOR HYDROGEN COMPONENTS

6.1	GENERAL PROVISIONS

6.1.1	The Hydrogen Components shall function in a correct and safe way as specified in this Regulation. They shall reliably withstand the mechanical, thermal and chemical service conditions specified in Paragraph 2.4 of this Regulation without leaking or visibly deforming.

6.1.2	The materials of the components which are in contact with hydrogen shall be compatible with hydrogen and expected additives and production contaminants.

6.1.3	Those parts of a component whose correct and safe functioning is liable to be influenced by hydrogen, high pressure or vibrations shall be submitted to the relevant test procedures described in the Annexes to this Regulation. In particular the provisions of Paragraph 6 shall be fulfilled.

6.1.4	All Hydrogen Components designed to allow uni-directional flow only, shall have the flow direction clearly indicated.

6.1.5	Unless indicated otherwise the following Design Pressures shall be used for all Hydrogen Components other than the Container(s):

- The Hydrogen System upstream of the first or only Pressure Regulator, excluding the Container shall have a Design Pressure equal to at least the Design Pressure of the Container. It shall be designed with a coefficient of safety not less than that of the Container.

- The Hydrogen System downstream of a Pressure Regulator shall be protected against overpressure and shall be designed for at least 3.0 times the outlet pressure (downstream Working Pressure) of the first Pressure Regulator upstream.

6.1.6	All Hydrogen Components shall have the Working Pressure for which they have been designed or in the case of Specific Components approved, clearly indicated.

6.2	PROVISIONS REGARDING HYDROGEN CONTAINERS

6.2.1	Hydrogen containers shall be type approved pursuant to the provisions laid down in Annex 7 to this Regulation.

6.3	PROVISIONS REGARDING PRESSURE RELIEF DEVICES

6.3.1	Pressure Relief Device For The Container

6.3.1.1	The Pressure Relief Device shall be temperature triggered.

6.3.1.2	The Pressure Relief Device for the Container shall limit the pressure inside the Container by opening a temperature fusible plug at 110(C ( 10(C.

6.3.1.3	The Pressure Relief Devices of the Container shall be designed according to Annex 8A to this Regulation.

6.3.1.4	The rating of the Pressure Relief Devices shall be clearly marked. Tampering with the Pressure Relief Devices shall be prevented by means of a lead seal or equivalent system.

6.3.1.5	The Pressure Relief Devices shall be type approved pursuant to the provisions laid down in Annex 8A to this Regulation.

6.3.2	Pressure Relief Devices For Other Hydrogen Components

6.3.2.1	The rating of Pressure Relief Devices downstream of Pressure Regulators shall not exceed the Working Pressure of the components downstream of the Pressure Regulator.

6.3.2.2	Pressure Relief devices shall be temperature triggered, except when protecting Class 1, 2 ,3 and 4 Hydrogen Components or Systems in which case they may be pressure triggered.

6.3.2.3	The Pressure Relief Devices shall be designed and type approved pursuant to the provisions laid down in Annex 8A to this Regulation.

6.4	PROVISIONS REGARDING HYDROGEN VALVES

6.4.1	The Hydrogen valves shall be type approved pursuant to the provisions laid down in Annex 8B to this Regulation.

6.4.2	Automatic Valves shall fail to the safest mode of operation for the particular application, i.e. fail safe.

6.5	PROVISIONS REGARDING HEAT EXCHANGERS

6.5.1	The Working Pressure of the contact surface between the different circuits of the Heat Exchanger shall be based on the highest Working Pressure of the different circuits.

6.5.2	A safety system shall be provided to detect failure of the Heat Exchanger or prevent any hydrogen from entering the circuit(s) located downstream of it, if the circuits(s) has not been designed for this.

6.5.3	Heat Exchangers shall be type approved pursuant to the provisions laid down in Annex 8C to this Regulation.

6.6	PROVISIONS REGARDING REFUELLING CONNECTIONS OR RECEPTACLES

6.6.1	The Refuelling Connections Or Receptacles shall be protected against contamination and vandalism.

6.6.2	The Refuelling Connections Or Receptacles shall be type approved pursuant to the provisions laid down in Annex 8D to this Regulation.

6.7	PROVISIONS REGARDING PRESSURE REGULATORS

6.7.1	The Pressure Regulators shall be type-approved pursuant to the provisions laid down in Annex 8E to this Regulation.

6.8	PROVISIONS REGARDING SENSORS FOR HYDROGEN SYSTEMS

6.8.1	Sensors for Hydrogen Systems shall be type approved pursuant to the provisions laid down in Annex 8F to this Regulation.

6.9	PROVISIONS REGARDING FLEXIBLE FUEL LINES

6.9.1	Flexible Fuel Lines shall be type approved pursuant to the provisions laid down in Annex 8G to this Regulation.

6.10	PROVISIONS REGARDING FITTINGS OR SCREWED CONNECTION SYSTEMS

6.10.1	Fittings Or Screwed Connection Systems shall be type approved pursuant to the provisions laid down in Annex 8H to this Regulation.

6.11	PROVISIONS REGARDING EXCESS FLOW SYSTEMS

6.11.1	Excess Flow Systems shall be type approved pursuant to the provisions laid down in Annex 8I to this Regulation.

6.12	PROVISIONS REGARDING HYDROGEN FILTERS

6.12.1	Hydrogen Filters shall be type approved pursuant to the provisions laid down in Annex 8J to this Regulation.

6.13	GENERAL PROVISIONS REGARDING ELECTRICAL COMPONENTS

6.13.1	Electrical components of equipment in contact with hydrogen shall:

    - Be insulated in such a manner that no current passes through hydrogen containing parts,

    - Have the electrical system of the device insulated from:

      - the body of the component,

      - the Container.

    - Insulation resistance shall be > 10 M(.

6.13.2	All electrical connections for the Hydrogen System shall comply with insulation class IP 54 according to IEC 60529 Degrees of Protection Provided By Enclosures (IP Code) 11/1989 and Amendment No.1 (11/99), except where they are within a gas tight housing as required by Paragraph 14.4.3 of this Regulation when the requirements of Paragraph 14.8.3 of this Regulation shall apply.

6.13.3	To establish an isolated and tight electrical connection for power supply bushing, it shall be of a Gas Tight sealed type where Hydrogen Components are present or hydrogen leaks are possible.

7	MODIFICATIONS OF A TYPE OF A SPECIFIC COMPONENT AND EXTENSION OF APPROVAL

7.1	Every modification of a type of a Specific Component shall be notified to the Administrative Department which granted the type approval. The Administrative Department may then either:

7.1.1	Consider that the modifications made are unlikely to have an appreciably adverse effect, and that the component still meets the requirements of this Regulation; or

7.1.2	Require a further report from the Technical Service responsible for carrying out the tests.

7.2	Notice of confirmation, extension or refusal of approval shall be communicated by the procedure specified in Paragraph 5.3 of this Regulation to the Parties to the Agreement which apply this Regulation.

7.3	The competent authority issuing the extension of approval shall assign a series number to each communication form (specified in Paragraph 5.3 of this Regulation) issued for such an extension, and shall inform the other Parties to the Agreement with a form conforming to the model in Annex 4 to this Regulation.

8	CONFORMITY OF PRODUCTION

8.1	The conformity of production procedures shall comply with those set out in the Agreement, Appendix 2 (E/ECE/324-E/ECE/TRANS/505/Rev.2) and with the following requirements:

8.1.1	A Hydrogen Component approved to this Regulation shall be manufactured so as to conform to the type approved by meeting the requirements specified in Paragraph 6 above.

8.1.2	The authority which has granted Type Approval may at any time verify the conformity control methods applied in each production facility. The normal frequency of these verifications shall be once every two years.

9	PENALTIES FOR NON-CONFORMITY OF PRODUCTION

9.1	The approval granted in respect of a type of component in accordance with this Regulation may be withdrawn if the requirements laid down in Paragraph 8 above are not complied with.

9.2	If a Contracting Party to the Agreement which applies this Regulation withdraws an approval it has previously granted, it shall immediately notify the other Contracting Parties applying this Regulation by means of a communication form conforming to the model in Annex 4 to this Regulation.

10	PRODUCTION DEFINITELY DISCONTINUED

If the holder of the approval for a type of component approved in accordance with this Regulation, permanently ceases to manufacture the component, he shall immediately inform the authority which granted the approval. Upon receiving the relevant communication, that authority shall inform the other Parties to the Agreement applying this Regulation of that communication, by means of a communication form conforming to the model in Annex 4 to this Regulation.

11	NAMES AND ADDRESSES OF TECHNICAL SERVICES RESPONSIBLE FOR CONDUCTING APPROVAL TESTS, AND OF ADMINISTRATIVE DEPARTMENTS

The Parties to the Agreement applying this Regulation shall communicate to the United Nations Secretariat the names and addresses of the Technical Services responsible for conducting approval tests and of the Administrative Departments which grant approval and to which forms certifying approval or extension or refusal or withdrawal of approval issued in other countries, are to be sent.

PART II

VEHICLES WITH REGARD TO THE INSTALLATION OF SPECIFIC COMPONENTS FOR THE USE OF COMPRESSED GASEOUS HYDROGEN

12	APPLICATION FOR APPROVAL

12.1	The application for Approval of a Vehicle Type with regard to the installation of Specific Components for the use of compressed gaseous hydrogen shall be submitted by the vehicle Manufacturer or by his duly accredited representative.

12.2	The application shall be accompanied by a description of the vehicle comprising all the relevant particulars referred to in Annex 2 to this Regulation in triplicate.

12.3	A vehicle, representative of the Vehicle Type to be approved, shall be submitted to the Technical Service conducting the approval tests.

12.4	The competent authority shall verify the existence of satisfactory arrangements for ensuring effective control of conformity of production before type approval is granted.

13	APPROVAL

13.1	If the vehicle submitted for Type Approval pursuant to this Regulation is fitted with Specific Components in accordance with Part I of this Regulation and meets the requirements of Part II of this Regulation, approval of that Vehicle Type shall be granted.

13.2	An approval number shall be assigned to each Vehicle Type approved. Its first two digits shall indicate the series of amendments to this Regulation incorporating the most recent major technical amendments made at the time of granting the approval (00 for the Regulation in its original form). The same Contracting Party shall not assign the approval number to another Vehicle Type.

13.3	Notice of approval or of refusal or of extension of Approval of a Vehicle Type in accordance with this Regulation shall be communicated to the Parties to the Agreement applying this Regulation by means of a form conforming to the model in Annex 6 to this Regulation.

13.4	There shall be affixed to every Vehicle Type approved under this Regulation, conspicuously and in a readily accessible space specified on the approval form referred to in Paragraph 13.3 above, an international approval mark consisting of:

13.4.1	A circle surrounding the letter "E“ followed by the distinguishing number of the country which has granted approval (see Note 1/ below).

13.4.2	The number of this Regulation, followed by the letter "R", a dash and the approval number to the right of the circle prescribed in Paragraph 13.4.1 above. This approval number consists of the Vehicle Type approval number which appears on the certificate completed for this type (see Paragraph 13.2 and 13.3 above and Annex 6).

13.5	If the vehicle conforms to a vehicle approved under one or more other Regulations annexed to the Agreement in the country which has granted approval under this Regulation, the symbol prescribed in Paragraph 13.4.1 above need not to be repeated. In such a case, the Regulation and approval numbers and the additional symbols of all the Regulations under which approval has been granted in the country which has granted approval under this Regulation shall be placed in vertical columns to the right of the symbol prescribed in Paragraph13.4.1.

13.6	The approval mark shall be clearly legible and be indelible.

13.7	The approval mark shall be placed closed to or on the statutory plate of the vehicle.

13.8	Annex 5 to this Regulation gives examples of the arrangement of the approval mark referred to above.

__________________________________________________________________________

Note 1/:

1 for Germany, 2 for France, 3 for Italy, 4 for Netherlands, 5 for Sweden, 6 for Belgium, 7 for Hungary, 8 for the Czech Republic, 9 for Spain, 10 for Yugoslavia, 11 for the United Kingdom, 12 for Austria, 13 for Luxembourg, 14 for Switzerland, 15 (vacant), 16 for Norway, 17 for Finland, 18 for Denmark, 19 for Romania, 20 for Poland, 21 for Portugal, 22 for the Russian Federation, 23 for Greece, 24 Ireland, 25 for Croatia, 26 for Slovenia, 27 for Slovakia, 28 for Belarus, 29 for Estonia, 30 (vacant), 31 for Bosnia and Herzegovina, 32-36 (vacant), 37 for Turkey,38-39 (vacant) and 40 for the former Yugoslav Republic of Macedonia, 43 Japan.

Subsequent numbers shall be assigned to other countries in the chronological order in which they ratify or accede to the Agreement concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions, and the numbers thus assigned shall be communicated by the Secretary-General of the United Nations to the Contracting Parties to the Agreement.

14	REQUIREMENTS FOR THE INSTALLATION OF SPECIFIC COMPONENTS FOR THE USE OF COMPRESSED GASEOUS HYDROGEN WITHIN MOTOR VEHICLES

14.1	GENERAL

14.1.1	The Hydrogen System of a vehicle shall function in a safe and proper manner up to the Working Pressure for which it has been designed and approved. It shall reliably withstand the mechanical, thermal and chemical service conditions specified in Paragraph 2.4 of this Regulation without leaking or visibly deforming. The number of Hydrogen Components, connections and the length of lines shall be kept to the minimum compatible with safety and the correct functioning of the Hydrogen System.

14.1.2	Specific Components of Hydrogen Systems shall be type approved pursuant to Part I of this Regulation.

14.1.3	The materials used in Hydrogen Systems shall be compatible with gaseous hydrogen and expected additives and production contaminants, and expected temperatures and pressures.

14.1.4	All components of a Hydrogen System shall be mounted and connected in a proper way.

14.1.5	The Hydrogen System shall be Gas Tight.

14.1.6	The Hydrogen System shall be installed such that it is protected against damage so far as is reasonably practical, such as damage due to moving vehicle components, collision, grit or due to the loading or unloading of the vehicle or the shifting of loads.

14.1.7	The service temperature range shall be in accordance with Paragraph 2.4.6 of this regulation. The service temperature range can create a pressure increase in the Container(s) and in the other Hydrogen Components which are installed upstream of the first pressure regulator.

14.1.8	No component of the Hydrogen System, including any protective materials that form part of such components, shall project beyond the outline of the vehicle or protective structure. When the vehicle is ready for use the lowest part of the Hydrogen System shall not reduce the Ground Clearance Of The Vehicle. This shall not apply if a Hydrogen Component is adequately protected and no part of the Hydrogen Component is located lower than this protective structure.

14.1.9	No component of the Hydrogen System shall be located near the exhaust or other heat source, unless such components are adequately shielded against heat.

14.1.10The ventilating or heating system for a passenger compartment and places where leakage or accumulation of hydrogen is possible shall be kept apart so that hydrogen is not drawn into the vehicle.

14.1.11Failure of the heating or cooling circuits shall not damage the Hydrogen System.

14.1.12The Hydrogen System and in particular Container(s) and Safety Devices shall be adequately protected against any kind of corrosion, e.g. due to road de-icing salt, leakage of acid batteries, etc.

14.1.13All Pressure Relief Devices, other safety components and vent lines shall be protected against vandalism so far as reasonably practicable.

14.1.14A minimum overpressure of 0.2 MPa shall be maintained in the Container at ambient temperature.

14.1.15In the event of Hydrogen leakage or venting hydrogen shall not be allowed to accumulate in enclosed or semi-enclosed spaces

14.2	COMPONENTS OF A HYDROGEN SYSTEM

14.2.1	A Hydrogen System shall contain at least the following components:

14.2.1.1	Container(s),

14.2.1.2	Automatic valve(s),

14.2.1.3	Excess flow system

14.2.1.4	Fittings or screwed connection systems,

14.2.1.5	Flexible fuel lines or rigid fuel lines,

14.2.1.6	Hydrogen conversion system, e.g. combustion engine, fuel cell, catalytic heater etc.,

14.2.1.7	Pressure or hydrogen remaining indicator,

14.2.1.8	Pressure and temperature sensors,

14.2.1.9	Pressure regulator(s)

14.2.1.10	Pressure relief device (temperature triggered),

14.2.1.11	Refuelling connection or receptacle,

      - Safety instrumented system,

14.2.1.13	Check or non-return valve(s).

14.2.2	The Hydrogen System could also include the following components:

14.2.2.1	Electronic control unit,

14.2.2.2	Fuel selection system and electrical systems,

14.2.2.3	Gas flow adjuster,

14.2.2.4	Gas tight housing,

14.2.2.5	Hydrogen injector(s) or hydrogen/air mixer,

14.2.2.6	Hydrogen sensor,

14.2.2.7	Manual valve(s),

14.2.2.8	Pressure relief device (pressure triggered) - shall not be used in Class 0 Hydrogen Components or Systems,

14.2.2.9	Flow sensor,

14.2.2.10	Heat exchanger,

14.2.2.11	Hydrogen filter,

All Specific Components must have a type approval

14.3	INSTALLATION OF A HYDROGEN CONTAINER ON-BOARD A VEHICLE

14.3.1	Container(s) shall be permanently installed on-board the vehicle and may only be removed for maintenance. Container(s) shall not be installed in the propulsion system compartment.

14.3.2	Container(s) can fulfil integrated functions of the vehicle. Container(s) shall be designed to fulfil the integrated function requirements plus the Container requirements.

14.3.3	Container(s) including Safety Devices must be mounted and fixed so that the following accelerations can be absorbed (without damage of the safety related parts) when the Container(s) are full. No uncontrolled release of hydrogen is permitted.

Vehicles of categories M1 and N1:

a) +/-20 g in the direction of travel

b) +/-8 g horizontally perpendicular to the direction of travel

Vehicles of categories M2 and N2:

a) +/-10 g in the direction of travel

b) +/-5 g horizontally perpendicular to the direction of travel

Vehicles of categories M3 and N3:

a) +/-6.6 g in the direction of travel

b) +/-5 g horizontally perpendicular to the direction of travel

14.3.4	The provision of Paragraph 14.3.3 shall not apply if the vehicle is approved according to 96/79/EC or ECE R 94 and 96/27/EC or ECE R 95.

14.3.5	Pressure Relief Device(s) shall form the fire protection system for a Container to prevent rupture. Thermal insulation shall only be used as a secondary protective measure.

14.3.6	Container with non-metallic liners shall not be installed inside the vehicle.

14.4	ACCESSORIES FITTED TO A CONTAINER

14.4.1	Automatic Valves Or Non-return Valves

14.4.1.1	All hydrogen Fuel Supply Lines shall be secured with an Automatic Valve (idle closed). These valves shall be mounted directly on or within every Container.

14.4.1.2	The Refuelling Connection or Receptacle shall be integrated with a Non-return Valve. If the Refuelling Connection or Receptacle is not mounted directly on or within the Container, a Non-return Valve or an Automatic Valve integrating the function of a Non-return Valve shall be mounted directly on or within the Container to secure the refuelling line.

14.4.1.3	In the event of breakage of the Withdrawal and refuelling lines, the isolating valves referred to in Paragraphs 14.4.1.1 and 14.4.1.2. shall not be separated from the Container.

14.4.1.4	Automatic Valves isolating each Container shall close if any safety related malfunction of the Hydrogen System occurs and in the event of a crash or break of the Fuel Supply Line(s).

14.4.1.5	The Automatic Valve for the Fuel Supply Line of the Propulsion System shall be operated such that the hydrogen supply is cut off when the Propulsion System is switched off, irrespective of the position of the activation switch, and shall remain closed until the Propulsion System is required to operate.

14.4.1.6	The Automatic Valve for the Fuel Supply Line of other Hydrogen Conversion System(s) shall be operated such that the hydrogen supply is cut off when the respective Hydrogen Conversion System is switched off, irrespective of the position of the activation switch, and shall remain closed until the Hydrogen Conversion System is required to operate.

14.4.2	Pressure Relief Devices

14.4.2.1	A Pressure Relief Device (temperature triggered) shall be fitted to or within each Container in such a manner that it shall discharge into an atmospheric outlet line that vents to the outside of the vehicle.

14.4.2.2	It shall not be possible to isolate the Pressure Relief Devices from the Hydrogen Components or section of the Hydrogen System protected by the Pressure Relief Device, by the normal operation or failure of another component.

14.4.2.3	The vent lines of Pressure Relief Devices shall not discharge into a wheel arch, nor shall they be aimed at a heat source such as the exhaust or at other Containers if fitted. Additionally they shall discharge such that hydrogen cannot enter the inside of the vehicle.

14.4.2.4	If a Container is greater than 1.65m long a second Pressure Relief Device (temperature triggered) shall be fitted at the opposite end of the Container to that required in Paragraph 14.4.2.1 above.

14.4.2.5	The internal dimensions of the Pressure Relief Device and the Lines both before and after the Pressure Relief Devices shall not impede the function of the Pressure Relief Devices.

14.4.2.6	In the event of accidents, e.g. vehicle rolling over, it must be ensured so far as is reasonably practicable that the Pressure Relief Device and the associated vent line remain capable of functioning.

14.4.2.7	The vent line of the Pressure Relief Device shall be protected against blockage, e.g. by dirt, ice, and ingress of water etc. so far as is reasonably practicable.

14.4.2.8	The vent line of the Pressure Relief Device shall be protected against vandalism so far as is reasonably practicable.

14.4.2.9	The outlet of the Pressure Relief Device shall be orientated such that if the vent line becomes detached from the Pressure Relief Device, the resulting gas flow does not impinge directly on other Containers where fitted unless they are protected.

14.4.3	Gas Tight Housing On The Container(s)

14.4.3.1	All non-welded connections between Hydrogen carrying components and Hydrogen Components which can leak hydrogen, that are mounted within the passenger or luggage compartment or other non-ventilated compartment shall be enclosed by a Gas Tight housing.

14.4.3.2	The Gas Tight housing shall be vented to the atmosphere.

14.4.3.3	The ventilation opening of the Gas Tight housing shall be at the highest point of the housing when installed in the vehicle. It shall not ventilate into a wheel arch, nor shall it be aimed at a heat source such as the exhaust. Additionally it shall vent such that hydrogen cannot enter the inside of the vehicle.

14.4.3.4	There shall be no unprotected ignition sources inside the gas tight housing.

14.4.3.5	The Gas Tight housing shall be hermetically sealed for test purposes and when tested shall be Gas Tight at an over pressure of 0.01 MPa and without any permanent deformations.

14.4.3.6	Any connecting system shall be secured by clamps, or other means, to the Gas Tight housing or sleeve and the lead-through to ensure that a Gas Tight joint is formed.

14.4.4	Excess Flow System

14.4.4.1	An Excess Flow System shall be connected to, or mounted within, the Container which shall automatically shut off, or limit the flow of hydrogen gas when the flow exceeds 1.5 times the maximum design value.

14.4.4.2	The Excess Flow System may incorporate the Automatic Valve referred to in Paragraph 14.4.1.1 of this Regulation.

14.4.4.3	The Excess Flow System may be designed with a bypass to allow for the equalisation of pressures. If a bypass is fitted the flow through the bypass when the flow is limited by the system shall not exceed 500 Ncm3/min at a differential pressure of 0.7 MPa.

14.5	RIGID AND FLEXIBLE FUEL LINES

14.5.1	Rigid Fuel Lines shall be secured such that they shall not be subjected to critical vibration or other stresses.

14.5.2	Flexible Fuel Lines shall be secured such that they shall not be subjected to torsional stresses and abrasion is avoided.

14.5.3	At the fixing points the fuel line, flexible or rigid, shall be fitted in such a way that they cannot make metal to metal contact to prevent galvanic and crevice corrosion.

14.5.4	Rigid and flexible fuel lines shall be routed to reasonably minimise exposure to accidental damage whether inside the vehicle, e.g. due to placing or movement of luggage or other loads, or outside the vehicle, e.g. due to rough ground or vehicle jacks etc.

14.5.5	At passages through the vehicle body or other hydrogen components, the fuel lines shall be fitted with grommets or other protective material.

14.5.6	Rigid and Flexible Fuel lines shall be mounted to reasonably minimise stresses in the lines during removal or installation of adjoining Hydrogen Components.

14.5.7	In the passenger or enclosed luggage compartment the fuel lines shall be enclosed in a sleeve which meets the same requirements as specified for a Gas Tight housing in Paragraphs 14.4.3.2 to 14.4.3.6.

14.5.8	Metallic Rigid Fuel Lines shall be seamless if used in Class 0 Hydrogen Systems, and shall elongate by at least 14% before rupture.

14.5.9	For all Class 0 Hydrogen Systems the complete Fuel Line assemblies shall be pressure cycle tested in accordance with Paragraph 14.3 of Annex 9 to this Regulation.

14.5.10Full penetration butt welding shall be used for welded connections of metallic Rigid Fuel Lines if used in Class 0 Hydrogen Systems.

14.6	FITTINGS OR GAS CONNECTIONS BETWEEN HYDROGEN COMPONENTS

14.6.1	Fittings for stainless steel tubes shall only be stainless steel fittings.

14.6.2	The number of joints shall be limited to a minimum.

14.6.3	Any joints shall be made in locations where access is possible for inspection without the use of tools and also for leak testing.

14.7	REFUELLING CONNECTION OR RECEPTACLE

14.7.1	The Refuelling Connection or Receptacle shall be secured against maladjustment and rotation, and shall be protected from dirt and water. It shall be safe against reasonably foreseeable handling errors.

14.7.2	The Refuelling Connection or Receptacle shall be installed such that access for refuelling shall not be required in the passenger, luggage, or in any other unventilated compartment.

14.7.3	The refuelling line shall be secured at the container as described in Paragraph 14.4.1.2.

14.7.4	It shall be ensured that, where fitted, the Propulsion System or Hydrogen Conversion System(s) excluding Safety Devices are not operating and that the vehicle is immobilised while the Refuelling Connection or Receptacle is connected to the refuelling infrastructure.

14.7.5	The Refuelling Connection or Receptacle shall not be mounted within the external energy absorbing elements, e.g. bumper.

14.8	ELECTRICAL INSTALLATION

14.8.1	The electrical components of the Hydrogen System shall be protected against overloads.

14.8.2	Electric or electronic equipment in the gas tight housing shall be applicable for the hazardous zone 1 according to IEC 60079-10 "Electrical apparatus for explosive gas atmospheres- Part10 Classification of hazardous areas" from 12/1995 and comply with EN 50014:1997 Electrical Apparatus For Potentially Explosive Atmospheres - General Requirements, to EN 50021.

14.8.3	The metallic components of the Hydrogen System shall have electrical continuity with the vehicle’s earth.

14.8.4	During the refuelling process the Hydrogen system shall have electrical continuity with the refuelling facilities before hydrogen transfer is permitted.

14.9	SAFETY INSTRUMENTED SYSTEMS

14.9.1	Safety Instrumented Systems shall be fail-safe or redundant.

14.9.2	If Safety Instrumented Systems are fail-safe or self monitoring electronic systems, the special requirements according to Annex 10 to this Regulation are to be applied.

14.10	REQUALIFICATION

14.10.1	Periodic Requalification

Recommendations for periodic requalification by visual inspection or testing during the service life of the Container shall be provided by the Container manufacturer on the basis of use under the service conditions specified in this Annex. Every Container shall be visually inspected at least every 36 months, and at the time of any re-installation, for external damage and deterioration, including under the support straps. The visual inspection shall be performed by a competent agency approved or recognised by the Regulatory Authority, in accordance with the Manufacturers specifications:  Containers without a marking containing mandatory information, or with  labels containing mandatory information that are illegible in any way shall be removed from service. If the Container can be positively identified by manufacturer and serial number, a replacement label may be applied, allowing the Container to remain in service.

14.10.2	Containers Involved In Collisions

Containers which have been subject to direct impact damage during vehicle collisions or other accidents, e.g. during maintenance, shall be condemned and removed from service.

Containers which have been subjected to indirect impact damage that may have affected the Container, e.g. mechanical stresses transferred from the vehicle structure, shall be subjected to requalification inspection or testing before the Container may be returned to service, or condemned and removed from service

14.10.3	Containers Involved In Fires

Containers which have been subject to the action of fire shall be condemned and removed from service.

15	MODIFICATION OF A VEHICLE TYPE OR HYDROGEN SYSTEM AND EXTENSION OF APPROVAL

15.1	Every modification of the Vehicle Type or of its installation of Specific Components for the use of hydrogen shall be notified to the Administrative Department which granted approval of the Vehicle Type. The Administrative Department may then either:

15.1.1	Consider that the modifications made are unlikely to have an appreciably adverse effect, and that the vehicle still complies with the requirements of this Regulation; or

15.1.2	Require a further report from the Technical Service responsible for carrying out the tests.

15.2	Notice of confirmation, extension or refusal of approval shall be communicated by the procedure specified in Paragraph 13.3 of this regulation to the Parties to the Agreement which apply this Regulation.

15.3	The competent authority issuing the extension of approval shall assign a series number to each communication form (specified in Paragraph 13.3 of this regulation) issued for such an extension.

16	CONFORMITY OF PRODUCTION

The conformity of production procedures shall comply with those set out in the Agreement, Appendix 2 (E/ECE/324- E/ECE/TRANS/505/rev.2) and with the following requirements:

16.1	A vehicle approved to this Regulation shall be manufactured so as to conform to the type approved by meeting the requirements specified in Paragraph 14 of this regulation.

16.2	The authority which has granted type approval may at any time verify the conformity control methods applied in each production facility. The normal frequency of these verifications shall be once every two years.

17	PENALTIES FOR NON-CONFORMITY OF PRODUCTION

17.1	The Type Approval granted in respect of a Vehicle Type in accordance with this Regulation may be withdrawn if the requirements laid down in Paragraph 16 of this regulation are not complied with.

17.2	If a Contracting Party to the Agreement which applies this Regulation withdraws an approval it has previously granted, it shall immediately notify the other Contracting Parties applying this Regulation by means of a communication form conforming to the model in Annex 6 to this Regulation.

18	PRODUCTION DEFINITELY DISCONTINUED

If the holder of the approval permanently ceases to manufacture a type of vehicle approved in accordance with this Regulation, he shall immediately inform the authority which granted the approval. Upon receiving the relevant communication, that authority shall inform the other Parties to the Agreement applying this Regulation, by means of a communication form conforming to the model in Annex 6 to this Regulation.

19	NAMES AND ADDRESSES OF TECHNICAL SERVICES RESPONSIBLE FOR CONDUCTING APPROVAL TESTS, AND OF ADMINISTRATIVE DEPARTMENTS

The Parties to the Agreement applying this Regulation shall communicate to the United Nations Secretariat the names and addresses of the Technical Services responsible for conducting approval tests and of the Administrative Departments which grant approval and to which forms certifying approval or extension or refusal or withdrawal of approval issued in other countries, are to be sent.

Annex 1

ESSENTIAL CHARACTERISTICS OF SPECIFIC COMPONENTS

1	Automatic Valve(s):

1.1	Make(s):

1.2	Type(s):

1.3	Description and drawings:

1.4	Working Pressure(s) 2/:		MPa

1.5	Material(s):

2	Check valve(s) or non-return valve(s):

2.1	Make(s):

2.2	Type(s):

2.3	Description and drawings:

2.4	Working Pressure(s) : 2/		MPa

2.5	Material(s):

3	Container(s):

3.1	Make(s):

3.2	Type(s):

3.3	Description:

3.4	Capacity:		litres (water)

3.5	Dimensions:

3.6	Material(s):

3.7	Working Pressure: 		MPa

3.8	Drawings of the container(s) and installation in the vehicle:

4	Excess flow system:

4.1	Make(s):

4.2	Type(s):

4.3	Description and drawings:

4.4	Working Pressure(s) 2/:		MPa

4.5	Material(s):

5	Fittings or screwed connection systems:

5.1	Make(s):

5.2	Type(s):

5.3	Description and drawings:

5.4	Working Pressure(s) 2/:		MPa

5.5	Material(s):

6	Flexible Fuel Lines(s): yes/no 1/

6.1	Make(s):

6.2	Type(s):

6.3	Description and drawings:

6.4	Working Pressure(s) 2/:		MPa

6.5	Material(s):

7	Heat exchanger(s): yes/no 1/

7.1	Make(s):

7.2	Type(s):

7.3	Description and drawings:

7.4	Working Pressure(s) 2/:		MPa

7.5	Material(s):

8	Hydrogen Filter(s): yes/no 1/

8.1	Make(s):

8.2	Type(s):

8.3	Description and drawings:

8.4	Working Pressure(s) 2/:		MPa

8.5	Material(s):

9	Manual valve(s): yes/no 1/

9.1	Make(s):

9.2	Type(s):

9.3	Description and drawings:

9.4	Working Pressure(s) 2/:		MPa

9.5	Material(s):

10	Pressure or temperature or flow sensor(s)1/:  yes/no 1/

10.1	Make(s):

10.2	Type(s):

10.3	Operating principles including description and drawings:

10.4	Working Pressure(s): 2/		MPa

10.5	Material(s):

11	Pressure regulator(s): yes/no 1/

11.1.	Make(s):

11.2	Type(s):

11.3	Drawings:

11.4	Number of main adjustment points:

11.5	Description of principle of adjustment through main adjustment points:

11.6	Number of idle adjustment points:

11.7	Description of principles of adjustment through idle adjustment points:

11.8	Other adjustment possibilities: if so and which (description and drawings):

11.9	Working Pressure(s): 2/		MPa

12	Pressure relief device (temperature triggered):

12.1	Make(s):

12.2	Type(s):

12.3	Description and drawings:

12.4	Service Temperature: 2/		°C

12.5	Working Pressure(s) 2/:		MPa

12.6	Material:

12.7	Set temperature: 2/

13	Pressure relief device (pressure triggered): yes/no 1/

13.1	Make(s):

13.2	Type(s):

13.3	Description and drawings:

13.4	Working Pressure(s) 2/:		MPa

13.5	Material:

13.6	Set pressure: 2/

14	Refuelling connection or receptacle:

14.1	Make(s):

14.2	Type(s):

14.3	Operating principles including description and drawings:

14.4	Working Pressure(s) 2/:		MPa

14.5	Material:

Notes:

1/  Strike out what does not apply.

2/  Specify the tolerance.

Annex 2

ESSENTIAL CHARACTERISTICS OF THE VEHICLE,

HYDROGEN RELATED PROPULSION SYSTEM

AND OTHER HYDROGEN RELATED SYSTEMS

0	Description Of The Vehicle Type

0.1	Make:

0.2	Type(s):

0.3	Name and address of the Manufacturer:

1	Description Of The Hydrogen System Used For The propulsion Of The Vehicle1/

1.1	Description of the propulsion system:

1.2	Name and address of the Manufacturer:

1.3	Manufacturer's propulsion system code(s) (as marked on the propulsion system, or other means of identification):

1.4	Automatic Valve(s):

1.4.1	Make(s):

1.4.2	Type(s):

1.4.3	Working Pressure(s) 2/:		MPa

1.4.4	Approval number:

1.5	Check valve(s) or non-return valve(s):

1.5.1	Make(s):

1.5.2	Type(s):

1.5.3	Working Pressure(s) : 2/		MPa

1.5.4	Approval number:

1.6	Container(s):

1.6.1	Make(s):

1.6.2	Type(s):

1.6.4	Capacity:		litres (water)

1.6.5	Approval number

1.6.6	Working Pressure:		MPa

1.7	Excess flow system:

1.7.1	Make(s):

1.7.2	Type(s):

1.7.3	Working Pressure(s) 2/:		MPa

1.7.4	Approval number:

1.8	Fittings or screwed connection systems:

1.8.1	Make(s):

1.8.2	Type(s):

1.8.3	Working Pressure(s) 2/:		MPa

1.8.4	Approval number:

1.9	Flexible Fuel Lines(s): yes/no 1/

1.9.1	Make(s):

1.9.2	Type(s):

1.9.3	Working Pressure(s) 2/:		MPa

1.9.4	Approval number:

1.10	Heat exchanger(s): yes/no 1/

1.10.1	Make(s):

1.10.2	Type(s):

1.10.3	Working Pressure(s) 2/:		MPa

1.10.4	Approval number:

1.11	Hydrogen filter(s): yes/no 1/

1.11.1	Make(s):

1.11.2	Type(s):

1.11.3	Working Pressure(s) 2/:		MPa

1.11.4	Approval number:

1.12	Manual valve(s): yes/no 1/

1.12.1	Make(s):

1.12.2	Type(s):

1.12.3	Working Pressure(s) 2/:		MPa

1.12.4	Approval number:

1.13	Pressure or temperature or flow sensor(s)1/:  yes/no 1/

1.13.1	Make(s):

1.13.2	Type(s):

1.13.3	Working Pressure(s) 2/:		MPa

1.13.4	Approval number:

1.14	Pressure regulator(s): yes/no 1/

1.14.1	Make(s):

1.14.2	Type(s):

1.14.3	Working Pressure(s): 2/		MPa

1.14.4	Approval number:

1.15	Pressure relief device (temperature triggered):

1.15.1	Make(s):

1.15.2	Type(s):

1.15.3	Service Temperature: 2/		°C

- Approval number:

1.15.5	Working Pressure(s): 2/		MPa

1.16	Pressure relief device (pressure triggered): yes/no 1/

1.16.1	Make(s):

1.16.2	Type(s):

1.16.3	Working Pressure(s) 2/:		MPa

1.16.4	Approval number:

1.17	Refuelling connection or receptacle:

1.17.1	Make(s):

1.17.2	Type(s):

1.17.4	Working Pressure(s) 2/:		MPa

1.17.4	Approval number:

2	Description Of The Hydrogen System(s) Used For Purposes Other Than The Propulsion Of The Vehicle1/

2.1	Description of the hydrogen system(s):

2.2	Name and address of the Manufacturer(s):

2.3	Manufacturer's system code(s) (as marked on the system, or other means of identification):

2.4	Automatic Valve(s): yes/ same component as used in propulsion system 1/

2.4.1	Make(s):

2.4.2	Type(s):

2.4.3	Working Pressure(s) 2/:		MPa

2.4.4	Approval number:

2.5	Check valve(s) or non-return valve(s): yes/ same component as used in propulsion system 1/

2.5.1	Make(s):

2.5.2	Type(s):

2.5.3	Working Pressure(s) : 2/		MPa

2.5.4	Approval number:

2.6	Container(s):  yes/ same component as used in propulsion system 1/

2.6.1	Make(s):

2.6.2	Type(s):

2.6.4	Capacity:		litres (water)

2.6.5	Approval number

2.6.6	Working Pressure(s) : 2/		MPa

2.7	Excess flow system: yes/ same component as used in propulsion system 1/

2.7.1	Make(s):

2.7.2	Type(s):

2.7.3	Working pressure(s) 2/:		MPa

2.7.4	Approval number:

2.8	Fittings or screwed connection systems: yes/ same component as used in propulsion system 1/

2.8.1	Make(s):

2.8.2	Type(s):

2.8.3	Working Pressure(s) 2/:		MPa

2.8.4	Approval number:

2.9	Flexible Fuel Lines(s): yes/no/same component as used in propulsion system1/

2.9.1	Make(s):

2.9.2	Type(s):

2.9.3	Working Pressure(s) 2/:		MPa

2.9.4	Approval number:

2.10	Heat exchanger(s): yes/no/same component as used in propulsion system 1/

2.10.1	Make(s):

2.10.2	Type(s):

2.10.3	Working Pressure(s) 2/:		MPa

2.10.4	Approval number:

2.11	Hydrogen Filter(s): yes/no/same component as used in propulsion system 1/

2.11.1	Make(s):

2.11.2	Type(s):

2.11.3	Working Pressure(s) 2/:		MPa

2.11.4	Approval number:

2.12	Manual valve(s): yes/no/same component as used in propulsion system 1/

2.12.1	Make(s):

2.12.2	Type(s):

2.12.3	Working Pressure(s) 2/:		MPa

2.12.4	Approval number:

2.13	Pressure or temperature or flow sensor(s) 1/:  yes/no/same component as used in propulsion system 1/

2.13.1	Make(s):

2.13.2	Type(s):

2.13.3	Working Pressure(s) 2/:		MPa

2.13.4	Approval number:

2.14	Pressure regulator(s): yes/no/same component as used in propulsion system1/

2.14.1	Make(s):

2.14.2	Type(s):

2.14.3	Working Pressure(s): 2/		MPa

2.14.4	Approval number:

2.15	Pressure relief device (temperature triggered):  yes/ same component as used in propulsion system 1/

2.15.1	Make(s):

2.15.2	Type(s):

2.15.3	Service Temperature: 2/		°C

2.15.4	Approval number:

2.15.5	Working Pressure(s): 2/		MPa

2.16	Pressure relief device (pressure triggered): yes/no/same component as used in propulsion system 1/

2.16.1	Make(s):

2.16.2	Type(s):

2.16.3	Working Pressure(s) 2/:		MPa

2.16.4	Approval number:

2.17	Refuelling connection or receptacle: yes/ same component as used in propulsion system 1/

2.17.1	Make(s):

2.17.2	Type(s):

2.17.4	Working Pressure(s) 2/:		MPa

2.17.4	Approval number:

3	Further documentation:

3.1	Process diagram (flow chart) for the hydrogen system

3.2	System lay-out including electrical connections, and other external system inputs or outputs, etc.

3.3	Key to symbols used in documentation:

3.4	Adjustment data:

  - Cooling/ heating system(s) including Working Pressures and Service Temperatures

3.6	Drawings showing requirements for installation and operation.

Notes:

1/  Strike out what does not apply.

2/  Specify the tolerance.

Annex 3

ARRANGEMENT OF THE SPECIFIC COMPONENT APPROVAL MARKS

(See Paragraph 5.4 of this Regulation)

Where:  a ( 8 mm

The above approval mark affixed to the Hydrogen Component shows that this component has been approved in Germany (E1), pursuant to the Regulation No. xx under approval number 002439. The first two digits of the approval number indicate that the approval was granted in accordance with the requirements of Regulation No. xx in its original form.

Annex 4

COMMUNICATION CONCERNING THE APPROVAL, OR REFUSAL, OR EXTENSION,

OR WITHDRAWAL, OR PRODUCTION DEFINITELY DISCONTINUED

OF A SPECIFIC COMPONENT PURSUANT TO REGULATION NO. XX

(Maximum format:  A4 (210 x 297 mm)

Issued by: 				Name of administration:

Concerning:	2

APPROVAL GRANTED

APPROVAL EXTENDED

APPROVAL REFUSED

APPROVAL WITHDRAWN

PRODUCTION DEFINITELY DISCONTINUED

of a type of Specific Component pursuant to Regulation No. xx

Approval No.: ...................................			Extension No.: ................…………

| 1. | Specific Component considered: |
| --- | --- |
|  | Automatic valve 2/ |
|  | Check valve or non-return valve 2/ |
|  | Container 2/ |
|  | Excess flow system 2/ |
|  | Fitting or screwed connection system 2/ |
|  | Flexible fuel line 2/ |
|  | Flow Sensor |
|  | Heat exchanger 2/ |
|  | Hydrogen Filter |
|  | Hydrogen Sensor |
|  | Manual valve 2/ |
|  | Pressure sensor 2/ |
|  | Temperature sensor 2/ |
|  | Flow sensor 2/ |
|  | Pressure or hydrogen remaining indicator |
|  | Pressure regulator 2/ |
|  | Pressure relief device (temperature triggered) 2/ |
|  | Pressure relief device (pressure triggered) 2/ |
|  | Refuelling connection or receptacle 2/ |

| 2. | Trade name or mark: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| --- | --- |
| 3. | Manufacturer's name and address: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 4. | If applicable, name and address of manufacturer's representative . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 5. | Submitted for approval on: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 6. | Technical service responsible for conducting approval tests: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 7. | Date of report issued by that service: . . . . . . . . . . . . . . . . . . . . . . . . . |
| 8. | No. of report issued by that service: . . . . . . . . . . . . . . . . . . . . . . . . . |
| 9. | Approval granted/refused/extended/withdrawn 2/ |
| 10. | Reason(s) of extension (if applicable): . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 11. | Place: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 12. | Date: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 13. | Signature: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 14. | The documents filed with the application or extension of approval can be obtained upon request. |

____________

1/	Distinguishing number of the country which has granted/extended/refused/withdrawn
approval (see approval provisions in the Regulation).

2/	Strike out what does not apply

Annex 5

ARRANGEMENTS OF APPROVAL MARKS FOR A VEHICLE TYPE WITH REGARD TO

THE INSTALLATION OF A HYDROGEN SYSTEM

Model A

(See Paragraph 13.4 of this Regulation)

Where:  a ( 8 mm

The above approval mark affixed to a vehicle shows that the vehicle has, with regard to the installation of a Hydrogen System for the use of compressed gaseous hydrogen, has been approved in Germany (E1), pursuant to the Regulation No. xx under approval number 002439. The first two digits of the approval number indicate that the approval was granted in accordance with the requirements of Regulation No. xx in its original form.

Model B

(See Paragraph 13.4 of this Regulation)

Where:  a ( 8 mm

The above approval mark affixed to a vehicle shows that the vehicle has been approved in Germany (E1), pursuant to the Regulation Nos. xx and 83. The approval numbers indicate that, at the dates when the respective approvals were given, Regulation No. xx was in its original form and Regulation No. 83 included the 02 series of amendments

Annex 6

COMMUNICATION CONCERNING THE APPROVAL, OR REFUSAL, OR EXTENSION, OR WITHDRAWAL, OR PRODUCTION DEFINITELY DISCONTINUED OF A VEHICLE TYPE WITH REGARD TO THE INSTALLATION OF A HYDROGEN SYSTEM PURSUANT TO REGULATION NO. XX

(Maximum format:  A4 (210 x 297 mm)

Issued by:				Name of administration:

Concerning:	2

APPROVAL GRANTED

APPROVAL EXTENDED

APPROVAL REFUSED

APPROVAL WITHDRAWN

PRODUCTION DEFINITELY DISCONTINUED

of a Vehicle Type with regard to the installation of a Hydrogen System pursuant to Regulation No. xx

Approval No.: ................................………...		Extension No.: ...............……………….….

| 1. | Trade name or mark of vehicle: . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| --- | --- |
| 2. | Vehicle type: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 3. | Vehicle category: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 4. | Manufacturer's name and address: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 5. | If applicable, name and address of manufacturer's representative: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 6. | Description of the vehicle with regard to the installation of Hydrogen System (add drawing if appropriate) . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 7. | Hydrogen System |
| 7.1 | Trade name or mark of components and their approval numbers: |
| 7.1.1 | Container: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 7.1.2 | Other components: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |

| 8. | Submitted for approval on: . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| --- | --- |
| 9. | Technical service responsible for conducting approval tests . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 10. | Date of report issued by that service . . . . . . . . . . . . . . . . . . . . . . . . . |
| 11. | No. of report issued by that service . . . . . . . . . . . . . . . . . . . . . . . . . |
| 12. | Approval granted/refused/extended/withdrawn 2/ |
| 13. | Reason(s) of extension (if applicable) . . . . . . . . . . . . . . . . . . . . . . . . |
| 14. | Place . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 15. | Date . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 16. | Signature . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . |
| 17. | The documents filed with the application or extension of approval can be obtained upon request. |

Drawings, diagrams and scheme plans regarding the components and the installation of the Hydrogen System considered to be of importance for the purpose of this Regulation:

.  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .

.  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .

Where applicable drawings of the various equipment and their position in the vehicle:

.  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .

.  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .  .

____________

1/	Distinguishing number of the country which has granted/extended/refused/withdrawn approval (see approval provisions in this Regulation).

2/	Strike out what does not apply

Annex 7

REQUIREMENTS AND APPROVAL TEST PROCEDURES

FOR CONTAINERS

Contents										Page

1	Scope

2	References

3	Service conditions

4	Design Approval

5	General Requirements Applicable To Container Types 1 To 4

6	Type 1 (Metal) Containers

7	Type (Hoop-wrapped) Containers

8	Type 3 (Fully-wrapped) Containers

9	Type 4 (All-composite) Containers

10	Markings

11	Preparation For Dispatch

Annexes

A	Test Methods

B	Report Forms (Informative)

C	Verification Of Stress Ratios Using Strain Gauges (Informative)

D	Fracture Performance Methods (Informative)

E	Container Manufacturer’s Instructions For Handling, Use And Inspection Of Containers (Informative)

F	Environmental Test (Informative)

G	Ultrasonic Inspection

1.	SCOPE

This Annex specifies minimum requirements for serially produced light-weight refillable compressed gaseous hydrogen Containers. The Containers are intended only for the on-board storage of high pressure compressed hydrogen gas as a fuel for automotive vehicles to which the containers are to be fixed. The service conditions do not include external loadings which may arise from vehicle collisions, or integration of the Container into the vehicle etc. Containers may be of any steel, aluminium or non-metallic material, design or method of manufacture suitable for the specified service conditions. Containers covered by this Annex are designated as follows:

Type 1 (Metal)		All metal construction.

Type 2 (Hoop Wrapped)	Metal Liner reinforced with resin impregnated continuous filament wrapped in discrete circumferential bands.

Type 3 (Fully Wrapped)	Metal Liner reinforced with resin impregnated continuous filament fully wrapped around the Liner.

Type 4 (Non-metallic)	Resin impregnated continuous filament with a non-metallic Liner.

Type 5 (Other)	Containers specified in Paragraph 2.2 of this Regulation in which the type and method of construction, including Containers of welded construction, is not covered by Types 1 to 4 above, shall be designed, constructed and tested in accordance with the requirements of the Competent Authority.

2	REFERENCES

The following standards contain provisions which, through reference in this text, constitute provisions of this Annex:

American Society for Testing and Materials (ASTM) Standards

ASTM B117-97	Standard Practice For Operating Salt Spray (Fog) Apparatus

ASTM B154-95	Standard Test Method For Mercurous Nitrate Test for Copper and Copper Alloys

ASTM D522-93a	Standard Test Method For Mandrel Bend Test Of Attached Organic Coatings

ASTM D2344-84(1995)Standard Test Method For Apparent Interlaminar Shear Strength of Parallel Fibre Composites By Short Beam Method

ASTM D2794-93	Standard Test Method For Resistance of Organic Coatings For The Effects of Rapid Deformation (Impact)

ASTM D3170-		Standard Test Method For Chipping Resistance Of Coatings

87(1996)e1

ASTM D3359-99	Standard Test Method For Measuring Adhesion By Tape Test

ASTM D3418-99	Standard Test Method For Transition Temperatures Of Polymers by Differential Scanning Calorimetry

ASTM E399-90(1997)Standard Test Method For Plain-strain Fracture Toughness Of Metallic Materials

ASTM E647-99	Standard Test Method For Measurement Of Fatigue Crack Growth Rates

ASTM G53-96	Standard Practice for Operating Light and Water Exposure Apparatus (Fluorescent UV-Condensation Type) For Exposure Of Non-metallic Materials

British Standards Institution (BSI) Standards

BS 7448:1 1991	Fracture Mechanics Toughness Tests: Part I - Method For Determination Of KIC, Critical CTOD And Critical J Values Of Metallic Materials (Partially replaced)

BS PD 6493: 1991	Guidance On Methods For Assessing The Acceptability Of Flaws In Fusion Welded Structures

CEN: European Committee For Standards

EN 50054: 1998	Electrical Apparatus For The Detection And Measurement Of Combustible Gases – General Requirements And Test Methods

EN 50057: 1998	Electrical Apparatus For The Detection And Measurement Of Combustible Gases – Performance Requirements For Group II Apparatus Indicating Up To 100% Lower Explosive Limit

EN 50058: 1998	Electrical Apparatus For The Detection And Measurement Of Combustible Gases – Performance Requirements For Group II Apparatus Indicating Up To 100% (v/v) Gas

International Organisation for Standardisation (ISO) Standards

ISO 148: 1983	Steel - Charpy Impact Test (V-notch)

ISO 306: 1994	Plastics - Thermoplastic Materials - Determination Of Vicat Softening Temperature

ISO 642: 1999	Steel - Hardenability Test By End Quenching (Jominy Test)

ISO 2808: 1997	Paints And Varnishes - Determination Of Film Thickness

ISO 527: Pt.1: 1993	Plastics - Determination of Tensile Properties

ISO 4624: 1978	Plastics And Varnishes - Pull-off Test For adhesion

ISO 6892: 1998	Metallic Materials - Tensile Testing At Ambient Temperature

ISO 6506:1 1999	Metallic Materials - Brinell Hardness Test - Part1: Test Method

ISO AWI 7225 Ed.2	Gas Cylinders - Precautionary Labels

ISO 7866: 1999	Gas Cylinders - Refillable Seamless Aluminium Alloy Gas Cylinders: Design, Construction And Testing

ISO 9001:1994	Quality Systems - Model For Quality Assurance In Design, Development, Production, Installation and Servicing

ISO 9002:1994	Quality Systems - Model For Quality Assurance In Design, Development, Production, Installation and Servicing

ISO 9712:1999	Non-destructive Testing - Qualification And Certification Of Personnel

ISO 9809-1: 1999	Gas Cylinders - Refillable Seamless Steel Gas Cylinders - Design, Construction And Testing - Part I: Quenched And Tempered Steel Cylinders With Tensile Strength < 1100 MPa

ISO 12737: 1996	Metallic Materials - Determination Of The Plane-strain Fracture Toughness

ISO 11114-1 (7/98)	Transportable Gas Cylinders – Compatibility Of Cylinder And Valve Materials With Gas Contents – Part 1: Metallic Materials

PrEN ISO 11114-2 (02/99)	Transportable Gas Cylinders – Compatibility Of Cylinder And Valve Materials With Gas Contents – Part 2: Non-metallic Materials

PrEN ISO 11114-4 (??/??)	Transportable Gas Cylinders – Compatibility Of Cylinder And Valve Materials With Gas Contents – Part 4: Test

3	SERVICE CONDITIONS

Unless indicated otherwise the service conditions specified in Paragraph 2.4 of this Regulation will apply throughout this Annex.

3.1	Design Number Of Refilling Cycles

Containers shall be designed to be refilled 1 000 times per year of service up to a Settled Pressure equal to their Working Pressure at a Settled Temperature of 15 °C.

3.2	Temperatures

See Paragraph 2.4.6 of this Regulation.

3.3	Refilling

For information: Transient temperatures due to the effects of refilling the Container shall not result in gas temperatures exceeding +850C.

3.4	External Surfaces

Containers need not be designed for continuous exposure to mechanical or chemical attack, e.g. leakage from cargo that may be carried on vehicles or severe abrasion damage from road conditions.

3.5	Gas Permeation Or Leakage

Permeation of gas through the wall of the Container or between the Liner and the wrapping, or leakage between the end connections and the liner, shall be considered in the design of Containers.

4.	DESIGN APPROVAL

4.1	General

Application for approval and approval of a Container shall be carried out in accordance with Part I of this Regulation, however, this Paragraph contains additional requirements for Containers that shall be satisfied before approval may be granted.

The following information shall be submitted by the Container Manufacturer with a request for approval to the Competent Authority:

- Statement of service (see Paragraph 4.2 of this Annex),

- Design data (see Paragraph 4.3 of this Annex),

- Manufacturing data (see Paragraph 4.4 of this Annex),

- Fracture performance and NDE (Non Destructive Examination) defect size (see Paragraph 4.5 of this Annex),

- Specification sheet (see Paragraph 4.6 of this Annex),

- Additional supporting data (see Paragraph 4.7 of this Annex).

- Quality system (see Paragraph 4.8 of this Annex),

4.2	Statement Of Service

The statement of service shall include:

- A statement that the Container design is suitable for use in the service conditions defined in Paragraph 3 of this Annex for the Service Life of the Container shall be provided,

- The Service Life shall be specified,

- The minimum in-service test or inspection requirements shall be specified,

- The pressure relief devices or insulation required shall be specified,

- Support methods, protective coatings, etc., required but not provided shall be specified,

- A description of the Container design shall be provided,

- Any other information necessary to ensure the safe use and inspection of the Container.

4.3	Design Data

4.3.1.	Drawings

Drawings shall show the following information as a minimum:

- Title, reference number, date of issue, and revision numbers with dates of issue if applicable,

- Reference to this Regulation and the Container Type,

- All dimensions complete with tolerances, including details of end closure shapes with minimum thickness and of openings,

- Mass including tolerance of the Container,

- Material specifications, complete with minimum mechanical and chemical properties or tolerance ranges and the specified hardness range,

- Other data such as, Auto-frettage Pressure range, minimum Test Pressure, details of the fire protection system and of the exterior protective coating.

4.3.2	Stress Analysis Report

A finite element stress analysis or other stress analysis shall be provided, including a table summarising the calculated stresses in the report, unless the Container is designed in accordance with ISO 9809.

4.3.3	Material Test Data

A detailed description of the materials and tolerances of the materials properties used in the design shall be provided. Test data shall also be presented characterising the mechanical properties and the suitability of the materials for service under the service conditions specified in Paragraph 3 of this Annex.

4.3.4	Design Qualification Test Data

The Container material, design, manufacture and examination shall be deemed to be adequate for their intended service by meeting the requirements of the tests required for the particular Container design, when tested in accordance with the relevant methods of test detailed in this Annex. The test data shall also document the dimensions, wall thickness and weights of each of the test Containers.

4.3.5	Fire Protection

The arrangement of Pressure Relief Device(s) that will protect the Container from sudden rupture when exposed to the fire conditions specified in Paragraph A.15 (Appendix A of this Annex) shall be specified. Test data shall substantiate the effectiveness of the arrangement of Pressure Relief Device(s).

4.3.6	Container Supports

Details of Container supports or support requirements shall be provided in accordance with Paragraph 5.11 of this Annex.

4.4	Manufacturing Data

Details of all fabrication processes, non-destructive examinations, production tests and batch tests shall be provided. The tolerances for all production processes such as heat treatment, end forming, resin mix ratio, filament winding tension and speed, curing times and temperatures, and Auto-frettage procedures shall be specified. Surface finish, thread details, acceptance criteria for ultrasonic scanning (or equivalent), and maximum lot sizes for batch tests shall also be specified.

4.5	Fracture Performance And Non-destructive Examination (NDE) Defect Size

4.5.1	Fracture performance

The manufacturer shall demonstrate the Leak-Before-Break performance of the design as described in Paragraph 5.7 of this Annex.

4.5.2	NDE Defect Size

Using the approach described in Paragraph 5.15.2 of this Annex, the Manufacturer shall establish the maximum defect size for non-destructive examination which will prevent the failure of the Container during its Service Life due to fatigue, or failure of the Container by rupture.

4.6	Specification Sheet

A summary of the documents providing the information required in Paragraph 4.1 of this Annex shall be listed on a specification sheet for each Container design. The title, reference number, revision numbers and dates of original issue and version issues of each document shall be given. All documents shall be signed or initialled by the issuer. The specification sheet shall be given a number, and revision numbers if applicable, that can be used to designate the Container design and shall carry the signature of the engineer responsible for the design. Space shall be provided on the specification sheet for a stamp indicating registration of the design.

4.7	Additional Supporting Data

Additional data which supports the application for approval, such as the service history of material proposed for use, or the use of a particular Container design in other service conditions, shall be provided where applicable.

4.8	Quality Assurance Programme

The Manufacturer shall specify methods and procedures in accordance with ISO 9001 and ISO 9002.

4.9	Approval And Certification

4.9.1	Inspection And Testing

Evaluation of conformity is required to be performed in accordance with the provisions of Part I, Paragraph 8 of this Regulation.

In order to ensure that the Containers are in compliance with this Regulation they shall be subject to inspection performed by the Competent Authority in accordance with Paragraphs 5.13, 5.14 and 5.15 of this Annex.

4.9.2	Test Certificate

If the results of prototype testing according to Paragraph 5.13 of this Annex are satisfactory, the Competent Authority shall issue a test certificate. An example of a test certificate is given in Appendix B to this annex.

5	GENERAL REQUIREMENTS APPLICABLE TO CONTAINER TYPES 1 TO 4

5.1	General

The following requirements are generally applicable to Container Types 1 to 4. Type specific requirements are specified in Paragraphs 6 to 9 of this Annex and shall take precedence over the requirements of this Paragraph. The design of cylinders shall cover all relevant aspects which are necessary to ensure that every cylinder produced to the design is fit for its purpose throughout its specified Service Life.

5.2	Design

This Regulation does not provide design formulas nor permissible stresses or strains, but requires the adequacy of the design to be established by appropriate calculations and demonstrated by Containers being capable of consistently passing the materials, design qualification, production and batch tests specified in this Regulation.

All designs shall ensure a "leakage before break" failure mode under feasible degradation of pressure parts during normal service. If failure of the Container occurs, it shall be only by the growth of a fatigue crack. The design shall identify the maximum size of an allowable defect at any point of a Container operating at the Working Pressure, which will not grow to a critical size within the specified retest period or Service Life if no retest is specified.

5.3	Materials

5.3.1	General

Materials used shall be suitable for the service conditions specified in Paragraph 3 of this Annex. Incompatible materials shall not be in contact with each other. The component materials which are in contact with hydrogen shall be compatible with hydrogen and expected additives and production contaminants, in accordance with EN11114-1 and prEN11114-2. Hydrogen compatibility of Container materials shall be determined in accordance with Paragraph A.28 (Appendix A of this Annex). The design qualification tests for materials are summarised in Table 7.2.

5.3.2	Steel

5.3.2.1	Composition

Steels shall be produced to predominantly fine grain practice. The chemical composition of all steels shall be declared and defined at least by:

- Carbon and manganese, contents in all cases,

- Nickel, chromium, molybdenum, boron and vanadium contents, and any other alloying elements intentionally added.

The following limits shall not be exceeded in the cast analysis:

| Tensile Strength | <950 MPa | (950 MPa |
| --- | --- | --- |
| Sulphur content | 0,020% | 0.010% |
| Phosphorus content | 0,020% | 0.020% |
| Sulphur and phosphorus content | 0,030% | 0.025% |

5.3.2.2	Tensile Properties

The mechanical properties of the steel in the finished Container or Liner shall be determined in accordance with Paragraph A.1 (Appendix A of this Annex). The elongation for steel shall be at least 14 %.

5.3.2.3	Impact Properties

The impact properties of the steel in the finished Container or Liner shall be determined in accordance with Paragraph A.2 (Appendix A of this Annex). Impact values shall not be less than that indicated in Table 7.3 of this Annex.

5.3.3.	Aluminium

5.3.3.1	Composition

Aluminium alloys shall be quoted in line with Aluminium Association practice for a given alloy system. The impurity limits for lead and bismuth in any aluminium alloy shall not exceed 0.003 %.

5.3.3.2	Corrosion Tests

Aluminium alloys shall meet the requirements of the corrosion tests carried out in accordance with Paragraph A.4 (Appendix A of this Annex).

5.3.3.3	Sustained Load Cracking

Aluminium alloys shall meet the requirements of the sustained load cracking tests carried out in accordance with Paragraph A.5 (Appendix A of this Annex).

5.3.3.4	Tensile Properties

The mechanical properties of the aluminium alloy in the finished Container or Liner shall be determined in accordance with Paragraph A.1 (Appendix A of this Annex). The elongation for aluminium shall be at least 12%.

5.3.4	Resins

5.3.4.1	General

The material for impregnation may be thermosetting or thermoplastic resins. Examples of suitable matrix materials are epoxy, modified epoxy, polyester and vinylester thermosetting plastics, and polyethylene and polyamide thermoplastic material.

5.3.4.2	Shear Strength

Resin materials shall be tested in accordance with Paragraph A.26 (Appendix A of this Annex) and meet the requirements therein.

5.3.4.3	Glass Transition Temperature

The glass transition temperature of the resin material shall be determined in accordance with ASTM D3418.

5.3.5	Fibres

Structural reinforcing filament material types shall be glass fibre, aramid fibre or carbon fibre. If carbon fibre reinforcement is used, the design shall incorporate means to prevent galvanic corrosion of metallic components of the cylinder. The manufacturer shall keep on file the published specifications for composite materials, the material manufacturer's recommendations for storage, conditions and shelf life and the material manufacturer's certification that each shipment conforms to the aforesaid specification requirements. The fibre manufacturer shall certify that the fibre material properties conform to the manufacturer's specifications for the product.

5.3.6	Plastic Liners

The tensile yield strength and ultimate elongation shall be determined in accordance with Paragraph A.22 (Appendix A of this Annex). Tests shall demonstrate the ductile properties of the plastic liner material at temperatures of -50 °C or lower by meeting the values specified by the manufacturer. The polymeric material shall be compatible with the service conditions specified in Paragraph 3 of this Annex. In accordance with the method described in Paragraph A.23 (Appendix A of this Annex), the softening temperature shall be the greater of 130 °C or the functioning temperature of the temperature triggered pressure relief device plus 10 °C, and the melting temperature shall be the greater of 160 °C or the functioning temperature of the temperature triggered pressure relief device plus 30 °C.

5.4	Test Pressure

The minimum Test Pressure used shall be 1.5 x Working Pressure.

5.5	Burst Pressures And Fibre Stress Ratios

For all types of cylinder the minimum actual burst pressure ratio shall not be less than the values given in Table 7.4 of this Annex. For Type 2, 3 and 4 Containers the composite over-wrap shall be designed for high reliability under sustained loading and cyclic loading. This reliability shall be achieved by meeting or exceeding the composite reinforcement stress ratio values given in Table 7.4 of this Annex. Stress ratio is defined as the stress in the fibre at the specified minimum burst pressure divided by the stress in the fibre at Design Pressure. The burst pressure ratio is defined as the actual burst pressure of the cylinder divided by the Design Pressure. For Type 4 Containers, the stress ratio is equal to the burst pressure ratio. For Type 2 and 3 Containers stress ratio calculations must include:

- An analysis method with capability for non-linear materials (special purpose computer program or finite element analysis program).

- Elastic-plastic stress-strain curve for liner material must be known and correctly modelled.

- Mechanical properties of composite materials must be correctly modelled.

- Calculations must be made at: Auto-frettage, zero after Auto-frettage, working and minimum burst pressures.

- Prestress from winding tension must be accounted for in the analysis.

- Minimum burst pressure must be chosen such that the calculated stress at minimum burst pressure divided by the calculated stress at the Working Pressure meets the stress ratio requirements for the fibre used.

- When analysing cylinders with hybrid reinforcement (two or more different fibres), the load share between the different fibres must be considered based on the different elastic modulii of the fibres. The stress ratio requirements for each individual fibre type must be in accordance with the values given in Table 7.4 of this Annex. Verification of the stress ratios may also be performed using strain gauges. An acceptable method is outlined in Appendix C to this Annex.

5.6	Stress Analysis

A stress analysis shall be performed to justify the minimum design wall thicknesses. It shall include the determination of the stresses in Liners and fibres of composite designs.

5.7	Leak Before Break Assessment

Type 1, 2, 3 and 4 Containers shall demonstrate Leak Before Break (LBB) performance in accordance with the requirements of Paragraphs 6, 7, 8 and 9 of this Annex. Demonstration of LBB performance is not required for Container designs that provide a fatigue life of 45,000 pressure cycles or greater when tested in accordance with Paragraph A.13 (Appendix A of this Annex). Two methods of LBB assessment are included for information in Appendix D of this Annex.

5.8	Inspection And Testing

The manufacturing inspection shall specify programmes and procedures for:

- Manufacturing inspection, tests and acceptance criteria, and,

- Periodic in-service inspection, tests and acceptance criteria. The interval of visual re-inspection of the external Container surfaces shall be in accordance with Part II, Paragraph 14.10 of this Regulation unless varied by the Competent Authority. The Manufacturer shall establish the visual re-inspection rejection criteria based on the results of pressure cycling tests performed on Containers containing flaws. A guide for Manufacturer's instructions for handling, use and inspection is provided in Appendix E to this Annex.

5.9	Fire Protection

All Containers shall be protected from fire with temperature triggered Pressure Relief Devices. The Container, its materials, Pressure Relief Devices and any added insulation or protective material shall be designed collectively to ensure adequate safety during fire conditions in the test specified in Paragraph A.15 (Appendix A to this Annex).

Pressure relief devices shall be tested in accordance Annex 8A and Annex 9 to this Regulation.

5.10	Openings

5.10.1	General

Openings are permitted in Container heads only. The centre line of openings shall coincide with the longitudinal axis of the Container. Threads shall be clean cut, even, without surface discontinuities, and to gauge.

5.10.2	Tapered Threads

Openings with tapered threads may be used in all Containers Types. Tapered threads shall comply with a recognised international or national standard.

5.10.3	Straight Threads

Openings with straight threads shall comply with a recognised international or national standard. The thread shear stress at Container Test Pressure calculated using the equations given below shall not exceed one quarter of the ultimate shear stress of the threaded material.

A = p.n.L.d.[1/(2n) ¸ (d-D)/3]		Eqn.(1)

T = P.p.(b/2)²/10			Eqn.(2)

S = T/A				Eqn.(3)

where:

A = shear area of internal thread, mm2

n = number of threads per mm

d = minimum major diameter of external thread, mm

D = maximum pitch diameter of internal thread, mm

L = length of thread engagement, mm

P = hydrostatic Test Pressure, MPa

b = basic pitch diameter of external thread, mm

T = thrust force, N

S = average shear stress on internal thread, MPa

5.11	Container Supports

The Manufacturer shall specify the means by which Containers shall be supported for installation on vehicles. The manufacturer shall also supply support installation instructions, including clamping force and torque to provide the required restraining force but not cause unacceptable stress in the Container or damage to the Container surface.

5.12	Exterior Environmental Protection

The exterior of Containers shall meet the requirements of the environmental test conditions of Paragraph A.14 (Appendix A to this Annex). Exterior protection may be provided by using any of the following:

- A surface finish giving adequate protection (e.g. metal sprayed on aluminium, anodising); or

- The use of a suitable fibre and matrix material (e.g. carbon fibre in resin); or

- A protective coating (e.g. organic coating, paint) that shall meet the requirements of Paragraph A.9 (Appendix A to this Annex).

Any coatings applied to cylinders shall be such that the application process does not adversely affect the mechanical properties of the Container. The coating shall be designed to facilitate subsequent in service inspection and the manufacturer shall provide guidance on coating treatment during such inspection to ensure the continued integrity of the Container.

Manufacturers are advised that an environmental performance test that evaluates the suitability of coating systems is provided in the informative Appendix F to this Annex.

5.13	Design Qualification Tests

For the approval of each Container type the material, design, manufacture and examination shall be proved to be adequate for their intended service by meeting the appropriate requirements of the material qualification tests summarised in Table 7.2 of this Annex and the Container qualification tests summarised in Table 7.5 of this Annex, with all tests in accordance with the relevant methods of test as described in Appendix A to this Annex. The test Containers or Liners shall be selected and the tests witnessed by the Competent Authority. If more Containers or Liners are subjected to the tests than are required by this Annex, all results shall be documented.

5.14	Batch tests

The batch tests specified in this Annex for each Container type shall be conducted on Containers or Liners taken from each batch of Finished Containers or Liners. Heat treated witness samples shown to be representative of Finished Containers or Liners may also be used. Batch tests required for each Container Type are specified in Table 7.6 of this Annex.

In no case shall a Batch be permitted to exceed 200 Finished Containers or Liners (not including Containers or Liners used in destructive tests), or one shift of successive production, whichever is greater.

5.15	Production Examinations And Tests

5.15.1	General

Production examinations and tests shall be carried out on all Containers produced in a batch. Each Container shall be examined during manufacture and after completion by the following means:

- Ultrasonic scanning (or demonstrated equivalent) of metallic Containers and Liners in accordance with Appendix G to this Annex, or demonstrated equivalent method, to ensure that the maximum defect size present does not exceed the size specified in the design.

- Verification that the critical dimensions and mass of the completed Container and of any Liner and Over-wrapping are within design tolerances.

- Verification of compliance with specified surface finish with special attention to deep drawn surfaces and folds or laps in the neck or shoulder of forged or spun end enclosures or openings.

- Verification of markings.

- Hardness tests of metallic Containers and Liners in accordance with Paragraph A.8 (Appendix A to this Annex) shall be carried out after the final heat treatment and the values thus determined shall be in the range specified for the design.

- Hydrostatic proof test in accordance with Paragraph A.11 (Appendix A to this Annex).

A summary of critical production inspection requirements to be performed on each Container is provided in Table 7.7 of this Annex.

5.15.2	Maximum Defect Size

For Container Type 1, 2 and 3 designs, the maximum defect size at any location in the metal cylinder or metal liner that will not grow to a critical size within the specified Service Life shall be determined. The critical defect size is defined as the limiting through-wall (Container or Liner) thickness defect that would allow stored gas to be discharged without rupturing the Container. Defect sizes for the rejection criteria for ultrasonic scanning, or equivalent shall be smaller than the maximum allowable defect sizes. For Container Type 2 and 3 designs, it shall be assumed that there is no damage to non-metallic materials due to any time-dependent mechanisms. The allowable defect size for NDE shall be determined by an appropriate method. Two such methods are outlined in the informative Appendix D to this Annex.

5.16	Failure To Meet Test Requirements

In the event of failure to meet test requirements, retesting or reheat treatment and retesting shall be carried out as follows:

- If there is evidence of a fault in carrying out a test, or an error of measurement, a further test shall be performed. If the result of this test is satisfactory, the first test shall be ignored.

- If the test has been carried out in a satisfactory manner, the cause of test failure shall be identified.

If the failure is considered to be due to the heat treatment applied, the Manufacturer may subject all the Containers of the batch to a further heat treatment.

If the failure is not due to the heat treatment applied, all the identified defective Containers shall be rejected or repaired by an approved method. The unrejected Containers shall then be considered as a new batch.

In both cases the new batch shall be retested. All the relevant prototype or batch tests needed to prove the acceptability of the new batch shall be performed again. If one or more tests prove even partially unsatisfactory, all cylinders of the batch shall be rejected.

5.17	Change Of Design

A design change is any change in the selection of structural materials or dimensional change not attributable to normal manufacturing tolerances.

Minor design changes shall be permitted to be qualified through a reduced test program. Changes of design specified in Table 7.8 of this Annex shall require design qualification testing as specified in the Table.

Table 7.1 – Not used

Table 7.2 - Material Design Qualification Tests

|  | Relevant Paragraph Of This Annex |
| --- | --- |
|  | Steel | Aluminium | Resins | Fibres | Plastic liners |
| Tensile Properties | 5.3.2.2 | 5.3.3.4 |  | 5.3.5 | 5.3.6 |
| Impact Properties | 5.3.2.3 |  |  |  |  |
| Sustained Load Cracking Resistance |  | 5.3.3.3 |  |  |  |
| Stress Corrosion Cracking |  | 5.3.3.2 |  |  |  |
| Shear Strength |  |  | 5.3.4.2 |  |  |
| Glass Transition Temperature |  |  | 5.3.4.3 |  |  |
| Softening/Melting Temperature |  |  |  |  | 5.3.6 |
| Hydrogen compatibility | 5.3.1 | 5.3.1 | 5.3.1 | 5.3.1 | 5.3.1 |
| Fracture Mechanics * | 5.7 | 5.7 |  |  |  |
| * Not required if using flawed cylinder test approach in Paragraph A.17 (Appendix A to this Annex) |

Table 7.3 - Impact Test Acceptable Values

| Cylinder diameter D, mm | >140 | (140 |
| --- | --- | --- |
| Direction of testing | Transverse | Longitudinal |
| Width of test piece, mm | 3 - 5 | >5 - 7.5 | >7.5 - 10 | 3 to 5 |
| Test temperature, °C | -50 | -50 |
| Impact strength, J/cm² |  |  |  |  |
| Mean of 3 specimens | 30 | 35 | 40 | 60 |
| Individual specimen | 24 | 28 | 32 | 48 |

Table 7.4 - Minimum Burst And Stress Ratios

| Container Type | 1 All-metal | 2 Hoop-wrapped | 3 Fully-wrapped | 4 All-composite |
| --- | --- | --- | --- | --- |
| Over-wrapping | Burst pressure ratio | Stress ratio | Burst pressure ratio | Stress ratio | Burst pressure ratio | Stress ratio | Burst pressure ratio |
| All metal | 2.25 |  |  |  |  |  |  |
| Glass |  | 2.75 | 2.50 1) | 3.65 | 3.50 1) | 3.65 | 3.65 |
| Aramid |  | 2.35 | 2.35 | 3.10 | 3.00 1) | 3.1 | 3.10 |
| Carbon |  | 2.35 | 2.35 | 2.35 | 2.35 | 2.35 | 2.35 |
| Hybrid |  | 2) | 2) | 2) |
| Notes 1 - Minimum burst pressure ratio. In addition, calculations must be performed in accordance with Paragraph 5.5 of this Annex to confirm that the minimum stress ratio requirements are also met. 2 - Stress ratios and burst pressure ratios shall be calculated in accordance with Paragraph 5.5 of this Annex. |

Table 7.5 - Container Design Qualification Tests

|  | Container Type |
| --- | --- |
| Test And Annex Reference | 1 | 2 | 3 | 4 |
| A.6 | LBB Assessment | X | X | X | X |
| A.7 | Extreme temperature/cycle |  | X | X | X |
| A.12 | Burst | X | X | X | X |
| A.13 | Ambient temp/cycle | X | X | X | X |
| A.14 | Acid environment test |  | X | X | X |
| A.15 | Bonfire | X | X | X | X |
| A.16 | Penetration | X | X | X | X |
| A.17 | Flaw tolerance |  | X | X | X |
| A.18 | High temp. creep |  | X | X | X |
| A.19 | Stress rupture |  | X | X | X |
| A.20 | Drop test |  |  | X | X |
| A.21 | Permeation |  |  |  | X |
| A.25 | Boss torque test |  |  |  | X |
| A.27 | Hydrogen gas cycling |  |  |  | X |
| Notes: X = Test required |

Table 7.6 - Batch Tests

|  | Cylinder Type |
| --- | --- |
| Test And Annex Reference | 1 | 2 | 3 | 4 |
| A.1 | Tensile | X | X† | X† |  |
| A.2 | Impact (steel) | X | X† | X† |  |
| A.9.2 | Coating* | X | X | X | X |
| A.12 | Burst | X | X | X | X |
| A.13 | Ambient cycle | X | X | X | X |
| Notes: X = Test required * Except where no protective coating is used † Tests on liner material |

Table 7.7 - Critical Production Inspection Requirements

|  | Container Type |
| --- | --- |
| Inspection Requirement | 1 | 2 | 3 | 4 |
| Critical dimensions | X | X | X | X |
| Surface finish | X | X | X | X |
| Flaws (ultrasonic or equivalent) | X | X | X |  |
| Hardness of metal cylinders and metal liners | X | X | X |  |
| Hydrostatic proof test | X | X | X | X |
| Leak test | X | X | X | X |
| Markings | X | X | X | X |

Note:	X = Test required

|  | Type Of Test |
| --- | --- |
| Table 7.8 - Change Of Design Design Change | Materials A.1, A.2, A.4, & A.5 as applicable | LBB Assess-ment A.6 | Burst (Hydro-static) A.12 | Cycling (Ambient Temp.) A.13 | Acid Environ-mental A.14 | Bonfire A.15 | Penetra-tion A.16 | Flaw tolerance A.17 | Stress Rupture A.19 High. Temp. Creep A.18 | Impact test A.20 | Perm-eation A.21 Boss torque A.25 Hydrogen Cycling A.27 | PRD Perform. A.24 | Hydrogen Compati-bility A.28 |
| Fibre Manufacturer |  |  | 2, 3, 4 | 2, 3, 4 |  |  |  |  | 2, 3, 4 | 2, 3, 4 | 4 |  | 2, 3, 4 |
| Metallic Container Or Liner Material | 1, 2, 3 | 1, 2, 3 | 1, 2, 3 | 1, 2, 3 | 2, 3, 4 | 1, 2, 3 | 1, 2, 3 | 2, 3, 4 | 2, 3, 4 | 2, 3, 4 |  |  | 1, 2, 3 |
| Plastic Liner Material |  | 4 |  | 4 | 4 |  |  |  |  |  | 4 |  | 4 |
| Fibre Material |  |  | 2, 3, 4 | 2, 3, 4 | 2, 3, 4 | 2, 3, 4 | 2, 3, 4 | 2, 3, 4 | 2, 3, 4 | 2, 3, 4 | 4 |  | 2, 3, 4 |
| Resin Material |  |  | 2, 3, 4 |  | 2, 3, 4 |  | 2, 3, 4 | 2, 3, 4 | 2, 3, 4 | 3, 4 |  |  | 2, 3, 4 |
| Diameter Change (20% |  |  | 1, 2, 3, 4 | 1, 2, 3, 4 |  |  |  |  |  |  |  |  |  |
| Diameter Change >20% |  | 1, 2, 3, 4 | 1, 2, 3, 4 | 1, 2, 3, 4 |  | 1, 2, 3, 4 | 1, 2, 3, 4 | 2, 3, 4 |  | 3, 4 |  |  |  |
| Length Change ( 50% |  |  | 1, 2, 3, 4 |  |  | 1‡, 2‡, ‡3, 4‡ |  |  |  |  |  |  |  |
| Length Change> 50% |  |  | 1, 2, 3, 4 | 1, 2, 3, 4 |  | 1‡, 2‡, ‡3, 4‡ |  |  |  | 3, 4 |  |  |  |
| Working Pressure Change (20%@ |  |  | 1, 2, 3, 4 | 1, 2, 3, 4 |  |  |  |  |  |  |  |  |  |
| Dome Shape, Opening Size or Thread Size |  |  | 1, 2, 3, 4 | 1, 2, 3, 4 |  |  |  |  |  |  | 4 |  |  |
| Coating Change |  |  |  |  | 1, 2, 3, 4 |  |  |  |  |  |  |  |  |
| End Boss Design |  |  |  |  |  |  |  |  |  |  | 4 |  |  |
| Change In Manuf. Process |  |  | 1, 2, 3, 4 | 1, 2, 3, 4 |  |  |  |  |  |  |  |  |  |
| Pressure Relief Device |  |  |  |  |  | 1, 2, 3, 4 |  |  |  |  |  | 1, 2, 3, 4 |  |
| Notes: x = Test required, e.g. 2,3 means Test required for Container Types 2 and 3 only |
| ‡ Test only required when length increases |
| @ Only when thickness change proportional to diameter or pressure change |

6.	TYPE 1 (METAL) CONTAINERS

6.1	General

If the Container is of welded construction, it shall be designed, manufactured and tested in accordance with rules defined by the Approval Authorities and where applicable shall meet the additional requirements of this Regulation and its Annexes.

The design shall identify the maximum size of an allowable defect at any point in the Container which will not grow to a critical size within the specified retest period, or Service Life if no retest is specified, of a Container operating to the Working Pressure. Determination of leak-before-break (LBB) performance shall be carried out in accordance with the appropriate procedures defined in Paragraph A.6 (Appendix A to this Annex). Allowable defect size shall be determined in accordance with Paragraph 5.15.2 of this Annex.

6.2	Stress analysis

The stresses in the Container shall be calculated for

- 2.0 MPa,

- Working Pressure,

- Test Pressure,

- Design burst pressure.

The calculations shall use suitable analysis techniques using thin-shell theory that takes into account out-of-plane bending of the shell to establish stress distributions in the neck, transition regions and in the cylindrical part of the Container.

For Containers designed in accordance with ISO9809 a stress analysis report shall not be provided.

6.3	Manufacturing And Production Test Requirements

6.3.1	General

The ends of aluminium Containers shall not be closed by a forming process. The base ends of steel Containers which have been closed by forming, shall be NDE inspected or equivalent. Metal shall not be added in the process of closure at the end. Each Container shall be examined before end forming operations for thickness and surface finish.

After end forming, the Containers shall be heat treated to the hardness range specified for the design. Localised heat treatment is not permitted.

When a neck ring, foot ring or attachments for support are provided, it shall be of material compatible with that of the Container and shall be securely attached by a method other than welding, brazing or soldering.

6.3.2	Non-destructive Examination

The following tests shall be carried out on each metallic Container:

- Hardness test in accordance with Paragraph A.8 (Appendix A to this Annex),

- Ultrasonic examination, in accordance with Appendix G to this Annex, or demonstrated equivalent Non-destructive test (NDT) method, to ensure that the maximum defect size does not exceed the size specified in the design as determined in accordance with Paragraph 5.15.2 of this Annex.

6.3.3	Hydrostatic Pressure Testing

Each finished Container shall be hydrostatically pressure tested in accordance with Paragraph A.11 (Appendix A to this Annex).

6.4	Container Batch Tests

Batch testing shall be conducted on Finished Containers which are representative of normal production and are complete with identification marks. All results shall be documented. Two Containers shall be randomly selected from each batch upon which the following tests shall be carried out:

a)	Batch materials tests. One Container, or a heat treated witness sample representative of a finished Container, shall be subjected to the following tests:

- Critical dimensions checked against the design.

- One tensile test in accordance with Paragraph A.1 (Appendix A to this Annex) and meet the requirements of the design.

- For steel Containers, three impact tests in accordance with Paragraph A.2 (Appendix A to this Annex) and meet the requirements of Paragraph 5.3.2.3 of this Annex.

- When a protective coating is a part of the design, the coating shall be tested in accordance with Paragraph A.9.2 (Appendix A to this Annex).

All Containers represented by a batch test which fail to meet the specified requirements shall follow the procedures specified in Paragraph 5.16 of this Annex.

Where the coating fails to meet the requirements of Paragraph A.9.2 (Appendix A to this Annex), the batch shall be 100 percent inspected to remove similarly defective Containers. The coating on all defective Containers may be stripped and recoated. The coating batch test shall then be repeated.

b)	Batch burst test. One Container shall be hydrostatically pressurised to burst in accordance with Paragraph A.12 (Appendix A to this Annex).

If the burst pressure is less than the minimum calculated burst pressure the procedures specified in Paragraph 5.16 of this Annex shall be followed.

c)	Periodic pressure cycling test. Finished Containers shall be pressure cycled in accordance with Paragraph A.13 (Appendix A to this Annex) at a test frequency defined as follows:

- One Container from each batch shall be pressure cycled for a total of 1,000 times the specified Service Life in years, with a minimum 15,000 cycles.

- On 10 sequential production batches of a design family, i.e. similar materials and processes, should none of the pressure cycled Containers in i) above leak or rupture in less than 1,500 cycles times the specified life in years (minimum 22,500 cycles), then the pressure cycle test can be reduced to one Container from every 5 batches of production.

- On 10 sequential production batches of a design family, should none of the pressure cycled Containers in i) above leak or rupture in less than 2,000 cycles times the specified Service Life in years (minimum 30,000 cycles), then the pressure cycle test can be reduced to one Container from every 10 batches of production.

- Should more than 3 months have expired since the last batch of production, then a Container from the next batch of production shall be pressure cycle tested in order to maintain the reduced frequency of batch testing in ii) or iii) above.

- Should any reduced frequency pressure cycle test Container in ii) or iii) above fail to meet the required number of pressure cycles (minimum 22,500 or 30,000 pressure cycles respectively,) then it shall be necessary to repeat the batch pressure cycle test frequency in i) for a minimum 10 production batches in order to re-establish the reduced frequency of batch pressure cycle testing in ii) or iii) above.

- Should any Container in i), ii), or iii) above fail to meet the minimum cycle life requirement of 1 000 cycles times the specified Service Life in years (minimum 15000 cycles), then the cause of failure shall be determined and corrected following the procedures in Paragraph 5.16 of this Annex The pressure cycle test shall then be repeated on an additional three Containers from that batch. Should any of the three additional Containers fail to meet the minimum pressure cycling requirement of 1,000 cycles times the specified Service Life in years, then the batch shall be rejected.

6.5	Container Design Qualification Tests

6.5.1	General

Qualification testing shall be conducted on Finished Containers which are representative of normal production and complete with identification marks. Selection, witnessing and documentation of the results shall be in accordance with Paragraph 5.13 of this Annex.

6.5.2	Hydrostatic Pressure Burst Test

Three representative Containers shall be hydrostatically pressurised to failure in accordance with Paragraph A.12 (Appendix A to this Annex). The Container burst pressures shall exceed the minimum burst pressure calculated by the stress analysis for the design, and the burst pressure ratio shall be in accordance with Table 7.4 of this Annex.

6.5.3.	Ambient Temperature Pressure Cycling Test

Two Finished Containers shall be pressure cycled at ambient temperature in accordance with Paragraph A.13 (Appendix A to this Annex) to failure, or to a minimum of 45,000 cycles. The Containers shall not fail before reaching the specified Service Life in years times 1,000 cycles. Containers exceeding 1,000 cycles times the specified Service Life in years shall fail by leakage and not by rupture. Containers which do not fail within 45,000 cycles shall be destroyed either by continuing the cycling until failure occurs, or by hydrostatically pressurising to burst. Containers exceeding 45,000 cycles are permitted to fail by rupture. The number of cycles to failure and the location of the failure initiation shall be recorded.

6.5.4	Bonfire Test

Tests shall be conducted in accordance with Paragraph A.15 (Appendix A to this Annex) and meet the requirements therein.

6.5.5.	Penetration Test

Tests shall be conducted in accordance with Paragraph A.16 (Appendix A to this Annex) and meet the requirements therein.

6.5.6	LBB Performance

For Container designs not exceeding 45,000 cycles when tested in accordance with Paragraph 6.5.3 of this Annex, LBB performance tests shall be conducted in accordance with Paragraph A.6 (Appendix A to this Annex) and meet the requirements therein.

7.	TYPE 2 (HOOP WRAPPED) CONTAINERS

7.1	General

If the Liner is of welded construction, it shall be designed, manufactured and tested in accordance with rules defined by the Approval Authorities and where applicable shall meet the additional requirements of this Regulation and its Annexes.

During pressurisation, this type of Container design has a behaviour in which the displacements of the composite overwrap and the metal Liner are linearly superimposed. Due to different techniques of manufacture, this Annex does not give a specific method for design.

Determination of the leak-before-break (LBB) performance shall be in accordance with the appropriate procedures defined in Paragraph A.6 (Appendix A to this Annex). Allowable defect size shall be determined in accordance with Paragraph 5.15.2 of this Annex.

7.2	Design Requirements

7.2.1	Metal Liner

The metal Liner shall have a minimum burst pressure ratio of 1.30.

7.2.2	Composite Over-wrap

The tensile stress in the fibres shall meet the requirements of Paragraph 5.5 of this Annex.

7.2.3	Stress Analysis

The stresses in the Over-wrap and in the Liner after prestress shall be calculated. The pressures used for these calculations shall be zero, Working Pressure, Test Pressure and the design burst pressure. The calculations shall use suitable analysis techniques using thin-shell theory taking account of non-linear material behaviour of the Liner to establish stress distributions at the neck, transition regions and the cylindrical part of the Liner.

For designs using Auto-frettage to provide prestress, the limits within which the Auto-frettage Pressure must fall shall be calculated.

For designs using Controlled Tension Winding to provide prestress, the temperature at which it is performed, the tension required in each layer of the Over-wrap and the consequent prestress in the Liner shall be calculated.

7.3	Manufacturing Requirements

7.3.1	General

The Composite Container shall be fabricated from a Liner over-wrapped with continuous filament windings. Filament winding operations shall be computer or mechanically controlled. The filaments shall be applied under controlled tension during winding. After winding is complete, thermosetting resins shall be cured by heating, using a predetermined and controlled time-temperature profile.

7.3.2	Liner: The manufacture of a metallic Liner shall meet the requirements given under Paragraph 6.3 of this Annex for the appropriate type of Liner construction.

7.3.3	Over-wrap

The cylinders shall be fabricated in a filament winding machine. During winding the significant variables shall be monitored within specified tolerances, and documented in a winding record. These variables can include but are not limited to:

- Fibre type including sizing,

- Manner of impregnation,

- Winding tension,

- Winding speed,

- Number of windings,

- Band width,

- Type of resin and composition,

- Temperature of the resin,

- Temperature of the liner.

7.3.3.1	Curing Of Thermosetting Resins

If a thermosetting resin is used, the resin shall be cured after filament winding. During the curing, the curing cycle, i.e. the time-temperature history shall be documented.

The curing temperature shall be controlled and shall not affect the material properties of the Liner. The maximum curing temperature for Containers with aluminium Liners is 177 °C.

7.3.4.	Auto-frettage

Auto-frettage, if used, shall be carried out before the hydrostatic pressure test. The Auto-frettage Pressure shall be within the limits established in Paragraph 7.2.3 of this Annex, and the Manufacturer shall establish the method to verify the appropriate pressure.

7.4	Production Test Requirements

7.4.1	Non-destructive Examination

Non-destructive examinations (NDE) shall be carried out in accordance with a recognised ISO or an equivalent standard. The following tests shall be carried out on each metallic liner:

- Hardness test in accordance with Paragraph A.8 (Appendix A to this Annex);

- Ultrasonic examination, in accordance with Appendix G to this Annex, or demonstrated equivalent Non-destructive testing (NDT) method, to ensure that the maximum defect size does not exceed the size specified in the design.

7.4.2	Hydrostatic Pressure Testing

Each finished Container shall be hydrostatically pressure tested in accordance with Paragraph A.11 (Appendix A to this Annex). The Manufacturer shall define the appropriate limit of permanent volumetric expansion for the Test Pressure used, but in no case shall the permanent expansion exceed 5% of the total volumetric expansion at Test Pressure. Any cylinders not meeting the defined rejection limit shall be rejected and either destroyed or used for batch test purposes.

7.5	Container Batch Tests

7.5.1	General

Batch testing shall be conducted on Finished Containers which are representative of normal production and are complete with identification marks. Two Containers, or a Container and a Liner as appropriate, shall be randomly selected from each batch. If more Containers are subjected to the tests than are required by this Annex, all results shall be documented. The following tests shall be carried out as a minimum on these samples.

Where defects are detected in Over-wrapping before any Auto-frettage or hydrostatic pressure testing, the Over-wrapping may be completely removed and replaced.

a)	Batch materials tests.

One Container, or Liner, or heat treated witness sample that is representative of a finished Container, shall be subjected to the following tests:

- Dimensions checked against the design,

- One tensile test in accordance with Paragraph A.1 (Appendix A to this Annex) and meet the requirements of the design,

- For steel Liners, three impact tests in accordance with Paragraph A.2 (Appendix A to this Annex) and meet the requirements of the design,

- When a protective coating is a part of the design, the coating shall be tested in accordance with Paragraph A.9.2 (Appendix A to this Annex) and meet the requirements therein. All Containers or Liners represented by a batch test which fails to meet the requirements specified shall follow the procedures specified in Paragraph 6.16 of this Annex.

Where the coating fails to meet the requirements of Paragraph A.9.2 (Appendix A to this Annex), the batch shall be 100 per cent inspected to remove similarly defective Containers. The coating on all defective Containers may be stripped using a method that does not affect the integrity of the Over-wrapping, and recoated. The coating batch test shall then be repeated.

b)	Batch burst test.

One Container shall be tested in accordance with the requirements of Paragraph 6.4(b) of this Annex.

c)	Periodic pressure cycling test.

In accordance with the requirements of Paragraph 6.4(c) of this Annex.

7.6	Container Design Qualification Tests

7.6.1	General

Qualification testing shall be conducted on Containers which are representative of normal production and complete with identification marks. Selection, witnessing and documentation of the results shall comply with Paragraph 5.13 of this Annex.

7.6.2	Hydrostatic Pressure Burst Test

a)	One Liner shall be hydrostatically burst in accordance with Paragraph A.12 (Appendix A of this Annex). The burst pressure shall exceed the minimum burst pressure specified for the liner design.

b)	Three Containers shall be hydrostatically burst in accordance with Paragraph A.12 (Appendix A). Cylinder burst pressure ratios shall exceed the specified minimum burst pressure ratio established by the stress analysis for the design, in accordance with Table 7.4, and in no case be less than the value necessary to meet the stress ratio requirements of Paragraph 5.5 of this Annex.

7.6.3	Ambient Temperature Pressure Cycling Test

Two Finished Containers shall be pressure cycle tested at ambient temperature in accordance with Paragraph A.13 (Appendix A of this Annex) to failure, or to a minimum of 45,000 cycles. The Containers shall not fail before reaching the specified Service Life in years times 1,000 cycles. Containers exceeding 1000 cycles times the specified Service Life in years shall fail by leakage and not by rupture. Containers which do not fail within 45,000 cycles shall be destroyed either by continuing the cycling until failure occurs, or by hydrostatically pressurising to burst. Containers exceeding 45,000 cycles are permitted to fail by rupture. The number of cycles to failure and the location of the failure initiation shall be recorded.

7.6.4	Acid Environment Test

One Container shall be tested in accordance with Paragraph A.14 (Appendix A of this Annex) and meet the requirements therein. An optional environmental test is included in the informative Appendix H to this Annex.

7.6.5	Bonfire Test

Finished Containers shall be rested in accordance with Paragraph A.15 (Appendix A to this Annex) and meet the requirements therein.

7.6.6	Penetration Test

One finished Container shall be tested in accordance with Paragraph A.16 (Appendix A to this Annex) and meet the requirements therein.

7.6.7	Flaw Tolerance Tests

One finished Container shall be tested in accordance with Paragraph A.17 (Appendix A of this Annex) and meet the requirements therein.

7.6.8	High Temperature Creep Test

In designs where the glass transition temperature of the resin does not exceed the maximum design material temperature by at least 20°C, one Container shall be tested in accordance with Paragraph A.18 (Appendix A to this Annex) and meet the requirements therein.

7.6.9	Accelerated Stress Rupture Test

One finished Container shall be tested in accordance with Paragraph A.19 (Appendix A of this Annex) and meet the requirements therein.

7.6.10	LBB Performance

For Container designs not exceeding 45,000 cycles when tested in accordance with Paragraph 7.6.3 of this Annex, LBB performance tests shall be conducted in accordance with Paragraph A.6 (Appendix A of this Annex) and meet the requirements therein.

7.6.11	Extreme Temperature Pressure Cycling Test

One finished Container shall be tested in accordance with Paragraph A.7 (Appendix A of this Annex) and meet the requirements therein.

8.	TYPE 3 (FULLY-WRAPPED) CONTAINERS

8.1	General

If the Liner is of welded construction, it shall be designed, manufactured and tested in accordance with rules defined by the Approval Authorities and where applicable shall meet the additional requirements of this Regulation and its Annexes.

During pressurisation, this type of Container has a behaviour in which the displacements of the composite Over-wrap and the Liner are superimposed. Due to different techniques of manufacture, this Annex does not give a definite method for design. Determination of the leak-before-break (LBB) performance shall be in accordance with the appropriate procedures defined in Paragraph A.6 (Appendix A to this Annex). Allowable defect size shall be determined in accordance with Paragraph 5.15.2 above.

8.2	Design Requirements

8.2.1	Metal Liner

The compressive stress in the Liner at zero pressure and 15°C shall not cause the Liner to buckle or crease.

8.2.2	Composite Over-wrap

The tensile stress in the fibres shall meet the requirements of Paragraph 5.5 above.

8.2.3	Stress Analysis

The stresses in the tangential and longitudinal direction of the Container in the composite Over-wrap and in the Liner when subjected to internal pressure shall be calculated. The pressure used for these calculations shall be zero, Working Pressure, Test Pressure and design burst pressure. The limits within which auto-frettaging pressure must fall shall be calculated, The calculations shall use suitable analysis techniques using thin-shell theory taking account of non-linear material behaviour of the Liner to establish stress distributions at the neck, transition regions and the cylindrical part of the Liner.

8.3	Manufacturing Requirements

Manufacturing requirements shall be in accordance with Paragraph 7.3 of this Annex except that the Over-wrap shall also include helically wound filaments.

8.4	Production Test Requirements

Production test requirements shall be in accordance with the requirements of Paragraph 7.4 of this Annex.

8.5	Container Batch Tests

The batch tests shall be in accordance with the requirements of Paragraph 7.5 of this Annex.

8.6	Container Design Qualification Tests

8.6.1	Container design qualification tests shall be in accordance with the requirements of Paragraphs 7.6 and 8.6.2 of this Annex, except that the Liner burst in Paragraph 7.6.2 (a) of this Annex is not required.

8.6.2	Impact Test

One or more Finished Containers shall be drop tested in accordance with Paragraph A.20 (Appendix A to this Annex).

9.	TYPE 4 (ALL-COMPOSITE) CONTAINERS

9.1	General

This Annex does not give a definite method for the design of Containers with polymeric liners because of the variety of Container designs possible.

9.2	Design Requirements

Design calculations shall be used to provide justification of design adequacy. The tensile stresses in the fibres shall meet the requirements of Paragraph 5.5 of this Annex.

Tapered and straight threads in accordance with Paragraph 5.10.2 or 5.10.3 of this Annex shall be used on the metal end bosses.

Metal end bosses with threaded openings shall be able to withstand a torque force of 500 N-m, without damaging the integrity of the connection to the non-metallic Liner. The metal end bosses connected to the non-metallic Liner shall be of a material compatible with the service conditions specified in Paragraph 3 of this Annex.

9.3	Stress Analysis

The stresses in the tangential and longitudinal direction of the Container in the composite Over-wrap and in the Liner shall be calculated. The pressures used for these calculations shall be zero, Working Pressure, Test Pressure and design burst pressure. The calculations shall use suitable analysis techniques to establish stress distribution throughout the Container.

9.4	Manufacturing Requirements

Manufacturing requirements shall be in accordance with Paragraph 7.3 of this Annex except that the curing temperature for thermosetting resins shall be at least 10 °C below the softening temperature of the plastic Liner.

9.5	Production Test Requirements

9.5.1	Hydrostatic Pressure Testing

Each finished Container shall be hydrostatically pressure tested in accordance with Paragraph A.11 (Appendix A to this Annex). The Manufacturer shall define the appropriate limit of elastic expansion for the Test Pressure used, but in no case shall the elastic expansion of any Container exceed the average batch value by more than 10 per cent. Any Containers not meeting the defined rejection limit shall be rejected and either destroyed or used for batch test purposes.

9.5.2	Leak Testing

Each finished Container shall be leak tested in accordance with Paragraph A.10 (Appendix A to this Annex) and meet the requirements therein.

9.6	Container Batch Tests

9.6.1	General

Batch testing shall be conducted on Finished Containers which are representative of normal production and are complete with identification marks. One Container shall be randomly selected from each batch. If more Containers are subjected to the tests than are required by this Annex, all results shall be documented. The following tests shall be carried out as a minimum on these.

a)	Batch materials test

One Container, or Liner, or Liner witness sample that is representative of a finished Container, shall be subjected to the following tests:

- Dimensions checked against the design.

- One tensile test of the plastic Liner in accordance with Paragraph A.22 (Appendix A to this Annex) and meet the requirements of the design.

- The melt temperature of the plastic Liner shall be tested in accordance with Paragraph A.23 (Appendix A to this Annex), and meet the requirements of the design.

- When a protective coating is a part of the design, the coating shall be tested in accordance with Paragraph A.9.2 (Appendix A to this Annex). Where the coating fails to meet the requirements of Paragraph A.9.2 (Appendix A to this Annex), the batch shall be 100 per cent inspected to remove similarly defective Containers. The coating on all defective Containers may be stripped using a method that does not affect the integrity of the composite Over-wrapping, and recoated. The coating batch test shall then be repeated.

b)	Batch burst test

One Container shall be tested in accordance with the requirements of Paragraph 6.4(a) of this Annex.

c)	Periodic pressure cycling test

On one Container the end boss shall be torque tested to 500 Nm in accordance with the test method in Paragraph A.25 (Appendix A to this Annex). The Container shall then be pressure cycle tested in accordance with the procedures provided in Paragraph 6.4(c) of this Annex.

Following the required pressure cycling, the Container shall be leak tested in accordance with the method described in Paragraph A.10 (Appendix A to this Annex) and meet the requirements therein.

9.7	Container Design Qualification Tests

9.7.1	General

Container design qualification tests shall be in accordance with the requirements of Paragraphs 7.6, 9.7.2, 9.7.3 and 9.7.4 of this Annex.

9.7.2	Boss Torque Test

One Container shall be tested in accordance with Paragraph A.25 (Appendix A to this Annex).

9.7.3	Permeation Test

One Container shall be tested for permeation in accordance with Paragraph A.21 (Appendix A to this Annex) and meet the requirements therein.

9.7.4	Hydrogen Gas Cycling Test

One finished Container shall be tested in accordance with Paragraph A.27 (Appendix A to this Annex) and meet the requirements therein.

10.	MARKING

Markings on every Container shall be in accordance with Part I, Paragraph 4.3 of this Regulation.

11.	PREPARATION FOR DISPATCH

Prior to dispatch from the Manufacturers shop, every Container shall be internally cleaned and dried. Containers not immediately closed by the fitting of a valve, and Safety Devices if applicable, shall have plugs, which prevent entry of moisture and protect threads, fitted to all openings. A corrosion inhibitor, e.g. oil-containing, shall be sprayed into all steel Containers and liners prior to dispatch.

The Manufacturer's statement of service and all necessary information to ensure the proper handling, use and in-service inspection of the Container shall be supplied to the purchaser. The statement shall be in accordance with Appendix B to this Annex.

Annex 7 - APPENDIX A

TEST METHODS

A.1	TENSILE TESTS - STEEL AND ALUMINIUM

A tensile test shall be carried out on the material taken from the cylindrical part of the finished Container using a rectangular test piece shaped in accordance with the method described in ISO 9809 for steel and ISO 7866 for aluminium. The two faces of the test piece representing the inside and outside surface of the Container shall not be machined. The tensile test shall be carried out in accordance with ISO 6892.

NOTE - Attention is drawn to the method of measurement of elongation described in ISO 6892, particularly in cases where the tensile test piece is tapered, resulting in a point of fracture away from the middle of the gauge length.

A.2	IMPACT TEST, STEEL CONTAINERS AND STEEL LINERS

The impact test shall be carried out on the material taken from the cylindrical part of the finished Container on three test pieces in accordance with ISO 148. The impact test pieces shall be taken in the direction as required in Table 7.3 of Annex 7 from the wall of the Container. The notch shall be perpendicular to the face of the Container wall. For longitudinal tests the test piece shall be machined all over (on six faces), if the wall thickness does not permit a final test piece width of 10 mm, the width shall be as near as practicable to the nominal thickness of the Container wall. The test pieces taken in transverse direction shall be machined on four faces only, the inner and outer face of the Container wall shall not be machined.

A.3	Not used

A.4	CORROSION TESTS - ALUMINIUM

Corrosion tests for aluminium alloys shall be carried out in accordance with ISO 7866 Annex A and meet the requirements therein.

A.5	SUSTAINED LOAD CRACKING TESTS - ALUMINIUM

The resistance to sustained load cracking shall be carried out in accordance with ISO 7866 Annex D and shall meet the requirements therein.

A.6	LEAK-BEFORE-BREAK (LBB) PERFORMANCE TEST

Three Finished Containers shall be pressure cycled in accordance with the following procedure:

- Fill the Container to be tested with a non-corrosive fluid such as oil, inhibited water or glycol,

- Cycle the pressure in the Container between not more than 2.0 MPa and not less than 1.3 times Working Pressure at a rate not exceeding 10 cycles per minute.

The number of cycles to failure shall be reported, along with the location and description of the failure initiation.

The Containers tested shall fail by leakage and not by rupture.

A.7	EXTREME TEMPERATURE PRESSURE CYCLING

Finished Containers, with the composite wrapping free of any protective coating, shall be cycle tested without showing evidence of rupture, leakage, or fibre unravelling, as follows:

- Condition for 48 hours at zero pressure, 85 °C or higher, and 95 per cent or greater relative humidity. The intent of this requirement shall be deemed met by spraying with a fine spray or mist of water in a chamber held at 85 °C.

- Hydrostatically pressurised for 500 cycles times the specified Service Life in years between not more than 2.0 MPa and not less than 1.3 x Working Pressure at 85°C or higher and 95 per cent humidity.

- Stabilise at zero pressure and ambient temperature.

- Then pressurise from not more than 2.0 MPa to not less than 1.3 x Working Pressure for 500 cycles times the specified Service Life in years at the appropriate minimum temperature given in Paragraph 2.4.6 of this Regulation or lower.

- The pressure cycling rate of b) shall not exceed 10 cycles per minute. The pressure cycling rate of d) shall not exceed 3 cycles per minute unless a pressure transducer is installed directly within the Container. Adequate recording instrumentation shall be provided to ensure the minimum temperature of the fluid is maintained during the low temperature cycling.

Following pressure cycling at extreme temperatures, Containers shall be hydrostatically pressured to failure in accordance with the hydrostatic burst test requirements, and achieve a minimum burst pressure of 85 per cent of the minimum design burst pressure. For Container Type 4 designs, prior to the hydrostatic burst test the Container shall be leak tested in accordance with Paragraph A.10 of this Appendix.

A.8	BRINELL HARDNESS TEST

Hardness tests shall be carried out on the parallel wall at the centre and a domed end of each Container or Liner in accordance with ISO 6506. The test shall be carried out after the final heat treatment and the hardness values thus determined shall be in the range specified for the design.

A.9	COATING TESTS (Mandatory if Paragraph 5.12(iii) of Annex 7 is used)

A.9.1	Coating Performance Tests

Coatings shall be evaluated using the following test methods, or using equivalent National Standards:

- Adhesion testing in accordance with ISO 4624 using Method A or B as applicable. The coating shall exhibit an adhesion rating of either 4A or 4B, as applicable.

- Flexibility in accordance with ASTM D522 Mandrel Bend Test of Attached Organic Coatings, using Test Method B with a 12.7 mm (0.5 in) mandrel at the specified thickness at -20°C. Samples for the flexibility test shall be prepared in accordance with the ASTM D522 standard. There shall not be any visually apparent cracks.

- Impact resistance in accordance with ASTM D2794 Test method for Resistance of Organic Coatings to the Effects of Rapid Deformation (Impact). The coating at room temperature shall pass a forward impact test of 18 J (160 in-lbs).

- Chemical resistance when tested in general accordance with ASTM D1308 Effect of Household Chemicals on Clear and Pigmented Organic Finishes. The tests shall be conducted using the Open Spot Test Method and 100 hour exposure to a 30 per cent sulphuric acid solution (battery acid with a specific gravity of 1.219) and 24 hour exposure to a polyalkalene glycol (e.g. brake fluid). There shall be no evidence of lifting, blistering or softening of the coating. The adhesion shall meet a rating of 3 when tested in accordance with ASTM D3359.

- Minimum 1,000 hours exposure in accordance with ASTM G53 Practice for Operating Light and Water Exposure Apparatus (Fluorescent W-Condensation Type) for Exposure of non-metallic Materials. There shall be no evidence of blistering, and adhesion shall meet a rating of 3 when tested in accordance with ISO 4624. The maximum gloss loss allowed is 20 per cent.

- Minimum 500 hours exposure in accordance with ASTM B117 Test Method of Salt Spray (Fog) Testing. Undercutting shall not exceed 3 mm at the scribe mark, there shall be no evidence of blistering, and adhesion shall meet a rating of 3 when tested in accordance with ASTM D3359.

- Resistance to chipping at room temperature using the ASTM D3170 Chipping Resistance of Coatings. The coating shall have a rating of 7A or better, and there shall not be any exposure of the substrate.

A.9.2	Coating Batch Tests

i)	Coating Thickness

The thickness of the coating shall meet the requirements of the design when tested in accordance with ISO 2808.

ii)	Coating Adhesion

The coating adhesion strength shall be measured in accordance with ISO 4624, and shall have a minimum rating of 4 when measured using either Test Method A or B, as appropriate.

A.10	LEAK TEST

Containers shall be leak tested using the following procedure (or an acceptable alternative):

- Containers shall be thoroughly dried and pressurised to Working Pressure with dry air or nitrogen containing at least 10% helium.

- If the total leakage measured exceeds 0.004 Ncm3/hr the Container shall be rejected

A.11	HYDRAULIC TEST

Any internal pressure applied after Auto-frettage and previous to the hydrostatic test shall not exceed 90 per cent of the hydrostatic Test Pressure

One of the following two options shall be used for the hydraulic test:

Option 1 - Volumetric Expansion Test

- The Container shall be hydrostatically tested to at least 1.5 times Working Pressure. In no case may the Test Pressure exceed the Auto-frettage Pressure.

- Pressure shall be maintained for 30 seconds and sufficiently longer to ensure complete expansion.. If the Test Pressure cannot be maintained due to failure of the test apparatus, it is permissible to repeat the test at a pressure increased by 0.7 MPa. Not more than 2 such repeat rests are permitted.

- The manufacturer shall define the appropriate limit of permanent volumetric expansion for the Test Pressure used, but in no case shall the permanent expansion exceed 5 per cent of the total volumetric expansion measured under the Test Pressure. Any Containers not meeting the defined rejection limit shall be rejected and either rendered unserviceable or used for batch test purposes.

Option 2- Proof Pressure Test

The hydrostatic pressure in the Container shall be increased gradually and regularly until the Test Pressure, at least 1.5 times Working Pressure, is reached. The Container Test Pressure shall be held for a sufficiently long period (at least 30 seconds) to ascertain that there is no tendency for the pressure to decrease and there are no leaks.

A.12	HYDROSTATIC PRESSURE BURST TEST

- The rate of pressurisation shall not exceed 1.4 MPa per second at pressures in excess of 80 per cent of the design burst pressure. If the rate of pressurisation at pressures in excess of 80 per cent of the design burst pressure exceeds 0.35 MPa/second, then either the Container must be placed schematically between the pressure source and the pressure measurement device, or there must be a 5 second hold at the minimum design burst pressure.

- The minimum required (calculated) burst pressure ratio shall be in accordance with Table 7.4 of Annex 7, and in no case be less than the value necessary to meet the stress ratio requirements. The actual burst pressure shall be recorded. Rupture may occur in either the cylindrical region or the dome region of the Container.

A.13	AMBIENT TEMPERATURE PRESSURE CYCLING

Pressure cycling shall be performed in accordance with the following procedure:

- Fill the Container to be tested with a non-corrosive fluid such as oil, inhibited water or glycol.

- Cycle the pressure in the Container between not more than 2.0 MPa and not less than 1.3 times Working Pressure at a rate not exceeding 10 cycles per minute.

The number of cycles to failure shall be reported, along with the location and description of the failure initiation.

A.14	ACID ENVIRONMENT TEST

On a finished Container the following test procedure should be applied:

- Exposing a 150 mm diameter area on the Container surface for 100 hours to a 30 per cent sulphuric acid solution (battery acid with a specific gravity of 1.219) while the Container is held at 1.3 times Working Pressure.

- The Container shall then be burst in accordance with the procedure defined in Paragraph A.12 of this Appendix. The burst pressure shall exceed 85 per cent of the minimum design burst pressure.

A.15	BONFIRE TEST

A.15.1	General

The bonfire tests are designed to demonstrate that Finished Containers complete with the fire protection system (Pressure Relief Devices and where used integral thermal insulation) specified in the design will prevent the rupture of the Container when tested under the specified fire conditions. Extreme caution must be exercised during fire testing in the event that Container rupture occurs.

A.15.2	Container Set-up

- Containers shall be placed horizontally with the Container bottom approximately 100 mm above the fire source.

- Metallic shielding shall be used to prevent direct flame impingement on Container valves, fittings, or Pressure Relief Devices. The metallic shielding shall not be in direct contact with the specified fire protection system (Pressure Relief Devices or Container valve). Any failure during the test of a valve, fitting or tubing that is not part of the intended protection system for the design shall invalidate the result.

A.15.3	Fire Source

A uniform fire source of 1.65 m length shall provide direct flame impingement on the Container surface across its entire diameter.

Any fuel may be used for the fire source provided it supplies uniform heat sufficient to maintain the specified test temperatures until the Container is vented. The selection of fuel should take into consideration air pollution concerns. The arrangement of the fire shall be recorded in sufficient detail to ensure the rate of heat input to the Container is reproducible. Any failure or inconsistency of the fire source during a test shall invalidate the result.

A.15.4	Temperature And Pressure Measurements

Surface temperatures shall be monitored by at least three thermocouples located along the bottom of the Container and spaced not more than 0.75 m apart. Metallic shielding shall be used to prevent direct flame impingement on the thermocouples. Alternatively, thermocouples may be inserted into blocks of metal measuring less than 25 mm square.

Thermocouple temperatures and the Container pressure shall be recorded at intervals of every 30 seconds or less during the test.

A.15.5	General Test Requirements

Containers shall be pressurised with nitrogen or air and tested in the horizontal position at Working Pressure.

Immediately following ignition, the fire shall produce flame impingement on the surface of the Container along the 1.65 m length of the fire source and across the Container diameter. Within 5 minutes of ignition the temperature of at least one thermocouple shall indicate at least 590 °C. This minimum temperature shall be maintained for the remaining duration of the test.

A.15.6	Containers 1.65 M Length Or Less

The centre of the Container shall be positioned over the centre of the fire source.

A.15.7	Containers Greater Than 1.65 M Length

If the Container is fitted with a Pressure Relief Device at one end, the fire source shall commence at the opposite end of the Container. If the Container is fitted with Pressure Relief Devices at both ends, or at more than one location along the length of the Container, the centre of the fire source shall be centred midway between the Pressure Relief Devices that are separated by the greatest horizontal distance.

If the Container is additionally protected using thermal insulation, then two fire tests at Working Pressure shall be performed, one with the fire centred midway along the Container length, and the other with the fire commencing at one of the Container ends.

A.15.8	Acceptable Results

The Container shall vent through a Pressure Relief Device, and shall not rupture. At no point during venting of the Container shall the pressure inside the Container rise by more than 5% of the pressure at which venting starts.

A.16	PENETRATION TESTS

A Container pressurised to Working Pressure ± 1.0 MPa with compressed gas shall be penetrated by an armour piercing bullet with a diameter of 7.62 mm or greater. The bullet shall completely penetrate at least one side wall of the Container. For Container Type 2, 3 and 4 designs, the projectile shall impact the side wall at an approximate angle of 45°. The Container shall show no evidence of fragmentation failure. Loss of small pieces of material, each not weighing more than 45 grams, shall not constitute failure of the test. The approximate size of entrance and exit openings and their locations shall be recorded.

A.17	COMPOSITE FLAW TOLERANCE TESTS

For Container Type 2, 3 and 4 designs only, one finished Container, complete with protective coating, shall have flaws in the longitudinal direction cut into the composite Over-wrap. The flaws shall be greater than the visual inspection limits as specified by the Manufacturer.

The flawed Container shall then be pressure cycled from not more than 2.0 MPa to not less than 1.3 times the Working Pressure for 3,000 cycles, followed by an additional 12,000 cycles at ambient temperature. The Container shall not leak or rupture within the first 3,000 cycles, but may fail by leakage during the last 12,000 cycles. All Containers which complete this test shall be destroyed.

A.18	HIGH TEMPERATURE CREEP TEST

This test is required for all Container Type 4 designs, and all Container Type 2 and 3 designs in which the glass transition temperature of the resin matrix does not exceed the maximum design material temperature given in Paragraph 3.2 of Annex 7 by at least 20°C. One finished Container shall be tested as follows:

- The Container shall be pressurised to 1.3 times the Working Pressure and held at a temperature of 100 °C for not less than 200 hours.

- Following the test, the Container shall meet the requirements of the hydraulic test Paragraph A.11 of this Appendix, the leak test Paragraph A.10 of this Appendix, and the burst test Paragraph A.12 of this Appendix.

A.19	ACCELERATED STRESS RUPTURE TEST

For Container Type 2, 3, and 4 designs only, one Container free of protective coating shall be hydrostatically pressurised to 1.3 times the Working Pressure while immersed in water at 85 °C. The Container shall be held at this pressure and temperature for 1000 hours. The Container shall then be pressured to burst in accordance with the procedure defined in Paragraph A.12 of this Appendix except that the burst pressure shall exceed 85 per cent of the minimum design burst pressure.

A.20	IMPACT DAMAGE TEST

One or more Finished Containers shall be drop tested at ambient temperature without internal pressurisation or attached valves. The surface onto which the Containers are dropped shall be a smooth, horizontal concrete pad or flooring. One Container shall be dropped in a horizontal position with the bottom 1.8 m above the surface onto which it is dropped. One Container shall be dropped vertically on each end at a sufficient height above the floor or pad so that the potential energy is 488 J, but in no case shall the height of the lower end be greater than 1.8 m. One Container shall be dropped at a 45° angle onto a dome from a height such that the centre of gravity is at 1.8 m; however, if the lower end is closer to the ground than 0.6 m, the drop angle shall be changed to maintain a minimum height of 0.6 m and a centre of gravity of 1.8 m.

Following the drop impact, the Containers shall be pressure cycled from not more than 2.0 MPa to not less than 1.3 times the Working Pressure for 1000 cycles times the specified Service Life in years. The Containers may leak but not rupture, during the cycling. Any Containers completing the cycling test shall be destroyed.

A.21	PERMEATION TEST

This test is only required on Container Type 4 designs. One finished Container shall be filled with compressed hydrogen gas or a 90 per cent nitrogen/10 per cent helium mixture to Working Pressure, placed in an enclosed sealed chamber at ambient temperature, and monitored for leakage for a time sufficient to establish a steady state permeation rate. The permeation rate shall be less than 0.25 ml of hydrogen or helium per hour per litre water capacity of the Container.

A.22	TENSILE PROPERTIES OF PLASTICS

The tensile yield strength and ultimate elongation of plastic Liner material shall be determined at - 50 °C using ISO 527, and meet the requirements of Paragraph 5.3.6 of Annex 7.

A.23	MELTING TEMPERATURE OF PLASTICS

Polymeric materials from finished Liners shall be tested in accordance with the method described in ISO 306, and meet the requirements of Paragraph 5.3.6 of Annex 7.

A.24	Not used

A.25	BOSS TORQUE TEST

The body of the Container shall be restrained against rotation and a torque of 500 Nm shall be applied to each end boss of the Container, first in the direction to tighten the threaded connection, then in the untightening direction, and finally again in the tightening direction. The Container shall be deemed to meet the requirements of this Paragraph if it subsequently passes the burst test defined in Paragraph A.12 of this Appendix.

A.26	RESIN SHEAR STRENGTH

Resin materials shall be tested on a sample coupon representative of the composite Over-wrap in accordance with ASTM D2344, or an equivalent National Standard. Following a 24 hour water boil the composite shall have a minimum shear strength of 13.8 MPa.

A.27	HYDROGEN GAS CYCLING TEST

Special consideration must be given to safety when conducting this test.

Prior to conducting this test, Containers shall have successfully passed the test requirements of:

- Paragraph A.10 of this Appendix(Leak Test),

- Paragraph A.12 of this Appendix (Hydrostatic Pressure Burst Test),

- Paragraph A.13 of this Appendix(Ambient Temperature Pressure Cycling Test),

- Paragraph A.21 of this Appendix (Permeation Test).

One finished Container shall be pressure cycled using compressed hydrogen gas from less than 2.0 MPa to Working Pressure for 1000 cycles. Each cycle, consisting of the filling and venting of the Container, shall not exceed 1 hour. The Container shall be leak tested in accordance with Paragraph A.10 of this Appendix and meet the requirements therein. Following the completion of the hydrogen gas cycling the Container shall be sectioned and the Liner/end boss interface inspected for evidence of any deterioration, such as fatigue cracking or electrostatic discharge.

A.28	HYDROGEN COMPATIBILITY TEST

Hydrogen compatibility testing shall be carried out in accordance with prEN/ISO 11114 - 4.

Annex 7 - APPENDIX B (Informative)

REPORT FORM

NOTE - This appendix is not a mandatory part of Annex 7.

The following forms may be used:

- Report of Manufacture & Certificate of Conformance - Required to be clear, legible and in the format of Form 1.

- Report 1/ of Chemical Analysis of Material for Metallic Containers, Liners, or Bosses - Required Essential Elements, Identification, Etc.

- Report 1/ of Mechanical Properties of Material for Metallic Containers and Liners - Required To Report All Tests Required By This Regulation.

- Report 1/ of Physical and Mechanical Properties of Materials for Non Metallic Liners - Required To Report All Tests And Information Required In This Regulation.

- Report 1/ of Composite Analysis - Required To Report All Tests And Data Required In This Regulation.

- Report of Hydrostatic Tests, Periodic Pressure Cycling and Burst Tests - Required to Report Test And Data Required In This Regulation.

______________

Note: 1/	Report forms 2 through 6 shall be developed by the manufacturer and must fully identify Containers and requirements. Each report shall be signed by the Competent Authority and the Manufacturer.

Form 1: Report of Manufacturer and Certification of Conformance

Manufactured by:

Located at:

Regulatory Registration Number:

Manufacturers Mark and Number:

Serial Number: to be inclusive

Container description:

SIZE: Outside diameter: ……….... mm	Length: …….......mm

Marks stamped on shoulder or on labels of the Container are (delete as appropriate):

- "HYDROGEN (H2) ONLY":

- "DO NOT USE AFTER":

- Manufacturer's mark:

- Serial or part number:

- Working pressure in MPa:

- ECE Regulation:

- Fire protection:	Type

- Date of original test (month & year):

- Tare mass of empty Container in kg:

- Authorised Body or Inspectors Mark:

- Water capacity in L:

- Test pressure in MPa:

- Any special instructions:

Each Container was made in compliance with all requirements of ECE Regulation No. xx in accordance with the Container description above. Required reports of test results are attached.

I hereby certify that all the attached test results proved satisfactory in every way and are in compliance with the requirements for the ECE type listed above.

Comments :

Competent Authority:			Inspector’s name:

Inspectors signature:

Place, Date:

Manufacturer's representative:	Name and position:

Manufacturer's signature:

Place, Date:

Annex 7 - APPENDIX C (Informative)

VERIFICATION OF STRESS RATIOS USING STRAIN GAUGES

C.1	The stress-strain relationship for fibres is always assumed to be elastic, therefore, stress ratios and strain ratios are equal.

C.2	High elongation strain gauges are required.

C.3	Strain gauges should be orientated in the direction of the fibres on which they are mounted, e.g. with hoop fibre on the outside of the Container, mount gauges in the hoop direction.

C.4	Method 1 (applies to Containers that do not use high tension winding)

- Prior to Auto-frettage, apply strain gauges and calibrate.

- Measure strains at Auto-frettage and zero after Auto-frettage Pressure, Working Pressure, and minimum burst pressure have been met.

- Confirm that the strain at burst pressure divided by strain at , Working Pressure meets the stress ratio requirements. For hybrid construction, the strain at, Working Pressure, is compared with the rupture strain of Containers  reinforced with a single fibre type.

C.5	Method 2 (applies to all Containers)

- At zero pressure after winding and Auto-frettage, apply strain gauges and calibrate.

- Measure strains at zero pressure, Working Pressure, and minimum burst pressure.

- At zero pressure, after strain measurements have been taken at the , Working Pressure and minimum burst pressure, and with strain gauges monitored, cut the Container section apart so that the region containing the strain gauge is approximately five inches long. Remove the Liner without damaging the composite Over-wrap. Measure the strains after the Liner is removed.

- Adjust the strain readings at zero pressure, Working Pressure, and minimum burst pressure by the amount of strain measured at zero pressure with and without the Liner.

- Confirm that the strain at burst pressure divided by strain at Working Pressure meets the stress ratio requirements. For hybrid construction, the strain at Working Pressure is compared with the rupture strain of Containers reinforced with a single fibre type.

Annex 7 - APPENDIX D (Informative)

FRACTURE PERFORMANCE METHODS

D.1	Determine fatigue sensitive sites on the Container. The location and orientation of fatigue failure in Containers shall be determined by appropriate stress analysis or by full scale fatigue tests on Finished Containers as required under the design qualification tests for each type of design. If finite element stress analysis is used, the fatigue sensitive site shall be identified based on the location and orientation of the highest tensile principle stress concentration in the Container wall or Liner at the Working Pressure.

D.2	Leak-Before-Break (LBB)

D.2.1	Engineering Critical Assessment

This analysis may be carried out to establish that the finished Container will leak in the event of a defect in the Container or Liner growing into a through-wall crack rather than rupture. A leak-before-break assessment shall be performed at the Container side wall. If the fatigue sensitive location is outside the side wall, a LBB assessment shall also be performed at that location using a Level II approach as outlined in BS PD 6493. The assessment shall include the following steps:

- Measure the maximum length, i.e. major axis, of the resultant through-wall surface crack (usually elliptical in shape) from the three Containers cycle tested under the design qualification tests (according to Paragraphs A.13 and A.14 of Appendix A to this Annex) for each type of design. Use the longest crack length of the three Containers in the analysis. Model a semi-elliptical through-wall crack with a major axis equal to twice the measured longest major axis and with a minor axis equal to 0.9 times Container wall thickness. The semi-elliptical crack shall be modelled at the critical locations where the stress ratio is maximum. The crack shall be oriented such that the highest tensile principal stress shall drive the crack.

- Stress levels in the Container wall/Liner at 1.3 times Working Pressure obtained from the stress analysis as outlined in Paragraph 5.6 of Annex 7 shall be used for the assessment. Appropriate crack driving forces shall be calculated using either Section 9.2 or 9.3 of BS PD 6493.

- Fracture toughness of the finished Container or the Liner from a finished Container, as determined at room temperature for aluminium and at - 40 °C for steel, shall be established using a standardised testing technique (either ISO/FDIS 12737, ASTM 813-89 or BS 7448) in accordance with Section 8.4 and 8.5 of BS PD 6493.

- Plastic collapse ratio shall be calculated in accordance with Section 9.4 of BS PD6493.

- The modelled flaw shall be acceptable in accordance with Section 11.2 of BS PD6493.

D.2.2	LBB By Flawed Container Burst

A fracture test shall be performed on the Container side wall. If the fatigue sensitive locations as determined in Paragraph A.7 of Appendix A to Annex 7 is outside the side wall, the fracture test shall also be performed at that location. The test procedure is as follows:

a)	Determination Of Leak-Before-Break Flaw Length

The length of the LBB flaw at the fatigue sensitive site shall be twice the length of the maximum length measured of the resultant through-wall surface crack from the three Containers cycle tested to failure under the design qualification tests.

b)	Container Flaws

For Container Type 1 designs having fatigue sensitive sites in the cylindrical part in the axial direction, external flaws shall be machined longitudinally, approximately at mid-length of the cylindrical part of the Container. The flaws shall be located at minimum wall thickness of the midsection based on thickness measurements at four points around the Container. For Container Type 1 designs having fatigue sensitive sites outside of the cylindrical part, the LBB flaw shall be introduced at the internal surface of the Container along the fatigue sensitive orientation. For Container Type 2 and 3 designs the LBB flaw shall be introduced in the metal Liner.

For flaws to be tested by monotonic pressure, the flaw cutter shall be approximately 12.5 mm thick with an angle of 45° and a dip radius of 0.25 mm maximum. The cutter diameter shall be 50 mm for Containers with outside diameter less than 140 mm, and 65 to 80 mm for Containers with outside diameter greater than 140 mm (a standard CVN cutter is recommended).

NOTE - The cutter should be sharpened regularly to assure tip radius meets the specification.

The depth of the flaw may be adjusted to obtain a leak by monotonic hydro-pressurisation. The crack shall not propagate by more than 10 per cent outside of the machined flaw measured on the external surface.

c)	Test Procedure

The test shall be performed by monotonic pressurisation or cyclic pressurisation as described below:

i)	Monotonic Pressurisation To Burst

The Container shall be pressurised hydrostatically until pressure is released from the Container at the flaw location. The pressurisation shall be performed as described in Paragraph A.12 (Appendix A to this Annex).

ii)	Cyclic Pressure

The test procedure shall be in accordance with the requirements of Paragraph A.13 (Appendix A to this Annex)

b)	Acceptance Criteria For The Flawed Container Test

The Container passes the tests if the following conditions are met:

i)	For flawed Container burst tests, the failed pressure shall be equal to or greater than 1.3 times Working Pressure.

For monotonic pressurised burst test, a total crack length measured on the external surface of 1.1 times the original machined length is allowed.

ii)	For cycle tested Containers, fatigue crack growth beyond the original machined flaw length is allowed. However, the failure mode must be a "leak". Propagation of the flaw by fatigue should occur over at least 90 per cent of the length of the original machined flaw.

NOTE -	If these requirements are not fulfilled (failure occurs below 1.3 times Working Pressure and the failure is a leak), a new test can be performed with a less deep flaw. Also, if rupture type failure occurs at a pressure greater than 1.3 times Working Pressure and flaw depth is shallow, a new test can be performed with a deeper flaw.

D.3	DEFECT SIZE FOR NON-DESTRUCTIVE EXAMINATION (NDE)

D.3.1	NDE Defect Size By Engineering Critical Assessment

Calculations shall be performed in accordance with British Standard PD 6493, Section 3, using the following steps:

- Fatigue cracks shall be modelled at the high stress location in the Container  wall/ Liner as planar flaws.

- The applied stress range at the fatigue sensitive site, due to a pressure between 2.0 MPa and Working Pressure shall be established from the stress analysis required by Paragraph 5.6 of Annex 7).

- The bending and membrane stress component may be used separately.

- The minimum number of pressure cycles is 15,000.

- The fatigue crack propagation data shall be determined in air in accordance with ASTM E647. The crack plane orientation shall be in the C-L direction, i.e. crack plane perpendicular to the circumferences and along the axis of the Container, as illustrated in ASTM E399. The rate shall be determined as an average of 3 specimen tests. Where specific fatigue crack propagation data are available for the material and service condition, they may be used in the assessment.

- The amount of crack growth in the thickness direction and in the length direction per pressure cycle shall be determined in accordance with the steps outlined in Section 14.2 of BS PD6493 by integrating the relationship between the rate of fatigue crack propagation, as established in e) above, and the range of crack driving force corresponding to the applied pressure cycle.

- Using the above steps, calculate the maximum allowable defect depth and length which shall not cause the failure of the Container during the design life due to either fatigue or rupture. The defect size for NDE shall be equal to or less than the calculated maximum allowable defect size for the design.

D.3.2	NDE Defect Size By Flawed Container Cycling

For Container Type 1, 2 and 3 designs, three Containers containing artificial defects that exceed the defect length and depth detection capability of the NDE inspection method required in Paragraph 5.15. of Annex 7, shall be pressure cycled to failure in accordance with the test method in Paragraph A.13 (Appendix A to Annex 7). For Container Type 1 designs having a fatigue sensitive site in the cylindrical part, external flaws shall be introduced on the side wall. For Container Type 1 designs having the fatigue sensitive site outside the side wall, and for Container Type 2 and 3 designs, internal flaws shall be introduced. Internal flaws may be machined prior to the heat treating and closing of the end of the Container.

The Containers shall not leak or rupture in less than 1000 cycles times the specified Service Life in years. The allowable defect size for NDE shall be equal to or less than the artificial flaw size at that location.

Annex 7 - APPENDIX E (Informative)

CONTAINER MANUFACTURER’S INSTRUCTIONS FOR

HANDLING, USE AND INSPECTION OF CONTAINERS

E.1	GENERAL

The primary function of this document is to provide guidance to the Container purchaser, distributor, installer and user for the safe use of the Container over its intended Service Life.

E.2	DISTRIBUTION

The Manufacturer shall advise the purchaser that the instructions shall be supplied to all parties involved in the distribution, handling, installation and use of the Containers. The document may be reproduced to provide sufficient copies for this purpose, however, it shall be marked to provide reference to the Containers being delivered.

E.3	REFERENCE TO EXISTING CODES, STANDARDS AND REGULATIONS

Specific instructions may be stated by reference to national or recognised codes, standards and regulations.

E.4	CONTAINER HANDLING

Handling procedures shall be provided to ensure that the Containers will not suffer unacceptable damage or contamination during handling.

E.5	INSTALLATION

Installation instructions shall be provided to ensure that the Containers will not suffer unacceptable damage during installation and during normal operation over the intended Service Life.

Where the mounting is specified by the Manufacturer, the instructions shall contain where relevant, details such as mounting design, the use of resilient gasket materials, the correct tightening torque and avoidance of direct exposure of the Container to the environment, chemicals and mechanical contacts.

Where the mounting is not specified by the Manufacturer, the Manufacturer shall draw the purchaser's attention to possible long term impacts of the vehicle mounting system, for example, vehicle body movements and Container expansion/contraction in the pressure and temperature conditions of service.

Where applicable, the purchaser's attention shall be drawn to the need to provide installations such that liquids or solids cannot be collected to cause Container material damage.

The correct Pressure Relieve Device(s) to be fitted shall be specified.

E.6	USE OF CONTAINERS

The Manufacturer shall draw the purchaser's attention to the intended service conditions specified by this Regulation, in particular the Container's allowable number of pressure cycles, its life in years, the gas quality limits and the allowable maximum pressures.

E.7	IN-SERVICE INSPECTION

The manufacturer shall clearly specify the user's obligation to observe the required Container inspection requirements, e.g. reinspection interval, by authorised personnel. This information shall be in agreement with the design approval requirements.

Annex 7 - APPENDIX F (Informative)

ENVIRONMENTAL TEST

F.1	SCOPE

The environmental test demonstrates that hydrogen Containers of Types 2, 3 and 4 can withstand exposure to the automotive underbody environment and occasional exposure to other fluids.

F.2	SUMMARY OF TEST METHOD

A Container is first preconditioned by a combination of pendulum and gravel impacts to simulate potential underbody conditions. The Container is then subjected to a sequence of immersion in simulated road salt/acid rain, exposure to other fluids, pressure cycles and high and low temperature exposures. At the conclusion of the test sequence the Container will be hydraulically pressured to destruction. The remaining residual burst strength of the Container shall be not less than 85 % of the minimum design burst strength.

F.3	CONTAINER SET-UP AND PREPARATION

Two containers shall be tested in a condition representative of installed geometry including coating (if applicable), brackets and gaskets, and pressure fittings using the same sealing configuration, i.e. O-rings, as that used in service. Brackets may be painted or coated prior to installation in the immersion test if they are painted or coated prior to vehicle installation.

One container shall be exposed to environmental conditions in accordance with Paragraph F.5(a) of this Appendix, Immersion Environment, and the other container shall be exposed to environmental conditions in accordance with Paragraph F.5(b) of this Appendix, Other Fluids Exposure. Both container shall be subjected to the appropriate pre-conditioning in the exposure areas and subjected to the complete pressure cycling requirements specified in Paragraphs F.6 and F.7 of this Appendix.

The upper section used for the “other Fluids Exposure“ test will be divided into 5 distinct areas and marked for preconditioning and fluid exposure (see Figure F.1 of this Appendix). The areas will be nominally 100 mm in diameter. The areas shall not overlap on the container surface. While convenient for testing, the areas need not be oriented along a single line, but must not overlap the immersed section of the container.

Although preconditioning and fluid exposure is performed on the cylindrical section of the container, all of the container, including the domed sections, should be as resistant to the exposure environments as are the exposed areas.

As an alternative, one container may be used for both the Immersion Environment and Other Fluids Exposure tests, as long as care is taken to prevent cross contamination among the fluids.

Other fluid

exposure areas

To be supplied

Immersion area

(lower third)

Figure F.1 - Container Orientation And Layout Of Exposure Areas

F.4	PRECONDITIONING APPARATUS

The following apparatus are needed for preconditioning the test Container by pendulum and gravel impact.

a)	Pendulum Impact

The impact body shall be of steel and have the shape of a pyramid with equilateral triangle faces and a square base, the summit and the edges being rounded to a radius of 3 mm. The centre of percussion of the pendulum shall coincide with the centre of gravity of the pyramid. Its distance from the axis of rotation of the pendulum shall be 1 m. The total mass of the pendulum referred to its centre of percussion shall be 15 kg. The energy of the pendulum at the moment of impact shall be not less than 30 Nm and as close to that value as possible.

During pendulum impact, the Container shall be held in position by the end bosses or by the intended mounting brackets.

b)	Gravel Impact

Gravel impact machine shall be constructed according to the design specifications shown in Figure F.2 of this Appendix. The procedure for operation of the equipment shall follow that described in ASTM D3170, Standard Test Method for Chip Resistance of Coatings with the exception that the Container may be at ambient temperature during gravel impact.

c)	Gravel

Alluvial road gravel passing through a 16 mm space screen but retained on a 9.5 mm space screen. Each application is to consist of 550 ml of graded gravel (approx. 250 to 300 stones).

To be supplied

Figure F.2 - Gravel Impact Test

F.5	EXPOSURE ENVIRONMENTS

a)	Immersion Environment

At the specified stage in the test sequence Table F.1 of this Appendix, the Container will be oriented horizontally with the lower third of the Container diameter immersed in a simulated acid rain/road salt water solution. The solution will consist of the following compounds:

Deionised water;

Sodium chloride:	2.5 % by weight ±0.1 %

Calcium chloride:	2.5 % by weight ±0,1 %

Sulphuric acid - Sufficient to achieve a solution pH of 4.0±0.2

Solution level and pH are to be adjusted prior to each test step which uses this liquid.

The temperature of the bath shall be 21 ± 5 °C. During immersion, the unsubmerged section of the Container shall be in ambient air.

b)	Other Fluid Exposure

At the appropriate stage in the test sequence shown in Table F.1 of this Appendix, each marked area is to be exposed to one of five solutions for 30 minutes. The same environment shall be used for each location throughout the test. The solutions are:

Sulphuric acid:	19 % solution by volume in water

Sodium hydroxide:	25 % solution by weight in water;

Methanol/gasoline:	30/70 % concentrations

Ammonium nitrate:	28 % by weight in water

Windshield washer fluid.

When exposed, the test sample will be oriented with the exposure area uppermost. A pad of glass wool one layer thick (approximately 0.5 mm) and trimmed to the appropriate dimensions is to be placed on the exposure area. Using a pipette, apply 5 ml of the test fluid to the exposure area. Remove the gauze pad after pressurisation of the Container for 30 minutes.

F.6	TEST CONDITIONS

a)	Pressure Cycle

As defined in the test sequence, the Container shall be hydraulically pressure cycled between not more than 2.0 MPa and not less than 1.3 times Working Pressure. The total cycle shall be not less than 66 seconds and will include a 60 second minimum hold at 1.3 times Working Pressure. The nominal cycle process will be:

- Ramp up from 2.0 MPa to 1.3 times Working Pressure

- Hold at 1.3 times Working Pressure for 60 seconds minimum

- Ramp down from 1.3 times Working Pressure to 2.0 MPa

- Total minimum cycle time to be 66 seconds.

b)	Pressure During Other Fluid Exposure

Following application of the other fluids, the Container shall be pressured to not less than 1.3 times Working Pressure for a minimum of 30 minutes.

c)	High And Low Temperature Exposure

As defined in the test sequence, the entire Container shall be exposed to high or low temperature air in contact with its external surface. The high and low air temperatures shall be in accordance with Paragraph 2.4.6 of this Regulation ± 5°C. For the low temperature exposure, the fluid temperature of Type 1 Containers shall be monitored using a thermocouple installed within the Container.

F.7	TEST PROCEDURE

a)	Preconditioning of the Container.

Each of the five areas marked for other fluid exposure an the upper section of the Container shall be preconditioned by a single impact of the pendulum body summit at their geometric centre. Following impact, the five areas shall be further conditioned by a gravel impact application.

The central section of the bottom portion of the Container that will be submerged shall be preconditioned by an impact of the pendulum body summit at three locations spaced approximately 150 mm apart.

Following impact, the same central section that was impacted shall be further conditioned by a gravel impact application.

The Container shall be unpressurised during preconditioning.

b)	Test Sequence And Cycles

The sequence of the environment exposure, pressure cycles, and temperature to be used are defined in Table F.1 of this Appendix.

The Container surface is not to be washed or wiped between stages.

F.8	ACCEPTABLE RESULTS

Following the above test sequence, the Container shall be hydraulically tested to destruction in accordance with the procedure in Paragraph A.12 of Appendix A to this Annex. The burst pressure of the Container shall be not less than 85 % of the minimum design burst pressure.

Table F.1 - Test Conditions And Sequence

|  | Test Steps |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Two | Container Approach | Single Container Approach | Environments | Number of pressure cycles | Temperature |
| Immersion container | Other Fluids container | Alternative single container |  |  |  |
| - | 1 | 1 | Other fluids (40 minutes) | - | Ambient |
| 1 | - | 2 | Immersion | 500 x Service Life (yrs) | Ambient |
| - | 2 | - | Air | 500 x Service Life (yrs) | Ambient |
| - | 3 | 3 | Other Fluids (40 minutes) | - | Ambient |
| 2 | 4 | 4 | Air | 250 x Service Life (yrs) | Low |
| - | 5 | 5 | Other Fluids (40 minutes) | - | Ambient |
| 3 | 6 | 6 | Air | 250 x Service Life (yrs) | High |

Annex 7 - APPENDIX G

ULTRASONIC INSPECTION

G.1	SCOPE

Other techniques of ultrasonic inspection may be used, provided these have been demonstrated to be at least equivalent to this Annex and suitable for the manufacturing method adopted.

G.2	GENERAL REQUIREMENTS

Ultrasonic testing shall be carried out by the Container Manufacturer.

The ultrasonic testing equipment shall be capable of at least detecting the reference standard as described in Paragraph G.3.2 of this Appendix. It shall be serviced regularly in accordance with the manufacturers operating instructions to ensure that its accuracy is maintained. Inspection records and approval certificates for the equipment shall be maintained.

The operation of the test equipment shall be by trained personnel and supervised by qualified and experienced personnel certified to level 2 of ISO 9712:1992.

The outer and inner surfaces of any Container which is to be tested ultrasonically shall be in a condition suitable for an accurate and reproducible test.

For flaw detection the pulse echo system shall be used. For thickness measurement either the resonance method or the pulse echo system shall be used. Either contact or immersion techniques of testing shall be used.

A coupling method which ensures adequate transmission of ultrasonic energy between the testing probe and the Container shall be used.

G.3	FLAW DETECTION OF THE CYLINDRICAL PARTS

G.3.1	Procedure

The Container to be inspected and the search unit shall have a rotating motion and translation relative to one another such that a helical scan of the Container will be described. The velocity of rotation and translation shall be constant within ( 10%. The pitch of the helix shall be less than the width covered by the probe (at least a 10% overlap shall be guaranteed) and be related to the effective beam width such as to ensure 100 % coverage at the velocity of rotation and translation used during the calibration procedure.

An alternative scanning method may be used for transverse defect detection, in which the scanning or relative movement of the probes and the work piece is longitudinal, the sweeping motion being such as to ensure a 100% surface coverage with about 10 % overlap of the sweeps.

The Container wall shall be tested for longitudinal defects with the ultrasonic energy transmitted in both circumferential directions and for transverse defects in both longitudinal directions.

In this case, or when optional testing is carried out, on the transition areas between the wall and neck or wall and base, this may be conducted manually if not carried out automatically.

The effectiveness of the equipment shall be periodically checked by passing a Reference Standard through the test procedure. This check shall be carried out at least at the beginning and end of each shift. If during this check the presence of the appropriate reference notch is not detected then all Containers tested subsequent to the last equipment acceptance check shall be retested after the equipment has been reset.

G.3.2	Reference Standard

A Reference Standard of convenient length shall be prepared from a Container of similar diameter and wall thickness range, and from material with the same acoustic characteristics and surface finish as the Container to be inspected. The Reference Standard shall be free from discontinuities which may interfere with the detection of the reference notches.

Reference notches, both longitudinal and transverse, shall be machined on the outer and inner surface of the reference standard. The notches shall be separated such that each notch can be clearly identified.

The dimensions and shape of notches in the Reference Standard shall be as follows:

- The length of the notches shall be no be greater than 50 mm.

- The width of the notches shall be no greater than twice the nominal depth of the notches. However, where this condition cannot be met a maximum width of 1.0 mm is acceptable.

- The depth of the notches shall be 5% ( 0.75 % of the nominal thickness of the reference standard with a minimum of 0.2 mm and a maximum of 1.0 mm, over the full length of the notch. Runouts at each end of the notch are permissible.

- The notches shall be sharp edged at their intersection with the surface of the of the Container wall. The cross section of the notches shall be rectangular except where spark erosion machining methods are used in which case the bottom of the notch may be rounded.

- The shape and dimensions of the notches shall be checked by an appropriate method.

G.3.3	Calibration Of Equipment

Using the Reference Standard described in Paragraph G.3.2 of this Appendix, the equipment shall be adjusted to give clearly identifiable indications from both inner and outer reference notches. The amplitude of the indications shall be as near equal as possible. The indication of smallest amplitude shall be used as the rejection level and for setting visual, audible, recording or sorting devices. The equipment shall be calibrated with the Reference Standard or probe, or both, moving in the same manner, in the same direction and in the same speed as will be used during the inspection of the Container. All visual, audible, recording or sorting device shall operate satisfactorily at the test speed.

G.4	WALL THICKNESS MEASUREMENT

If the measurement of the wall thickness is not carried out at another stage of production, the cylindrical part shall be 100 % examined to ensure that the thickness is not less than the guaranteed minimum value.

G.5	INTERPRETATION OF RESULTS

Containers with indications which are equal to or greater than the lowest of the indications from the reference notches shall be withdrawn.

Surface defects may be removed. After removal of surface defects the Container shall be resubjected to ultrasonic flaw detection and thickness measurement.

Any Container which is shown to be below the guaranteed minimum wall thickness shall be rejected.

Annex 8

REQUIREMENTS FOR SPECIFIC COMPONENTS

Annex 8A

PROVISIONS REGARDING THE APPROVAL OF PRESSURE RELIEF DEVICES

1.	Working Pressure:

Class 0:		See Part I, Paragraph 6.1.5 of this Regulation

Class 1, 2, 3 & 4:	See Part I, Paragraph 6.1.5 of this Regulation

2.	Set pressure:

Working Pressure of the Container

3.	Service Temperature:

See Paragraph 2.4.6 of this Regulation

4.	Applicable test procedures:

Material hydrogen compatibility	Annex 9

Material temperature compatibility	Annex 9

Pressure test				Annex 9

External leakage test			Annex 9

Seat leakage test			Annex 9

Endurance test (applicable to	Annex 9

pressure triggered devices only)	(1000 operation cycles)

Corrosion resistance			Annex 9 */ ***/

Pressure cycle test			Annex 9

Temperature cycle test		Annex 9 **/

5.	Further Requirements For Pressure Relief Devices (Temperature Triggered)

    - Pressure Relief Devices (Temperature Triggered) specified by the Manufacturer shall be shown to be compatible with the service conditions listed in Paragraph 3 of Annex 7 and through the following qualification tests:

    - One specimen shall be held at a controlled temperature of not less than 100°C and a pressure not less than Test Pressure for 24 hours. At the end of this test there shall be no leakage or visible sign of extrusion of any fusible metal used in the design.

    - One specimen shall be fatigue tested at a pressure cycling rate not to exceed 4 cycles per minute as follows:

      - Held at 85 °C while pressured for 10,000 cycles between 2.0 MPa and 1.3 times Working Pressure.

      - Held at - 40 °C while pressure for 10,000 cycles between 2.0 MPa and Working Pressure.

At the end of this test there shall be no leakage, or any visible sign of extrusion of any fusible metal used in the design.

    - Exposed brass pressure retaining components of Pressure Relief Devices shall withstand, without stress corrosion cracking, a mercurous nitrate test as described in ASTM B154. The Pressure Relief Device shall be immersed for 30 minutes in an aqueous mercurous nitrate solution containing 10 g of mercurous nitrate and 10 ml of nitric acid per litre of solution. Following the immersion, the Pressure Relief Device shall be leak tested by applying a pneumatic pressure of 1.3 times Working Pressure for one minute during which time the component shall be checked for external leakage. Any leakage shall not exceed 200 cm3/h.

    - Exposed stainless steel pressure retaining components of Pressure Relief Devices shall be made of an alloy type resistant to chloride induced stress corrosion cracking.

_____________________

*/	only for metallic parts

**/	only for non-metallic parts

***/	only for equipment outside of the Gas Tight housing.

Annex 8B

PROVISIONS REGARDING THE APPROVAL OF HYDROGEN VALVES

1.	Working Pressure:

See Part I, Paragraph 6.1.5 of this Regulation

2.	Service Temperature:

See Paragraph 2.4.6 of this regulation

3.	Applicable test procedures:

Material hydrogen compatibility	Annex 9

Material temperature compatibility	Annex 9

Pressure test				Annex 9

External leakage test			Annex 9

Seat leakage test			Annex 9

Endurance test			Annex 9

Manual:	20000 operation cycles

Automatic:	20000 operation cycles

Corrosion resistance			Annex 9 */ ***/

Resistance to dry-heat		Annex 9

Ozone ageing				Annex 9 **/

Temperature cycle test		Annex 9 **/

_____________________

*/	only for metallic parts

**/	only for non-metallic part

***/	only for equipment outside of the Gas Tight housing.

Annex 8C

PROVISIONS REGARDING THE APPROVAL OF HEAT EXCHANGERS

1.	Working Pressure:

See Part I, Paragraph 6.1.5 of this Regulation

2.	Service Temperature:

See Paragraph 2.4.6 of this Regulation

3.	Applicable test procedures:

Material hydrogen compatibility	Annex 9

Material temperature compatibility	Annex 9

Pressure test				Annex 9

External leakage test			Annex 9

Corrosion resistance			Annex 9 */

Resistance to dry-heat		Annex 9

Ozone ageing				Annex 9 **/

Pressure cycle test			Annex 9

Temperature cycle test		Annex 9 **/

_____________________

*/	only for metallic parts

**/	only for non-metallic part

Annex 8D

PROVISIONS REGARDING THE APPROVAL OF REFUELLING CONNECTIONS OR RECEPTACLES

1.	Working Pressure:

See Part I, Paragraph 6.1.5 of this Regulation

2.	Service Temperature:

See Paragraph 2.4.6 of this Regulation

3.	Applicable test procedures:

Material hydrogen compatibility	Annex 9

Material temperature compatibility	Annex 9

Pressure test				Annex 9

External leakage test			Annex 9

Seat leakage test			Annex 9

Endurance test			Annex 9

(20000 operation cycles)

Corrosion resistance			Annex 9 */

Resistance to dry-heat		Annex 9

Ozone ageing				Annex 9 **/

Temperature cycle test		Annex 9 **/

_____________________

*/	only for metallic parts

**/	only for non-metallic part

Annex 8E

PROVISIONS REGARDING THE APPROVAL OF PRESSURE REGULATORS

1.	Working Pressure:

Class 0:		See Part I, Paragraph 6.1.5 of this Regulation

Class 1, 2, 3 & 4:	2.0 x Outlet Pressure of the upstream stage of the Pressure Regulator or the first upstream Pressure Regulator.

2.	Service Temperature:

See Paragraph 2.4.6 of this Regulation

3.	Applicable test procedures:

Material hydrogen compatibility	Annex 9

Material temperature compatibility	Annex 9

Pressure test				Annex 9

External leakage test			Annex 9

Seat leakage test			Annex 9

Endurance test			Annex 9

(20000 operation cycles)

Corrosion resistance			Annex 9 */ ***/

Resistance to dry-heat		Annex 9

Ozone ageing				Annex 9 **/

Pressure cycle test			Annex 9

Temperature cycle test		Annex 9 **/

_____________________

*/	only for metallic parts

**/	only for non-metallic parts

***/	only for equipment outside of the Gas Tight housing.

Annex 8F

PROVISIONS REGARDING THE APPROVAL OF SENSORS FOR HYDROGEN SYSTEMS

1.	Working Pressure:

See Part I, Paragraph 6.1.5 of this Regulation

2.	Service Temperature:

See Paragraph 2.4.6 of this Regulation

3.	Applicable test procedures for every sensor except Hydrogen Sensors:

Pressure test			Annex 9

External leakage test		Annex 9

Corrosion resistance		Annex 9 */ ***/

Resistance to dry-heat	Annex 9

Ozone ageing			Annex 9 **/

Temperature cycle test	Annex 9 **/

4.	Additional test procedure for pressure sensors only

Pressure cycle test		Annex 9

5.	Hydrogen Sensors shall be designed and approved in accordance with EN 50054, EN 50057 and EN 50058.

__________________

*/	only for metallic parts

**/	only for non-metallic parts

***/	only for equipment outside of the Gas Tight housing.

Annex 8G

PROVISIONS REGARDING THE APPROVAL OF FLEXIBLE FUEL LINES

1	SCOPE

This annex covers three types of flexible fuel lines:

- Class 0 - High pressure

- Class 1 - Medium pressure

- Class 2 - Low pressure

2	GENERAL

2.1	Applicable test procedures for every Flexible Fuel Line:

Material hydrogen compatibility	Annex 9

Pressure test				Annex 9

External leakage test			Annex 9

Corrosion resistance			Annex 9 */ ***/

Resistance to dry-heat		Annex 9

Ozone ageing				Annex 9 **/

Temperature cycle test		Annex 9 **/

Pressure cycle test			Annex 9

Notes:

*/	only for metallic parts

**/	only for non-metallic parts

***/	only for equipment outside of the Gas Tight housing.

2.2	Specific requirements related to the Pressure Classification of the Flexible Fuel Lines are given in the following paragraphs.

2.3	For all Class 0 Hydrogen Systems the complete Fuel Line assemblies shall be Pressure Cycle tested in accordance with Paragraph 14.3 of Annex 9 to this regulation.

3	CLASS 0 - HIGH PRESSURE FLEXIBLE FUEL LINES

3.1	General Specifications

3.1.1	Working Pressure shall be 1.50 x Working Pressure of the Container.

3.1.2	Service Temperatures shall be in accordance with Paragraph 2.4.6 of this Regulation.

3.1.3	The inside diameter shall be in compliance with Table 1 of ISO 1307: 1992 Rubber And Plastic Hoses For General purpose Industrial Applications - Bore Diameters And Tolerances, And Tolerances On Length.

3.2	Flexible Fuel Line Construction

3.2.1	The Flexible Fuel Line shall comprise a smooth bore tubular lining and a cover of suitable synthetic material, reinforced with one or more interlayer(s).

3.2.2	The reinforcing interlayer(s) shall be protected by a cover against corrosion, unless corrosion-resistant-material, i.e. stainless-steel is used for the reinforcing interlayer(s).

3.2.3	The lining shall be smooth and free from pores, holes, etc.

3.2.4	The cover shall be intentionally perforated to avoid the formation of bubbles between the layers, however, it shall otherwise be free from pores, holes etc..

3.3	Specifications And Tests For The Lining

3.3.1	Tensile Strength And Elongation

Tensile strength and elongation at break shall be in accordance with ISO 37: 1994 Rubber, vulcanised Or Thermoplastic - Determination Of Tensile Stress-strain Properties. The tensile strength shall be not less than 20 MPa and elongation at break not less than 250 per cent.

3.3.2	Resistance to ageing shall be in accordance with ISO 188: 1998 Rubber, Vulcanised Or Thermoplastic - Accelerated Ageing And Heat Resistance Tests with the following conditions:

- Temperature: 75°C (test temperature = maximum Service Temperature - 10°C)

- Exposure period: 168 hours

Requirements:

- Maximum change in tensile strength 25 per cent

- Maximum change in elongation at break -30 per cent and +10 per cent

3.4	Specifications And Tests For The Cover

3.4.1	Tensile strength and elongation at break shall be in accordance with ISO 37: 1994 Rubber, vulcanised Or Thermoplastic - Determination Of Tensile Stress-strain Properties. The tensile strength shall be not less than 10 MPa and elongation at break not less than 250 per cent.

3.4.2	Resistance to ageing shall be in accordance with ISO 188: 1998 Rubber, Vulcanised Or Thermoplastic - Accelerated Ageing And Heat Resistance Tests with the following conditions:

- Temperature: 70°C (test temperature = maximum Service Temperature - 10°C)

- Exposure period: 336 hours

Requirements:

- Maximum change in tensile strength 25 per cent

- Maximum change in elongation at break -30 per cent and +10 per cent

3.5	Specifications For Flexible Fuel Line

3.5.1	Gas-tightness (Permeability)

3.5.1.1	One finished flexible fuel line shall be filled with compressed hydrogen gas or a 90 per cent nitrogen/10 per cent helium mixture to Working Pressure, placed in an enclosed sealed chamber at ambient temperature, and monitored for leakage for a time sufficient to establish a steady state permeation rate.

3.5.1.2	The leakage through the wall of the hose shall not exceed 25 cm3 of helium or hydrogen per metre of hose per 24 hours.

3.5.2	Resistance At Low Temperature

3.5.2.1	The test shall be carried out in compliance with the method described in ISO 4672: 1978 Rubber And Plastic Hoses - Sub-ambient Temperature Flexibility Tests, method B.

3.5.2.2	The test-temperature shall be the appropriate minimum temperature from Paragraph 2.4.6 of this Regulation ± 3°C.

3.5.2.3	The test piece shall not crack or rupture.

3.5.3	Bending test

3.5.3.1	An empty Flexible Fuel Line, with a length of approximately 3.5 m must be able to withstand 3,000 times the following bending-test without breaking. After the test the hose must be capable of withstanding the test-pressure stated in Paragraph 3.5.4.2 of this Annex

3.5.3.2Bending radius and distance between bending centres shall be as follows:

| Inside Diameter of Flexible Fuel Line (mm) | Bending Radius (mm) | Distance Between Centres Vertical Horizontal mm mm |
| --- | --- | --- |
| Up to 13 | 102 | 241 102 |
| 13 to 16 | 153 | 356 153 |
| From 16 to 20 | 178 | 419 178 |

3.5.3.3	The testing-machine shall consist of a rigid frame, provided with two wheels, with a rim-width of 130 mm.

The radius of the wheels, measured to the bottom of the groove, shall be as indicated in Paragraph 3.5.3.2 of this Annex. The circumference of the wheels shall be grooved for the guidance of the hose.

The longitudinal median planes of both wheels shall be in the same vertical plane and the distance between the wheel-centres shall be in accordance with Paragraph 3.5.3.2 of this Annex.

Each wheel shall be able to rotate freely round its pivot-centre.

A propulsion-mechanism shall pull the Flexible Fuel Line over the wheels at a speed of four complete motions per minute.

The Flexible Fuel Line shall be installed in an S-shape over the wheels. The end, that runs over the upper wheel shall be tightened against the wheels. The part that runs over the lower wheel is attached to the propulsion-mechanism.

The mechanism shall be adjusted, so that the Flexible Fuel Line travels a total distance of 1.2 m in both directions.

3.5.4	Hydraulic-Test-Pressure And Minimum Burst Pressure

3.5.4.1	The test shall be carried out in compliance with the method described in ISO 1402: 1994 Rubber And Plastic Hose Assemblies - Hydrostatic Testing.

3.5.4.2	The test-pressure shall be 4.0 x Working Pressure of the Container, and shall be applied for a period of 10 minutes without any leakage.

3.5.4.3	The burst pressure shall not be less than 8 x Working Pressure.

3.6	Couplings

The couplings shall be in accordance with Annex 8H of this Regulation.

3.7	Assembly Of Flexible Fuel Line And Couplings

3.7.1	The construction of the couplings must be such, that it is not necessary to peel the cover unless the reinforcement of the Flexible Fuel Line consists of corrosion-resistant material.

3.7.2	The Flexible Fuel Line assembly shall be subjected to an impulse test in compliance with ISO 1436: 1991 Rubber Hoses And Hose Assemblies - Wire Reinforced Hydraulic Type - Specification with the following requirements:

- The test shall be completed with circulating oil having a temperature of 93°C, and a minimum pressure of 3.0 MPa.

- The Flexible Fuel Line shall be subjected to 150,000 impulses.

- After the impulse-test the Flexible Fuel Line shall withstand the test-pressure as mentioned in Paragraph 3.5.4 of this Annex.

3.7.3	Gas-tightness

The Flexible Fuel Line assembly (Flexible Fuel Line with couplings) shall withstand for a period of five minutes a gas pressure of 4.0 x Working Pressure of the Container without any leakage.

3.8	Markings

3.8.1	Every hose shall be marked at intervals of not greater than 0.5 m, the following clearly legible and indelible identification markings consisting of characters, figures or symbols.

- Trade name or mark of the manufacturer

- Year and month of fabrication

- Size and pressure rating

- Identification-marking "CGH2 - Class 0",

- The marking “DO NOT USE AFTER yyyy/mm” where yyyy/mm is the year and month of approval plus the approved lifetime of the Container.

3.8.2	Every coupling shall bear the trade name or mark of the assembling manufacturer.

4	CLASS 1 - MEDIUM PRESSURE FLEXIBLE FUEL LINES

4.1	General Specifications

4.1.1	Working Pressure shall be 1.50 x Working Pressure (outlet) of the first upstream Pressure Regulator.

4.1.2	Service Temperatures shall be in accordance with Paragraph 2.4.6 of this Regulation.

4.1.3	The inside diameter shall be in compliance with Table 1 of ISO 1307: 1992 Rubber And Plastic Hoses For General purpose Industrial Applications - Bore Diameters And Tolerances, And Tolerances On Length.

4.2	Flexible Fuel Line Construction

4.2.1	The Flexible Fuel Line shall comprise a smooth bore tubular lining and a cover of suitable synthetic material, reinforced with one or more interlayer(s).

4.2.2	The reinforcing interlayer(s) shall be protected by a cover against corrosion, unless corrosion-resistant-material, i.e. stainless-steel is used for the reinforcing interlayer(s).

4.2.3	The lining shall be smooth and free from pores, holes, etc.

4.2.4	The cover may be intentionally perforated to avoid the formation of bubbles between the layers, however, it shall otherwise be free from pores, holes etc..

4.3	Specifications And Tests For The Lining

4.3.1	Tensile Strength And Elongation

Tensile strength and elongation at break shall be in accordance with ISO 37: 1994 Rubber, vulcanised Or Thermoplastic - Determination Of Tensile Stress-strain Properties. The tensile strength shall be not less than 10 MPa and elongation at break not less than 250 per cent.

4.3.2	Resistance to ageing shall be in accordance with ISO 188: 1998 Rubber, Vulcanised Or Thermoplastic - Accelerated Ageing And Heat Resistance Tests with the following conditions:

- Temperature: 110°C (test temperature = maximum Service Temperature - 10°C)

- Exposure period: 168 hours

Requirements:

- Maximum change in tensile strength 25 per cent

- Maximum change in elongation at break -30 per cent and +10 per cent

4.4	Specifications And Tests For The Cover

4.4.1	Tensile strength and elongation at break shall be in accordance with ISO 37: 1994 Rubber, vulcanised Or Thermoplastic - Determination Of Tensile Stress-strain Properties. Tensile strength not less than 10 MPa and elongation at break not less than 250 per cent.

4.4.2	Resistance to ageing shall be in accordance with ISO 188: 1998 Rubber, Vulcanised Or Thermoplastic - Accelerated Ageing And Heat Resistance Tests with the following conditions:

- Temperature: 110°C (test temperature = maximum Service Temperature - 10°C)

- Exposure period: 336 hours

Requirements:

- Maximum change in tensile strength 25 per cent

- Maximum change in elongation at break -30 per cent and +10 per cent

4.5	Specifications For Flexible Fuel Line

4.5.1	Gas-tightness (Permeability)

4.5.1.1	One finished flexible fuel line shall be filled with compressed hydrogen gas or a 90 per cent nitrogen/10 per cent helium mixture to Working Pressure, placed in an enclosed sealed chamber at ambient temperature, and monitored for leakage for a time sufficient to establish a steady state permeation rate.

4.5.1.2	The leakage through the wall of the hose shall not exceed 25 cm3 of helium or hydrogen per metre of hose per 24 hours.

4.5.2	Resistance At Low Temperature

4.5.2.1	The test shall be carried out in compliance with the method described in ISO 4672: 1978 Rubber And Plastic Hoses - Sub-ambient Temperature Flexibility Tests method B.

4.5.2.2	The test-temperature shall be the appropriate minimum temperature from Paragraph 2.4.6 of this Regulation ± 3°C.

4.5.2.3	The test piece shall not crack or rupture.

4.5.3	Bending test

4.5.3.1	An empty Flexible Fuel Line, with a length of approximately 3.5 m must be able to withstand 3,000 times the following bending-test without breaking. After the test the hose must be capable of withstanding the test-pressure stated in Paragraph 4.5.4.2 of this Annex

4.5.3.2Bending radius and distance between bending centres shall be as follows:

| Inside Diameter of Flexible Fuel Line (mm) | Bending Radius (mm) | Distance Between Centres Vertical Horizontal mm mm |
| --- | --- | --- |
| Up to 13 | 102 | 241 102 |
| 13 to 16 | 153 | 356 153 |
| From 16 to 20 | 178 | 419 178 |

4.5.3.3	The testing-machine shall consist of a rigid frame, provided with two wheels, with a rim-width of 130 mm.

The radius of the wheels, measured to the bottom of the groove, shall be as indicated in Paragraph 4.5.3.2 of this Annex. The circumference of the wheels shall be grooved for the guidance of the hose.

The longitudinal median planes of both wheels shall be in the same vertical plane and the distance between the wheel-centres shall be in accordance with Paragraph 4.5.3.2 of this Annex.

Each wheel shall be able to rotate freely round its pivot-centre.

A propulsion-mechanism shall pull the Flexible Fuel Line over the wheels at a speed of four complete motions per minute.

The Flexible Fuel Line shall be installed in an S-shape over the wheels. The end, that runs over the upper wheel shall be tightened against the wheels. The part that runs over the lower wheel is attached to the propulsion-mechanism.

The mechanism shall be adjusted, so that the Flexible Fuel Line travels a total distance of 1.2 m in both directions.

4.5.4	Hydraulic-Test-Pressure And Minimum Burst Pressure

4.5.4.1	The test shall be carried out in compliance with the method described in ISO 1402: 1994 Rubber And Plastic Hose Assemblies - Hydrostatic Testing.

4.5.4.2	The test-pressure shall be 4.0 x Working Pressure (outlet) of the first upstream Pressure Regulator, and shall be applied for a period of 10 minutes without any leakage.

4.5.4.3	The burst pressure shall not be less than 8 x Working Pressure.

4.6	Couplings

The couplings shall be in accordance with Annex 8H of this Regulation.

4.7	Assembly Of Flexible Fuel Line And Couplings

4.7.1	The construction of the couplings must be such, that it is not necessary to peel the cover unless the reinforcement of the Flexible Fuel Line consists of corrosion-resistant material.

4.7.2	The Flexible Fuel Line assembly shall be subjected to an impulse test in compliance with ISO 1436: 1991 Rubber Hoses And Hose Assemblies - Wire Reinforced Hydraulic Type - Specification with the following requirements:

- The test shall be completed with circulating oil having a temperature of 93°C, and a minimum pressure of 3.0 MPa.

- The Flexible Fuel Line shall be subjected to 150,000 impulses.

- After the impulse-test the Flexible Fuel Line shall withstand the test-pressure as mentioned in Paragraph 4.5.4 of this Annex.

4.7.3	Gas-tightness

The Flexible Fuel Line assembly (Flexible Fuel Line with couplings) shall withstand for a period of five minutes a gas pressure of 4.0 x Working Pressure (outlet) of the first upstream Pressure Regulator without any leakage.

4.8	Markings

4.8.1	Every hose shall be marked at intervals of not greater than 0.5 m, the following clearly legible and indelible identification markings consisting of characters, figures or symbols.

- Trade name or mark of the manufacturer

- Year and month of fabrication

- Size and pressure rating

- Identification marking "CGH2 - Class 1"

- The marking “DO NOT USE AFTER yyyy/mm” where yyyy/mm is the year and month of approval plus the approved lifetime of the Container.

4.8.2	Every coupling shall bear the trade name or mark of the assembling manufacturer.

5	CLASS 2 - LOW PRESSURE FLEXIBLE FUEL LINES

5.1	General Specifications

5.1.1	Working Pressure shall be 1.50 x Working Pressure (outlet) of the first upstream Pressure Regulator.

5.1.2	Service Temperatures shall be in accordance with Paragraph 2.4.6 of this Regulation.

5.1.3	The inside diameter shall be in compliance with Table 1 of ISO 1307: 1992 Rubber And Plastic Hoses For General purpose Industrial Applications - Bore Diameters And Tolerances, And Tolerances On Length.

5.2	Flexible Fuel Line Construction

5.2.1	The Flexible Fuel Line shall be of smooth bore tubular construction.

5.2.2	The Flexible Fuel Line shall be smooth and free from pores, holes, etc.

5.2.3	If the Flexible Fuel Line is constructed from a lining and cover, the cover may be intentionally perforated to avoid the formation of bubbles between the layers, however, it shall otherwise be free from pores, holes etc..

5.3	Specifications And Tests For The Lining

5.3.1	Tensile Strength And Elongation

Tensile strength and elongation at break shall be in accordance with ISO 37: 1994 Rubber, vulcanised Or Thermoplastic - Determination Of Tensile Stress-strain Properties. The tensile strength shall be not less than 10 MPa and elongation at break not less than 250 per cent.

5.3.2	Resistance to ageing shall be in accordance with ISO 188: 1998 Rubber, Vulcanised Or Thermoplastic - Accelerated Ageing And Heat Resistance Tests with the following conditions:

- Temperature: 120°C (test temperature = maximum Service Temperature)

- Exposure period: 168 hours

Requirements:

- Maximum change in tensile strength 35 per cent

- Maximum change in elongation at break -30 per cent and +10 per cent

5.4	Specifications And Tests For The Cover

5.4.1	Tensile strength and elongation at break shall be in accordance with ISO 37: 1994 Rubber, vulcanised Or Thermoplastic - Determination Of Tensile Stress-strain Properties. Tensile strength not less than 10 MPa and elongation at break not less than 250 per cent.

5.4.2	Resistance to ageing shall be in accordance with ISO 188: 1998 Rubber, Vulcanised Or Thermoplastic - Accelerated Ageing And Heat Resistance Tests with the following conditions:

- Temperature: 120°C (test temperature = maximum Service Temperature)

- Exposure period: 336 hours

Requirements:

- Maximum change in tensile strength 25 per cent

- Maximum change in elongation at break -30 per cent and +10 per cent

5.5	Specifications For Flexible Fuel Line

5.5.1	Gas-tightness (Permeability)

5.5.1.1	One finished flexible fuel line shall be filled with compressed hydrogen gas or a 90 per cent nitrogen/10 per cent helium mixture to Working Pressure, placed in an enclosed sealed chamber at ambient temperature, and monitored for leakage for a time sufficient to establish a steady state permeation rate.

      - The leakage through the wall of the hose shall not exceed 25 cm3 of helium or hydrogen per metre of hose per 24 hours.

5.5.2	Resistance At Low Temperature

      - The test shall be carried out in compliance with the method described in ISO 4672: 1978 Rubber And Plastic Hoses – Sub-ambient Temperature Flexibility Tests method B.

      - The test-temperature shall be the appropriate minimum temperature from Paragraph 2.4.6 of this Regulation ± 3°C.

      - The test piece shall not crack or rupture.

5.5.3	Bending test

5.5.3.1	An empty Flexible Fuel Line, with a length of approximately 3.5 m must be able to withstand 3,000 times the following bending-test without breaking. After the test the hose must be capable of withstanding the test-pressure stated in Paragraph 5.5.4.2 of this Annex

5.5.3.2Bending radius and distance between bending centres shall be as follows:

| Inside Diameter of Flexible Fuel Line (mm) | Bending Radius (mm) | Distance Between Centres Vertical Horizontal mm mm |
| --- | --- | --- |
| Up to 13 | 102 | 241 102 |
| 13 to 16 | 153 | 356 153 |
| From 16 to 20 | 178 | 419 178 |

5.5.3.3	The testing-machine shall consist of a rigid frame, provided with two wheels, with a rim-width of 130 mm.

The radius of the wheels, measured to the bottom of the groove, shall be as indicated in Paragraph 5.5.3.2 of this Annex. The circumference of the wheels shall be grooved for the guidance of the hose.

The longitudinal median planes of both wheels shall be in the same vertical plane and the distance between the wheel-centres shall be in accordance with Paragraph 5.5.3.2 of this Annex.

Each wheel shall be able to rotate freely round its pivot-centre.

A propulsion-mechanism shall pull the Flexible Fuel Line over the wheels at a speed of four complete motions per minute.

The Flexible Fuel Line shall be installed in an S-shape over the wheels. The end, that runs over the upper wheel shall be tightened against the wheels. The part that runs over the lower wheel is attached to the propulsion-mechanism.

The mechanism shall be adjusted, so that the Flexible Fuel Line travels a total distance of 1.2 m in both directions.

5.5.4	Hydraulic-Test-Pressure And Minimum Burst Pressure

5.5.4.1	The test shall be carried out in compliance with the method described in ISO 1402: 1994 Rubber And Plastic Hose Assemblies – Hydrostatic Testing.

5.5.4.2	The test-pressure shall be 4.0 x Working Pressure (outlet) of the first upstream Pressure Regulator, and shall be applied for a period of 10 minutes without any leakage.

5.5.4.3	The burst pressure shall not be less than 8 x Working Pressure.

5.6	Couplings

The couplings shall be in accordance with Annex 8H of this Regulation.

5.7	Assembly Of Flexible Fuel Line And Couplings

5.7.1	The construction of the couplings must be such, that it is not necessary to peel the cover unless the reinforcement of the Flexible Fuel Line consists of corrosion-resistant material.

5.7.2	The Flexible Fuel Line assembly shall be subjected to an impulse test in compliance with ISO 1436: 1991 Rubber Hoses And Hose Assemblies – Wire Reinforced Hydraulic Type – Specification with the following requirements:

- The test shall be completed with circulating oil having a temperature of 93°C, and a minimum pressure of 3.0 Mpa.

- The Flexible Fuel Line shall be subjected to 150,000 impulses.

- After the impulse-test the Flexible Fuel Line shall withstand the test-pressure as mentioned in Paragraph 5.5.4 of this Annex.

5.7.3	Gas-tightness

The Flexible Fuel Line assembly (Flexible Fuel Line with couplings) shall withstand for a period of five minutes a gas pressure of 4.0 x Working Pressure (outlet) of the first upstream Pressure Regulator without any leakage.

5.8	Markings

5.8.1	Every hose shall be marked at intervals of not greater than 0.5 m, the following clearly legible and indelible identification markings consisting of characters, figures or symbols.

- Trade name or mark of the manufacturer

- Year and month of fabrication

- Size and pressure rating

- Identification marking “CGH2 – Class 2”,

- The marking “DO NOT USE AFTER yyyy/mm” where yyyy/mm is the year and month of approval plus the approved lifetime of the Container.

5.8.2	Every coupling shall bear the trade name or mark of the assembling manufacturer.

Annex 8H

PROVISIONS REGARDING THE APPROVAL OF

FITTINGS OR SCREWED CONNECTION SYSTEMS

1.	Working Pressure:

See Part I, Paragraph 6.1.5 of this Regulation

2.	Service Temperature:

See Paragraph 2.4.6 of this Regulation

3.	Applicable test procedures:

Material hydrogen compatibility	Annex 9

Pressure test				Annex 9

External leakage test			Annex 9

Corrosion resistance			Annex 9 */ ***/

Resistance to dry-heat		Annex 9

Endurance test			Annex 9

(100 Connection and disconnection cycles)

Temperature cycle test		Annex 9 **/

Connection test			Annex 9

*/	only for metallic parts

**/	only for non-metallic parts

***/	only for equipment outside of the Gas Tight housing.

Annex 8I

PROVISIONS REGARDING THE APPROVAL OF EXCESS FLOW SYSTEMS

1.	Working Pressure:

See Part I, Paragraph 6.1.5 of this Regulation

2.	Service Temperature:

See Paragraph 2.4.6 of this Regulation

3.	Applicable test procedures:

Material hydrogen compatibility	Annex 9

Material temperature compatibility	Annex 9

Pressure test				Annex 9

External leakage test			Annex 9

Seat leakage test			Annex 9

Endurance test			Annex 9

(1000 operation cycles)

Corrosion resistance			Annex 9 */ ***/

Resistance to dry-heat		Annex 9

Ozone ageing				Annex 9 **/

Temperature cycle test		Annex 9 **/

*/	only for metallic parts

**/	only for non-metallic parts

***/	only for equipment outside of the Gas Tight housing.

Annex 8J

PROVISIONS REGARDING THE APPROVAL OF HYDROGEN FILTERS

1.	Working Pressure:

Class 0:		See Part I, Paragraph 6.1.5 of this Regulation

Class 1, 2, 3 & 4:	2.0 x Outlet Pressure of the upstream Pressure Regulator

2.	Service Temperature:

See Paragraph 2.4.6 of this Regulation

3.	Applicable test procedures:

Material hydrogen compatibility	Annex 9

Material temperature compatibility	Annex 9

Pressure test				Annex 9

External leakage test			Annex 9

Corrosion resistance			Annex 9 */ ***/

Resistance to dry-heat		Annex 9

Ozone ageing				Annex 9 **/

Pressure cycle test			Annex 9

Temperature cycle test		Annex 9 **/

*/	only for metallic parts

**/	only for non-metallic parts

***/	only for equipment outside of the Gas Tight housing.

Annex 9

APPROVAL TEST PROCEDURES FOR SPECIFIC COMPONENTS

EXCLUDING HYDROGEN CONTAINERS

1.	CLASSIFICATION

1.1	Hydrogen Components for use in vehicles shall be classified with regard to their Working Pressure and function, in accordance with Paragraph 2.3 of this Regulation.

1.2	The classification of Specific Components determines the tests which have to be performed for approval of the components or parts of the components.

2.	APPLICABLE TEST PROCEDURES

In Table 9.1 below the applicable test procedures to be carried out dependent upon the classification are stated.

Table 9.1

| TEST | Class 0 | Class 1 | Class 2 | Paragraph of this Annex |
| --- | --- | --- | --- | --- |
| Overpressure or strength | X | X | X | 4 |
| External leakage | X | X | X | 5 |
| Internal leakage | A | A | A | 6 |
| Durability tests | A | A | A | 7 |
| Hydrogen compatibility | A | A | A | 8 |
| Corrosion resistance | X | X | X | 9 |
| Resistance to dry heat | A | A | A | 10 |
| Ozone ageing | A | A | A | 11 |
| Burst/destructive tests | X | NA | NA | 12 |
| Temperature cycle | A | A | A | 13 |
| Pressure cycle | A | NA | NA | 14 |
| Vibration resistance | A | A | A | 15 |
| Service Temperatures | X | X | X | 16 |
| Connection test | X | X | X | 17 |

Key:

X	Applicable

NA	Not applicable

A	If applicable

3.	GENERAL REQUIREMENTS

3.1	Leakage tests shall be conducted with pressurised gas such as air or nitrogen containing at least 10% helium.

3.2	Water or another fluid may be used to obtain the required pressure for the hydrostatic strength test.

3.3	All test records shall indicate the type of test medium used, if applicable.

3.4	The test period for leakage and pressure tests shall be not less than 3 minutes.

3.5	All tests shall be performed at a temperature of 20°C ± 5°C, unless otherwise stated.

3.6	The materials used for the components shall have written specifications that fulfill test requirements laid down in this Annex with respect to:

- Temperature

- Pressure

- Hydrogen compatibility

- Durability

4.	PRESSURE TEST

4.1	A hydrogen containing component previously subjected to the durability test of Paragraph 7 shall withstand a hydraulic pressure test in accordance with Table 9.2 below, with the outlets of the high pressure part plugged without any visible evidence of rupture or permanent distortion.

Table 9.2

| Classification of component | Overpressure |
| --- | --- |
| Class 0 | 1.5 x Working Pressure |
| Class 1 | 1.5 x Working Pressure |
| Class 2 | 2.0 x Working Pressure |

4.2	The pressure supply system shall be equipped with a positive shut-off valve and a pressure gauge having a pressure range of not less than 1.5 times nor more than 2 times the test pressure.

4.3	For components requiring a leakage test, this test shall be performed prior to the pressure test.

5.	EXTERNAL LEAKAGE TEST

5.1	The external leakage test shall include external leakage and permeation. A component shall be free from leakage through stem or body seals or other joints, and shall not show evidence of porosity in casting when tested as described below at any pneumatic pressure between zero and its Working Pressure.

5.2	The test shall be performed on the same component at the following conditions:

- Temperature = 20°C ( 5°C.

- At the minimum Service Temperature (see Paragraph 2.4.6 of this Regulation) after 3 hours conditioning at this temperature.

- At the maximum Service Temperature (see Paragraph 2.4.6 of this Regulation) after 3 hours conditioning at this temperature.

5.3	During this test, the equipment under test shall be connected to a source of pneumatic pressure. A positive shut-off valve and a pressure gauge having a pressure range of not less than 1.5 times nor more than 2 times the Test Pressure shall be installed in the pressure supply piping. The pressure gauge is to be installed between the positive shut-off valve and the sample under test.

5.4	Throughout the test the sample shall be tested for leakage with a surface active agent without formation of bubbles or measured with a combined leakage and permeation rate less than 10 Ncm3/hour or other equivalent test method.

6.	SEAT LEAKAGE TEST

6.1	The following tests for seat leakage are to be conducted on samples which have previously been subjected to the external leakage test of Paragraph 5 of this Annex.

6.2	Seat leakage tests shall be conducted with:

- The inlet of the sample valve connected to a source of pneumatic pressure,

- The valve in the closed position,

- The outlet open.

6.3	A positive shut-off valve and a pressure gauge having a pressure range of not less than 1.5 times and not more than twice the Test Pressure are to be installed in the pressure supply piping. The pressure gauge is to be installed between the positive shut-off valve and the sample under test. While under the applied Test Pressure observations for leakage are to be made with the open outlet submerged in water or by a flowmeter installed on the inlet side of the valve under test, the test described in Paragraph 6.8 below or other equivalent test method. If a flowmeter is used it shall be capable of indicating accurately, for the test fluid being used, the maximum leakage flow rates permitted.

6.4	The seat of a shut-off valve, when in the closed position, shall not leak at a rate exceeding 10 cm3/hour at any pneumatic pressure between zero and its Working Pressure.

6.5	A non-return valve with a resilient seat, shall not leak when subjected to any pneumatic pressure between 50 kPa and its Working Pressure when in the closed position.

6.6	A non-return valve with a metal to metal seat shall not leak with a rate exceeding 500 cm3/hour when subjected to any pneumatic pressure between 50 kPa and its Working Pressure when in the closed position.

6.7	The seat of the upper non-return valve used in conjunction with the Refueling Unit or Connection shall be free from leakage at any pneumatic pressure between zero and its Working Pressure, when in the closed position.

6.8	Pressure triggered pressure relief devices shall not leak at a rate exceeding 10 cm3/hour at any pneumatic pressure between zero and their Working Pressure minus 10%.

6.9	Conformance with Paragraph 6 of this Annex may be determined by connecting a length of tubing to the valve outlet. The open end of this outlet tube is to be located within an inverted graduated cylinder which is calibrated in cubic centimetres. The inverted cylinder is to be closed 	by a water tight seal. The apparatus is to be adjusted so that:

- The end of the outlet tube is located approximately 13 mm above the water level within the inverted graduated cylinder, and

- The water within and exterior to the graduated cylinder is at the same level. With these adjustments made, the water level within the graduated cylinder is to be recorded. With the valve in the closed position assumed as the result of normal operation, the test gas at the specified Test Pressure is to be applied to the valve inlet for a test period of not less than 2 minutes. During this time, the vertical position of the graduated cylinder is to be adjusted, if necessary, to maintain the same water level within and exterior to it.

At the end of the test period and with the water within and exterior to the graduated cylinder at the same level, the level of water within the graduated cylinder is again recorded. From the change of volume within the graduated cylinder, the leakage rate is to be calculated according to the following formula:

Where:

V1	= leakage rate, cubic centimetres of air or nitrogen per hour.

Vt	= increase in volume within graduated cylinder during test.

T	= time of test, minutes.

P	= barometric pressure during test, in kPa.

T	= ambient temperature during test, in K.

7.	ENDURANCE TEST (CONTINUED OPERATION)

7.1	A hydrogen carrying component shall be capable of conforming to the applicable leakage test requirements of Paragraphs 5 and 6 of this Annex, after being subjected to the number of operation cycles specified for that component in Appendix 8 of this Regulation.

7.2	The appropriate tests for external leakage and seat leakage, as described in Paragraphs 5 and 6 of this Annex are to be conducted immediately following the durability tests.

7.3	The component shall be connected to a pressurised source of dry air or nitrogen securely connected to a suitable fitting and subjected to the number of cycles specified for that Specific Component in Appendix 8 of this Regulation. A cycle shall consist of one opening and one closing of the component within a period of not less than 10 ± 2 seconds.

7.4	The component shall be operated through the total number of specified cycles at a temperature of 20°C ( 5°C and at the Working Pressure of the component. During the off cycle the downstream pressure of the test fixture should be allowed to decay to 50 per cent of the Working Pressure of the component.

7.5	The component shall be operated through 2 per cent of the total cycles at the maximum Service Temperature (see Paragraph 2.4.6 of this Regulation) after 3 hours conditioning at this temperature and at the Working Pressure of the component. The component shall comply with Paragraph 5 of this Annex at the appropriate maximum Service Temperature at the completion of the high temperature cycles.

7.6	The component shall be operated through 2 per cent of the total cycles at the minimum Service Temperature (see Paragraph 2.4.6 of this Regulation) after 3 hours conditioning at this temperature and at the Working Pressure of the component. The component shall comply with Paragraph 5 of this Annex at the appropriate minimum Service Temperature at the completion of the low temperature cycles.

7.7	Where appropriate following the durability tests and leakage re-tests specified above, the component shall be capable of completely opening and closing when a torque not greater than that specified in Table 9.3 is applied to the component handle in a direction to open it completely and then in the reverse direction to close it completely.

Table 9.3

| Component Inlet Size (mm) | Max. Torque (Nm) |
| --- | --- |
| 6 | 1.7 |
| 8 or 10 | 2.3 |
| 12 | 2.8 |

This test shall be conducted at the appropriate maximum and minimum Service Temperatures specified (see Paragraph 2.4.6 of this Regulation).

- HYDROGEN COMPATIBILITY

8.1	Hydrogen compatibility testing shall be carried out in accordance with prEN/ISO 11114 - 4.

9.	CORROSION RESISTANCE

9.1	Metallic hydrogen containing components shall comply with the leakage tests specified Paragraphs 5 and 6 of this Annex after being submitted to 144 hours salt spray test in accordance with ISO 9227: 1990 Corrosion Tests In Artificial Atmospheres: Salt Spray Tests" with all connections closed.

9.2	A copper or brass Hydrogen containing component shall comply with the leakage tests specified Paragraphs 5 and 6 of this Annex after being submitted to 24 hours immersion in Ammonia in accordance with ISO 6957: 1988 Copper Alloys: Ammonia Test For Stress Corrosion Resistance with all connections closed.

10.	RESISTANCE TO DRY-HEAT

10.1	The test shall be undertaken in compliance with ISO 188: 1998 Rubber, Vulcanised Or Thermoplastic - Accelerated Ageing And Heat Resistance Tests. The test piece shall be exposed to air at a temperature equal to the maximum Service Temperature for 168 hours.

10.2	The change in tensile strength shall not exceed + 25 per cent.

10.3	The change in ultimate elongation shall not exceed the following values:

Maximum increase	10 per cent

Maximum decrease	30 per cent

11.	OZONE AGEING

11.1	The test shall be undertaken in compliance with ISO 1431: 1989 Rubber, Vulcanised Or Thermoplastic; Resistance To Ozone Cracking, Part 1 Static Strain Test. The test piece, which has to be stressed to 20 per cent elongation shall be exposed to air at 40°C with an ozone concentration of 50 parts per hundred million for a period of 120 hours.

11.2	No cracking of the test piece is allowed.

12.	BURST/DESTRUCTIVE TEST

Only applicable to containers - see Annex 7 of this Regulation.

13.	TEMPERATURE CYCLE TEST

13.1	A non-metallic part containing hydrogen shall comply with the leakage tests mentioned in Paragraphs 5 and 6 of this Annex after having been submitted to 96 hours temperature cycle from the minimum Service Temperature up to the maximum Service Temperature (see Paragraph 2.4.6 of this Regulation) with a cycle time of 120 minutes, under Maximum Working Pressure.

14.	PRESSURE CYCLE

14.1	Pressure cycle test requirements for Containers are specified in Annex 7 of this Regulation.

14.2	All Flexible Fuel Lines shall be capable of conforming to the applicable leakage test requirements of Paragraph 5 of this Annex after being subjected to 20000 pressure cycles. The pressure shall change from atmospheric pressure to the Working Pressure of the Container within less than five seconds, and after a time of at least five seconds, shall decrease to atmospheric pressure within less than five seconds. The appropriate test for external leakage, as described under external leakage test in Paragraph 5 of this Annex is to be conducted immediately following this test.

14.3	For all Class 0 Hydrogen Systems the complete Fuel Line assemblies shall be capable of conforming to the applicable leakage test requirements of Paragraph 5 of this Annex after being subjected to 20000 pressure cycles. The pressure shall change from atmospheric pressure to the Working Pressure of the Container within less than five seconds, and after a time of at least five seconds, shall decrease to atmospheric pressure within less than five seconds. The appropriate test for external leakage, as described under external leakage test in Paragraph 5 of this Annex is to be conducted immediately following this test.

14.4	All Heat Exchangers shall be capable of conforming to the applicable leakage test requirements of Paragraph 5 of this Annex after being subjected to 20000 pressure cycles. The pressure shall change from atmospheric pressure to the Working Pressure of the Container within less than five seconds, and after a time of at least five seconds, shall decrease to atmospheric pressure within less than five seconds. The appropriate test for external leakage, as described under external leakage test in Paragraph 5 of this Annex is to be conducted immediately following this test.

14.5	All Pressure Regulators shall be capable of conforming to the applicable leakage test requirements of Paragraph 5 of this Annex after being subjected to 20000 pressure cycles. The pressure shall change from atmospheric pressure to the Working Pressure of the Container within less than five seconds, and after a time of at least five seconds, shall decrease to atmospheric pressure within less than five seconds. The appropriate test for external leakage, as described under external leakage test in Paragraph 5 of this Annex is to be conducted immediately following this test.

14.6	All pressure sensors shall be capable of conforming to the applicable leakage test requirements of Paragraph 5 of this Annex after being subjected to 20000 pressure cycles. The pressure shall change from atmospheric pressure to the Working Pressure of the Container within less than five seconds, and after a time of at least five seconds, shall decrease to atmospheric pressure within less than five seconds. The appropriate test for external leakage, as described under external leakage test in Paragraph 5 of this Annex is to be conducted immediately following this test.

14.7	All Hydrogen Filters shall be capable of conforming to the applicable leakage test requirements of Paragraph 5 of this Annex after being subjected to 20000 pressure cycles. The pressure shall change from atmospheric pressure to the Working Pressure of the Container within less than five seconds, and after a time of at least five seconds, shall decrease to atmospheric pressure within less than five seconds. The appropriate test for external leakage, as described under external leakage test in Paragraph 5 of this Annex is to be conducted immediately following this test.

15.	VIBRATION RESISTANCE TEST

15.1	All components with moving parts shall remain undamaged, continue to operate, and comply with the component's leakage tests after 6 hours of vibration in accordance with the test method described below.

15.2	The component shall be secured in an apparatus and vibrated for 2 hours at 17 Hz with an amplitude of 1.5 mm (0,06 in.) in each of three orientation axes. On completion of 6 hours of vibration the component shall comply with Paragraphs 5 and 6 of this Annex.

16	SERVICE TEMPERATURES

The component shall remain fully functional within the appropriate Service Temperature ranges specified in Paragraph 2.4.6 of this Regulation

17.	CONNECTION TEST

17.1	All fittings or screwed connection systems shall be capable of conforming to the applicable leakage test requirements of Paragraph 5 of this Annex, after being subjected to 25 cycles of connection and disconnection.

17.2	The appropriate test for external leakage, as described under external leakage test in Paragraph 5 of this Annex, is to be conducted immediately following this test.

Annex 10

SPECIAL REQUIREMENTS TO BE APPLIED TO THE SAFETY ASPECTS OF

COMPLEX ELECTRONIC VEHICLE CONTROL SYSTEMS

1	GENERAL

This Annex defines the special requirements for documentation, verification and test with respect to the safety aspects of Complex Electronic Vehicle Control Systems (defined in Paragraph 2 of this Annex) as far as this Regulation is concerned.

2	DEFINITIONS

For the purposes of this Annex the definitions of Paragraph 2.1 of this regulation shall apply.

3	DOCUMENTATION

3.1	Requirements

The Manufacturer shall provide a documentation package which gives access to the basic design of “The System” and the means by which it is linked to other vehicle systems or by which it directly controls output variables. The function(s) of “The System” and the Safety Concept, as laid down by the Manufacturer, shall be explained. Documentation shall be brief, yet provide evidence that the design and development has had the benefit of expertise from all the system fields which are involved. For periodic technical inspections, the documentation shall indicate the means by which the current operational status of the system can be checked.

Documentation shall be made available in 2 parts:

- The formal documentation package for the approval, containing the material listed in Paragraph 3 of this Annex, which shall be supplied to the Technical Service at the time of submission of the Type Approval application. This will be taken as the basic reference for the Verification Process set out in Paragraph 4 of this Annex.

- Additional material and analysis data which shall be retained by the Manufacturer, but made open for inspection at the time of Type Approval.

3.2	Description of the Functions of “The System”.

A description shall be provided which gives a simple explanation of all the control functions of “The System” and the methods employed to achieve the objectives, including a statement of the mechanism(s) by which control is exercised including:

- A list of all input and sensed variables shall be provided and the working range of these defined.

- A list of all output variables which are controlled by “The System” shall be provided and an indication given, in each case, of whether the control is direct or via another vehicle system. The Range of Control exercised on each such variable shall be defined.

- Limits defining the Boundary of Functional Operation shall be stated where appropriate to system performance.

3.3	System Layout and Schematics

3.3.1	Inventory of Components

A list shall be provided, collating all the Units of “The System” and mentioning the other vehicle systems which are needed to achieve the control function in question. An outline schematic showing these Units in combination, shall be provided with both the equipment distribution and the interconnections clearly identified.

3.3.2	Functions of the Units

The function of each Unit of “The System” shall be outlined and the signals linking it with other Units or with other vehicle systems shall be shown. This may be provided by a labelled block diagram or other schematic, or by a description aided by such a diagram.

3.3.3	Interconnections

Interconnections within “The System” shall be shown by a circuit diagram for the electric Transmission Links, by a piping diagram for pneumatic or hydraulic Transmission Links and by a simplified diagrammatic layout for mechanical Transmission Links.

3.3.4	Signal Flow and Priorities

There shall be a clear correspondence between these Transmission Links and the signals carried between Units. Priorities of signals on multiplexed data paths shall be stated, wherever priority may be an issue affecting performance or safety as far as this Regulation is concerned.

3.3.5	Identification of Units

Each Unit shall be clearly and unambiguously marked with the Manufacturer’s identification marking to provide corresponding hardware and documentation association. Where functions are combined within a single Unit or indeed within a single computer, but shown in multiple blocks in the block diagram for clarity and ease of explanation, only a single identification marking shall be used. The Manufacturer shall, by the use of this identification marking, affirm that the equipment supplied conforms to the corresponding document.

The identification marking defines the hardware and software version and, where the latter changes such as to alter the function of the unit, this identification marking shall also be changed.

3.4	Safety Concept of the Manufacturer

3.4.1	The Manufacturer shall provide a statement which affirms that the strategy chosen to achieve “The System” objectives will not, under non-fault conditions prejudice the safe operation of systems which are subject to the prescriptions of this Regulation.

3.4.2	In respect of software employed in “The System”, the outline architecture shall be explained and the design methods and tools used shall be identified. The Manufacturer shall be prepared, if required, to show some evidence of the means by which they determined the realisation of the system logic, during the design and development process.

3.4.3	The Manufacturer shall provide the Technical Authorities with an explanation of the design provisions built into “The System” so as to generate safe operation under fault conditions. Possible design provisions for failure in “The System” are:

- Fall-back to operation using a partial system,

- Change-over to a separate back-up system,

- Removal of the High Level Function.

For each of the chosen provisions, the driver shall be warned for example by warning signals or message displays. When the system is not deactivated by the driver, e.g. by turning the vehicle activation switch to “off”, or by switching off that particular function if a special switch is provided for that purpose, the warning shall be present as long as the fault condition persists.

3.4.3.1	If the chosen provision selects a partial performance mode of operation under certain fault conditions, then these conditions shall be stated and the resulting limits of effectiveness defined.

3.4.3.2	If the chosen provision selects a second (back-up) means to realise the vehicle control system objective, the principles of the change-over mechanism, the logic and level of redundancy and any built in back-up checking features shall be explained and the resulting limits of back-up effectiveness defined.

3.4.3.3	If the chosen provision selects the removal of the Higher Level Function, all the corresponding output control signals associated with this function shall be inhibited, and in such a manner as to limit the transition disturbance.

3.4.4	The documentation shall be supported, by an analysis which shows, in overall terms, how the system will behave on the occurrence of any one of those specified faults which will have a bearing on vehicle control performance or safety. This may be based on a Failure Mode and Effect Analysis (FMEA), a Fault Tree Analysis (FTA) or any similar process appropriate to system safety considerations. The chosen analytical approach shall be established and maintained by the Manufacturer and shall be made open for inspection by the Technical Service at the time of the Type Approval.

3.4.5	The documentation shall itemise the parameters being monitored and shall set out, for each fault condition of the type defined in Paragraph 3.4.3 above, the warning signal to be given to the driver or to service/technical inspection personnel.

4	VERIFICATION AND TEST

4.1	The functional operation of “The System”, as laid out in the documents required in Paragraph 3 of this Annex shall be tested as follows:

4.1.1	Verification of the Function of “The System”

As the means of establishing the normal operational levels, verification of the performance of the vehicle system under non-fault conditions shall be conducted against the Manufacturer’s basic benchmark specification unless this is subject to a Specified Performance Test as part of the Approval Procedure of this or another Regulation.

4.1.2	Verification of the Safety Concept of Paragraph 3.4 of this Annex

The reaction of “The System” shall, at the discretion of the Type Approval Authority, be checked under the influence of a failure in any individual Unit by applying corresponding output signals to electrical Units or mechanical elements in order to simulate the effects of internal faults within the unit.

4.1.3	The verification results shall correspond with the documented summary of the failure analysis, to a level of overall effect such that the Safety Concept and execution are confirmed as being adequate.

4.2	The warning signal specified in Paragraph 3.4.3 of this Annex may, in general, be satisfied by one optical signal per complex vehicle system unless any other Regulation applicable to the same equipment specifically requires multiple signals.